## Slide 1: Build your own Wi-Fi automation lab Lab Guide - Day 2
Andreas Koksrud / Telenor Bedrift
Kjetil Teigen Hansen / Conscia

## Slide 2: References / inspiration
https://github.com/CiscoDevNet/yangsuite/
https://postman.com
https://docs.ansible.com/ansible/latest/collections/cisco/ios/ios_facts_module.html
https://www.wifireference.com/2020/01/14/viewing-network-telemetry-from-the-catalyst-9800-with-grafana/
https://grafana.com/grafana/dashboards/13462-device-health-monitoring/
https://grafana.com/grafana/dashboards/12468-catalyst-9800-client-stats/
https://wirelessisfun.wordpress.com/2020/12/10/network-telemetry-data-and-grafana-part-1-the-advanced-netconf-explorer/
https://python.org
https://codeium.com
https://blog.apnic.net/
References

## Slide 3: Copyright
© Andreas Koksrud 2024. All rights reserved. This presentation is provided for educational and informational purposes only. You may distribute and learn from this presentation, but commercial use or any form of monetization is strictly prohibited without prior written consent.
Copyright

## Slide 4: Prerequisites
Cisco.com account with access to downloading WLC (9800-CL at https://software.cisco.com)
Postman account (https://postman.com)
Windows laptop with administrative privileges
Complete the pre-lab exercises before the deep dive labs
  Pre-lab exercises are distributed in a separate PowerPoint document Build your own Wi-Fi automation lab - Pre-lab tasks (2024-xx-xx).pptx
Complete at least the Day 1 exercises that are relevant to what you will do in Day 2 (e.g Python, Ansible or Grafana you should have completed those parts from Day 1)
Without these, parts of the Deep Dive might be difficult to complete, or steps might differ severely
Communications

## Slide 5: Communications
WebEx space: Wi-Fi automation lab
Please help each other
Sharing is caring 
Communications

## Slide 6: Agenda
Pre-lab
Install VirtualBox
Install Cisco 9800-CL
Install Ubuntu Server w/Docker
Install Postman
Install VS Code
Day 1
Day 2
In-depth explore a topic of choice
Sort out pre-lab task problems
Grafana / TIG-stack
Grafana Cloud
Ansible
Python
Other vendors (MIST/Meraki/Aruba)
Get to know the lab environment
Configure your AP
Connect VS Code to Ubuntu
Install and explore Ansible
Explore Python automation
Install and explore YANG Suite
Explore Postman
Install and explore Grafana
Agenda

## Slide 7: Scope
In scope
  Getting started with various systems/languages/solutions for lab purposes
  Get a lab environment up and running on your own laptop
  Some nice examples to try various aspects of automation
  Inspiring you to explore deeper on your own
Out of scope topics
  Git
  Learning the languages (Ansible, Python, InfluxQL, etc)
  Learning Linux
  Deploying the systems for production use
Scope

## Slide 8: Topology
Lab topology

## Slide 9: About Day 2
In-depth exploration of one or more topics of your choice
You should have completed relevant parts of Pre-lab tasks and Day 1 exercises
For each exercise, we will try to do the following
  Tasks
    One or more slides, with one or more tasks
    Expected output
  Hints
    One or more slides, with hints or code snippets to get you in the right direction
  Example solution
    An example solution (Note that most exercises will have many possible solutions that are better than the example )
    Example output
Error handling
  Examples in this lab will have minimal error handling to keep the examples small and readable
  Depending on the usage (one-off vs. a recurring operations script) you will want some error handling
About day 2

## Slide 10: In-depth: Ansible
This part of the Day 2 labs will focus on using Ansible
The following lab exercises are included in this part
  Lab Exercise #20: Ansible - Run CLI commands
  Lab Exercise #21: Ansible - CLI configuration
  Lab Exercise #22: Ansible - Using Jinja2 templates
  Lab Exercise #23: Ansible - Using RESTCONF
  Lab Exercise #24: Ansible - Writing your own module using Python
  Lab Exercise #25: Ansible - Using RESTCONF + Python-module
  Lab Exercise #26: Ansible - Organizing projects using import_playbook
  Lab Exercise #27: Ansible - Organizing projects using roles
In-depth: Ansible

## Slide 11: Run a CLI command - Intro
In this exercise we will write a playbook that runs a single command on our WLC
We will observe that the output of the CLI command is passed back to the playbook, and can be used in further tasks
For this exercise, the output will be used in a task that prints the result of the CLI command out to the terminal where you ran the playbook
Lab Exercise #20: Ansible - Run CLI commands

## Slide 12: Run a CLI command - Tasks
Task 0: Set up the files and folders and VS Code
  Create a working directory
  Create a playbook file
  Remember to activate the ansible-venv
Task 1: Write a playbook that
  Runs the command "show wireless summary | inc Max APs"
  Output when running this on the WLC should be like this
Task 2: Run the playbook on your WLC
  You can copy the inventory file hosts.yml from Day 1
Lab Exercise #20: Ansible - Run CLI commands
  wlc9# show wireless summary | inc Max APs
  Max APs supported : 100
hosts.yml
wlc:
hosts:
192.168.10.{WLC-IP}:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: restconf-pass
ansible_password: restconf-pass
ansible_user: restconf-adm
ansible_host_key_checking: False
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab20_Ansible-run-cli-commands$ source ~/ansible-venv/bin/activate
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab20_Ansible-run-cli-commands$ ansible --version

## Slide 13: Run a CLI command - Hints
Lab Exercise #20: Ansible - Run CLI commands
run-cli-command-playbook.yml
---
- name: CLI Playbook
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Get Max APs supported with CLI command"
some_module_that_will_run_commands:
some_parameter: "show wireless summary | include Max APs"
register: result
- name: "View result"
some_builtin_module_that_can_output_messages:
some_parameter: "{{ result.stdout }}"
Playbook header
  name: Name of the playbook, make it descriptive
  hosts: The "wlc" here you can find in the hosts.yml file. Can be expanded to other types.
  connection: network_cli for most of our stuff
  gather_facts: A general-purpose gathering function
Our "tasks" section starts here
Instead of this placeholder, you would use a module that can run CLI commands. Try looking in the cisco.ios collection in the Ansible Docs https://docs.ansible.com/ansible/latest/collections/cisco/ios/index.html#plugins-in-cisco-ios
Instead of this placeholder, you will use a module that can output stuff. The example solution uses a builtin module to output the text in "results" as a debug message when you run the playbook. Try looking in the ansible.builtin collection https://docs.ansible.com/ansible/latest/collections/ansible/builtin/index.html#plugins-in-ansible-builtin
The structure of the file should be like this
Run the playbook with this command
  (ansible-venv) (.cut.)$ ansible-playbook -i hosts.yml run-cli-command-playbook.yml

## Slide 14: Run a CLI command - Example solution
---
- name: CLI Playbook
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Get Max APs supported with CLI command"
cisco.ios.ios_command:
commands: "show wireless summary | include Max APs"
register: result
- name: "View result"
ansible.builtin.debug:
msg: "{{ result.stdout }}"
cli-playbook.yaml
Lab Exercise #20: Ansible - Run CLI commands
Here is an example solution
The output should look like this

## Slide 15: Ansible - CLI configuration - Intro
In this exercise, we will write a playbook that does some CLI configuration
A key concept of Ansible is "idempotency". That basically means
  If something IT NOT configured, then go ahead and configure it
  If something IS configured, just skip the task.
  That means: DO NOT configure the same stuff again if it isn't necessary
This exercise will create a task that does this for a small part of the configuration. It can of course be expanded to a complete config. There are many ways to do this, some of which are
  Putting everything in a gigantic playbook with hundreds of tasks (it might get heavy to navigate)
  Splitting tasks for small config snippets in separate files, and call them all from a "master playbook"
  Using Jinja2 templates (we will try this in a later exercise)
  Using Ansible roles in combination with templates or tasks
  ... and many many more ;-)
Lab Exercise #21: Ansible - CLI configuration

## Slide 16: Ansible - CLI configuration - Tasks
Task 0: Set up the files and folders and VS Code
  Create a working directory
  Create a playbook file
  Remember to activate the ansible-venv
Task 1: Write a playbook that
  Ensure that this policy profile is present on the WLC
Task 2: Run the playbook on your WLC
  You can copy the inventory file hosts.yml from Day 1
Task 3: Verify the idempotency of the playbook. That means
  If the config IS NOT present, it should be configured
  If the config IS present, it should do nothing
Lab Exercise #21: Ansible - CLI configuration
  wireless profile policy clients_policy_profile
  idle-timeout 3000
  passive-client
  session-timeout 43200
  vlan 11
  no shutdown
hosts.yml
wlc:
hosts:
192.168.10.{WLC-IP}:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: restconf-pass
ansible_password: restconf-pass
ansible_user: restconf-adm
ansible_host_key_checking: False
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab21_Ansible_cli_config$ source ~/ansible-venv/bin/activate
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab21_Ansible_cli_config$ ansible --version

## Slide 17: Ansible - CLI configuration - Hints
Lab Exercise #21: Ansible - CLI configuration
cli_config-playbook.yml
---
- name: CLI Playbook
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Configure policy profile: clients_policy_profile"
some_module_that_will_do_ios_config:
some_parameter_with_config_lines:
- idle-timeout 3000
- passive-client
- session-timeout 43200
- vlan 11
- no shutdown
some_parent_parameter: wireless profile policy clients_policy_profile
Instead of this placeholder, you would use a module that can do CLI config on Cisco IOS devices. Try looking in the cisco.ios collection in the Ansible Docs https://docs.ansible.com/ansible/latest/collections/cisco/ios/index.html#plugins-in-cisco-ios
The module needs all the config lines that we want, as an ordered list, after a parameter specifying all those lines
The module also needs a parameter specifying which parent the config lines should belong to. The parent in this example is the policy profile. In another example it might be an interface, a WLAN, a site tag etc.
The structure of the file should be like this
Run the playbook with this command
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab21_Ansible_cli_config$ ansible-playbook -i hosts.yml cli-config-playbook.yml

## Slide 18: Ansible - CLI configuration - Hints 2
Lab Exercise #21: Ansible - CLI configuration
(parts of) cli_config-playbook.yml
- name: "Configure policy profile: clients_policy_profile"
cisco.ios.ios_config:
before:
- wireless profile policy clients_policy_profile
- shutdown
lines:
- idle-timeout 3000
- passive-client
- session-timeout 43200
- vlan 11
after:
- no shutdown
some_parent_parameter: wireless profile policy clients_policy_profile
These lines will be entered before the lines that we compare
Since we enter "no shutdown" after the lines themselves, we do not need this in the lines
These lines will be entered after the lines that we compare
If you try to change the VLAN ID from 11 to 12, you will notice that nothing changes on the WLC. That is because the policy profile needs to be shutdown before making changes if it already exists. You can test this on your WLC with the following commands
To address this, we can use the before: and after: statements in the task, to get Ansible to add certain commands before and after the lines that we compare. The before and after sections will only be run if the task itself would create a change (i.e. if the lines do not match)
  wlc9# wlc9#conf t
  wlc9(config)# wireless profile policy clients_policy_profile
  wlc9(config-wireless-policy)# vlan 12
  % Policy profile needs to be disabled before performing this operation.

## Slide 19: Ansible - CLI configuration - Example solution
---
- name: CLI configuration
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Configure policy profile: clients_policy_profile"
cisco.ios.ios_config:
before:
- wireless profile policy clients_policy_profile
- shutdown
lines:
- idle-timeout 3000
- passive-client
- session-timeout 43200
- vlan 11
after:
- no shutdown
parents: wireless profile policy clients_policy_profile
cli-playbook.yaml
Lab Exercise #21: Ansible - CLI configuration
Here is an example solution
First time run, output should be like this, and the policy profile appear on WLC
On next run, the config should already be present
  wlc9800#show run | sec wireless profile policy
  wireless profile policy lab-policy
  no central authentication
  no central dhcp
  no central switching
  dhcp-tlv-caching
  http-tlv-caching
  vlan 11
  no shutdown
  wireless profile policy clients_policy_profile
  idle-timeout 3000
  passive-client
  session-timeout 43200
  vlan 11
  no shutdown
  wireless profile policy default-policy-profile
  description "default policy profile"

## Slide 20: Ansible - CLI configuration - Extra tasks
Lab Exercise #21: Ansible - CLI configuration
Create some more tasks in the playbook, for configuring
  Interfaces. You can play with Gig2 and Gig3, or create VLAN interfaces or Loopbacks
  WLANs. PSKs might be tricky to get idempotent once they are encrypted.
  Global commands, like ensure restonf is enabled
Remember, for idempotency the commands must be exactly as they will appear in the running config. So don't use abbreviations in the config lines (like "desc" for description, "ip add" for ip address, etc.
  They will be run and work, but next time you run they will be configured again since the command to push is different from what is present on the device.
The before and after statemens will have to be changed accordingly. For tasks that do not need to be shutdown, you will probably not need the before and after sections

## Slide 21: Using Jinja2 templates - Intro
Lab Exercise #22: Ansible - Using Jinja2 templates
Jinja2 is a templating language, widely used by developers to create text files that have placeholders, which can be filled inn with various values. One very common example is HTML
Jinja2 is a native part of Ansible and the YAML files there. So anytime you write something in double curly braces it is a Jinja2 variable that will be replaced by the content of the variable when you run the playbook
Instead of using Jinja2 inline, we can store templates as separate files, and then refer to those templates when running our playbook
In this exercise, we will modify the playbook from our CLI configuration exercise to use Jinja2 templates instead of spelling out the commands in the playbook itself
One advantage of using templates is to reuse a playbook for various templates
Another advantage is the possibility to loop in the template itself, for instance looping over all site tags

## Slide 22: Using Jinja2 templates - Tasks
Lab Exercise #22: Ansible - Using Jinja2 templates
Task 0: Set up the files and folders and VS Code
  Create a working directory
  Create a playbook file
  Remember to activate the ansible-venv
Task 1: Write a playbook using a Jinja2 template
  Ensure that this policy profile is present on the WLC
  You can copy the inventory file hosts.yml from Day 1
  Verify the idempotency (changes stuff only when needed)
Task 2: Change some of the text in the j2 template
  Use a variable for the name and the VLAN ID
  Use a loop statement in the task to do multiple policy profiles with the same template
  wireless profile policy clients_policy_profile_j2
  session-timeout 43200
  vlan 11
  no shutdown
hosts.yml
wlc:
hosts:
192.168.10.{WLC-IP}:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: restconf-pass
ansible_password: restconf-pass
ansible_user: restconf-adm
ansible_host_key_checking: False
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab22_Ansible_Jinja2$ source ~/ansible-venv/bin/activate
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab22_Ansible_Jinja2$ ansible --version

## Slide 23: Using Jinja2 templates - Hints for task 1
Lab Exercise #22: Ansible - Using Jinja2 templates
jinja2-playbook.yml
---
- name: CLI Playbook
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Configure policy profile: clients_policy_profile_j2"
cisco.ios.ios_config:
before:
- wireless profile policy clients_policy_profile_j2
- shutdown
src: policy_profile_template.j2
match: line
after:
- no shutdown
This is where we put in the Jinja2 template file we created
The structure of the file should be like this
Now, go ahead and fill inn the "policy_profile_template.j2" file
Run the playbook with this command
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab22_Ansible_Jinja2$ ansible-playbook -i hosts.yml jinja2-playbook.yml
Hint: It should contain the commands that you want in the config, as they appear in the config
policy_profile_template.j2
wireless profile policy clients_policy_profile_j2
session-timeout 43200
vlan 11
no shutdown

## Slide 24: Using Jinja2 templates - Hints for task 2
Now we will try changing some of the static config in the template with some parameters
The parameters can come from different sources
  hosts.yml (will be used in this exercise)
  group_vars/ and host_vars/ directories
  External systems using APIs (NetBox, Catalyst Center, etc)
Let us modify our files
  hosts.yml
  jinja2-playbook.yml
  policy_profile_template.j2
Lab Exercise #22: Ansible - Using Jinja2 templates
Create some variables in the bottom of the hosts.yml file
Use the "loop" statement in the playbook, to loop over the policy_profiles list you created. - To reference the items that you loop over, you use keyword "item" - To reference sub-values, use dot notation or square bracket notation. Examples of both here, to reference the name and vlan of each item
Use the notation in the .j2 template as well

## Slide 25: Using Jinja2 templates - Example solution
Lab Exercise #22: Ansible - Using Jinja2 templates
Optional tasks:
  Can you change more parameters (ex. session-timeout value)?
  Can you create templates for other stuff? Loopback interfaces (safe to play with), wlans, site tags, etc?
jinja2-playbook.yml
---
- name: CLI configuration using Jinja2 template
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Configure policy profile from template: {{ item.name }}"
cisco.ios.ios_config:
before:
- wireless profile policy {{ item['name'] }}
- shutdown
src: policy_profile_template.j2
match: line
after:
- no shutdown
loop: "{{ policy_profiles }}"
hosts.yml
wlc:
hosts:
192.168.10.9:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2024!
ansible_password: ChangeMe2024!
ansible_user: devnet-adm
ansible_host_key_checking: False
policy_profiles:
- name: policy_profile_j2
vlan: 11
- name: policy_profile_j2_2
vlan: 12
- name: policy_profile_j2_3
vlan: 13
Change to YOUR WLC IP
hosts.yml
wireless profile policy {{ item['name'] }}
session-timeout 43200
vlan {{ item['vlan'] }}
no shutdown

## Slide 26: Ansible - Using RESTCONF - Intro
We can do RESTCONF calls directly from Ansible
Some pros with RESTCONF instead of CLI plugins from Ansible
  The return can be JSON, which is easy to use like a dictionary
  The speed of getting back data is high, especially if you compare to larger amount of CLI data. For instance, getting a table of connected clients when you have a lot of them
Some cons with RESTCONF instead of CLI plugins from Ansible
  There must exist a YANG model for what you are looking for
  You must find the correct xpath of the YANG model
In this exercise, we will get the certificates on the WLC, and more specifically the validity dates associated with the certs
We will use the YANG module "Cisco-IOS-XE-crypto-pki-oper" to get operational data about the certificates
Lab Exercise #23: Ansible - Using RESTCONF

## Slide 27: Ansible - Using RESTCONF - Tasks
Lab Exercise #23: Ansible - Using RESTCONF
Task 0: Set up the files and folders and VS Code
  Create a working directory
  Create a playbook file
  Copy the hosts.yml from previous projects
  Remember to activate the ansible-venv
Task 1: Use YANG Suite (or yangcatalog.org) to find the RESTCONF path that will give details about the certificates
  Load and view the details of the module "Cisco-IOS-XE-crypto-pki-oper"
  Test the RESTCONF call towards your WLC with Postman
  Add some filters, to only return the label, subject-name and validity-end
Task 2: Write the Ansible task to use your RESTCONF path
  Use the "ansible.builtin.uri" module to perform the RESTCONF call
  Print the results of the call
  (optional task) Print the results of just the validity date of each result
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab23_Ansible_RESTCONF$ source ~/ansible-venv/bin/activate
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab23_Ansible_RESTCONF$ ansible --version

## Slide 28: Ansible - Using RESTCONF - Hints for Task 1
Lab Exercise #23: Ansible - Using RESTCONF
Example on using YANG Suite to browse the "Cisco-IOS-XE-crypto-pki-oper" model
  RESTCONF call for 9800: https://{WLC_IP}/restconf/data/{YANG module}:{xpath} WLC_IP: 192.168.10.9 (change to YOUR WLC IP) YANG module: Cisco-IOS-XE-crypto-pki-oper Xpath: crypto-pki-oper-data/crypto-pki-bundle
  https://{{host}}/restconf/data/Cisco-IOS-XE-crypto-pki-oper:crypto-pki-oper-data/crypto-pki-bundle

## Slide 29: Ansible - Using RESTCONF - Hints for Task 1
Lab Exercise #23: Ansible - Using RESTCONF
Example on using yangcatalog.org to browse the "Cisco-IOS-XE-crypto-pki-oper" model
  Use your browser to enter https://yangcatalog.org
  Click "YANG Module Detail Viewer"
  Start writing and then select the module. Click "Get details"
  Click "Tree View"
  Decide which level of data you want to retrieve. Let's start with the full bundle. You can click each line to expand or compact levels, or click the + next to "Element" to expand the full tree
    On the right hand of the "crypto-pki-bundle" line you will find the path you need in the "Sensor Path" column
  Copy the sensor path, and create the RESTCONF call:
  https://{{host}}/restconf/data/Cisco-IOS-XE-crypto-pki-oper:crypto-pki-oper-data/crypto-pki-bundle

## Slide 30: Ansible - Using RESTCONF - Hints for Task 1
Lab Exercise #23: Ansible - Using RESTCONF
Enter the path in Postman
You should hopefully get something like this, where you can see lots of details for each certificate on the device
To choose only a few fields, use the operator "?fields=" after the path. This example shows picking the label, subject-name and validity-end from above
  https://{{host}}/restconf/data/Cisco-IOS-XE-crypto-pki-oper:crypto-pki-oper-data/crypto-pki-bundle?fields=label;cert/subject-name;cert/validity-end

## Slide 31: Ansible - Using RESTCONF - Hints for Task 2
Lab Exercise #23: Ansible - Using RESTCONF
Here are some tips for writing the Ansible playbook
To perform the RESTCONF call, use the module "ansible.builtin.uri". Check the Ansible documentation for how-to and examples
"url" should be copy-paste of what you have tested in Postman, just replace {{host}} with {{ ansible_host}}
Try to replicate headers, body format and method from Postman
Do not validate certs
Specify some valid HTTP status codes, at least status code 200
Create a second task for printing the results. Start by printing all of the result.
Try to narrow down the printing (think, what can you do with the results beside printing to the screen. It might be out of scope for this lab, but very nice to test how you can manipulate the results). Tips, msg: {{result['json']}} is the first step
Use a when: statement on the print results part. It should only run when the status code is 200 "OK".

## Slide 32: Ansible - Using RESTCONF - Example solution
---
- name: RESTCONF demo playbook
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: "Get Certificate list with RESTCONF"
ansible.builtin.uri:
url: "https://{{ ansible_host }}/restconf/data/Cisco-IOS-XE-crypto-pki-oper:crypto-pki-oper-data/crypto-pki-bundle?fields=label;cert/subject-name;cert/validity-end"
user: "{{ ansible_user }}"
password: "{{ ansible_password }}"
method: GET
headers:
Content-Type: 'application/yang-data+json'
Accept: 'application/yang-data+json'
body_format: json
body:
validate_certs: false
status_code:
- 200
- 204
- 404
register: result
- name: "View result"
ansible.builtin.debug:
msg: "{{ result['json']['Cisco-IOS-XE-crypto-pki-oper:crypto-pki-bundle'] }}"
when: result.status == 200
Lab Exercise #23: Ansible - Using RESTCONF
Playbook and task header is similar to previous tasks
Using ansible.builtin.uri
URL copy-paste from what is tested in Postman
Change host, user and password with the ansible_host, ansible_user and ansible_password values
Try to replicate method, headers and body format from Postman
Do not validate the HTTPS certs (at least in this lab)
Valid return status codes
View the results using ansible.builtin.debug module
Only when the HTTP status code of the RESTCONF call is 200 ("OK")
ansible-restconf-playbook.yml

## Slide 33: Ansible - Using RESTCONF - Example output
Lab Exercise #23: Ansible - Using RESTCONF
Example output

## Slide 34: Ansible - Writing your own module - Intro
Lab Exercise #24: Ansible - Writing your own module using Python
If you want to do some stuff that is not supported in the builtin or community modules, you can write your own module. It can be small or large project, but it can also be something that is simple in Python, but that you would need to make complex structures in Ansible to solve
The example will
  Get "show run" from our device(s) using the cisco.ios.ios_facts module
  Call our own module that use the input and return values based on that
  Print the result
This is a simple test/demo of a module. Some practical use of this module could be to check whether RESTCONF is enabled on a device, and based on the result of this test you could run other tasks as either RESTCONF, or fallback to CLI mode if RESTCONF is not available.

## Slide 35: Ansible - Writing your own module - Tasks
Lab Exercise #24: Ansible - Writing your own module using Python
Task 0: Set up the files and folders and VS Code
  Create a working directory and a playbook file "ansible-restconf-playbook.yml"
  Copy the hosts.yml from previous projects
  Create a "library" folder with a file "check_restconf_status.py" inside
  Create a "logs" folder where we will dump some log files later
  Remember to activate the ansible-venv (use this for both Ansible and Python files in this exercise)
Task 1: Create the Python module
  Use the example in the Ansible docs "Developing modules" as an example https://docs.ansible.com/ansible/latest/dev_guide/developing_modules_general.html
Task 2: Create the Ansible playbook
  The playbook should have 3 tasks
    Gather IOS facts (check docs on the cisco.ios.ios_facts module, https://docs.ansible.com/ansible/latest/collections/cisco/ios/ios_facts_module.html#ansible-collections-cisco-ios-ios-facts-module)
    Run your module, it should be called the same way as a regular module, and the arguments indented below the module
    Write the results to a YAML file
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab24_Ansible-module$ source ~/ansible-venv/bin/activate
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab24_Ansible-module$ ansible --version

## Slide 36: Ansible - Writing your own module - Hints for task 1
Lab Exercise #24: Ansible - Writing your own module using Python
I have removed all the docs from the example, you could probably keep it
module args should be "hostname" and "show_run", both dict objects of type 'str'
result should be dict, with changed=False and nothing else
In the part where the actual "doing" is taking place, put stuff into result dict. You can add new key-value-pairs as you like
Take the hostname from input parameters, put it in the result dict, under result['hostname']
Check if "restconf" is in the variable module.params['show_run']
  If yes, put "True" in result['restconf_enabled']
  If no, put "False" in result['restconf_enabled']
On exit, return the results back to Ansible

## Slide 37: Ansible - Writing your own module - Hints for task 2
Lab Exercise #24: Ansible - Writing your own module using Python
Same playbook opening as we have used in the previous examples
Gather IOS facts from the devices
Call your module as you would any other module. As long as the name matches (without the .py extension) and it is located in the library folder, it will be found automatically
Indented under the module you put the input variables
Write the results to a YAML file
Try to finish the line yourself (or look at next page)
(optional) Try writing the results to JSON, it should be pretty similar, just format the content using "to_nice_json" instead

## Slide 38: Ansible - Writing your own module - Example solution
# Written by Andreas Koksrud, based on framework from Erik Rongved and Espen Frøstrup.
from ansible.module_utils.basic import AnsibleModule
def run_module():
# Define available arguments/parameters available to pass to the module from Ansible
module_args = dict(
hostname=dict(type='str', required=True),
show_run=dict(type='str', required=True),
)
# Define the result object (which is passed back to Ansible)
result = dict(
changed=False
)
# Define the AnsibleModule object that will be instatiated when the module runs
module = AnsibleModule(
argument_spec=module_args,
supports_check_mode=True
)
# From this point and down, is where the actual "doing" of the module takes place
# We start populating the result object with the hostname of the WLC.
result['hostname']=module.params['hostname']
# Then we check if the text "restconf" is present in the run-config, and write some
# corresponding values to the result object to pass back to Ansible
if "restconf" in module.params['show_run']:
result['restconf_enabled']=True
result['comments']="RESTCONF status: Enabled"
else:
result['restconf_enabled']=False
result['comments']="RESTCONF status: Disabled"
# After doing the work, return the result back to Ansible as JSON
module.exit_json(**result)
def main():
run_module()
if __name__ == '__main__':
main()
check_restconf_status.py
Lab Exercise #24: Ansible - Writing your own module using Python
---
- name: Module demo
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: Gather IOS facts
cisco.ios.ios_facts:
gather_subset: all
register: facts
- name: Check if RESTCONF is enabled
check_restconf_status:
hostname: "{{ facts.ansible_facts.ansible_net_hostname }}"
show_run: "{{ facts.ansible_facts.ansible_net_config }}"
register: result
- name: Write results to YAML file
ansible.builtin.copy:
dest: "./logs/audit_{{ facts.ansible_facts.ansible_net_hostname }} ({{ '%Y-%m-%d' | strftime }}).yml"
mode: "0600"
content: "{{ result | to_nice_yaml }}"
ansible-using-module-playbook.yml
wlc:
hosts:
192.168.10.9:
192.168.10.30:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2024!
ansible_password: ChangeMe2024!
ansible_user: devnet-adm
ansible_host_key_checking: False
hosts.yml

## Slide 39: Ansible - Writing your own module - Example output
Lab Exercise #24: Ansible - Writing your own module using Python
Example output
Example of the written logfile (YAML) …. and the same, as JSON

## Slide 40: Ansible – Using RESTCONF + Python-module - Intro
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
This is another exercise where we create our own Python module to do some "magic" with output from Ansible, and return them back to Ansible after being processed
We will combine this with using RESTCONF directly from Ansible, as this is very fast compared to getting the same results using the command line
By "very fast" that refers to the run-time, but there will often be some more investigation to do first to get the correct YANG module path, compared to your well-known CLI command to do the same
The example will
  Get all interfaces from the IOS-XE device using RESTCONF, including the descriptions
  If the description of GigabitEthernet1 contains the word "Uplink" it will do nothing
  If the description of GigabitEthernet1 does NOT contain the word "Uplink", it will create a new text for the description, with "Uplink" and a timestamp for the change
  Push the updated interface config (description) back to the device using RESTCONF
Be aware that this example takes a lot of shortcuts, just to show the concept. Like being valid only for GigabitEthernet1's description. And no error checking (try to run it if you have no description at all on the Gig1 interface…)

## Slide 41: Ansible – Using RESTCONF + Python-module - Tasks
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
Task 0: Set up the files and folders and VS Code
  Create a working directory and a playbook file "ansible-using-module-playbook.yml"
  Copy the hosts.yml from previous projects
  Create a "library" folder with a file "update_description.py" inside
  Remember to activate the ansible-venv (use this for both Ansible and Python files in this exercise)
Task 1: Find the correct RESTCONF path
  Use YANG Suite or yangcatalog.org, check the module Cisco-IOS-XE-native and the :native/interface path
Task 2: Create the Ansible playbook
  Get interface list with RESTCONF (see Lab 23, but check out the YANG path Cisco-IOS-XE-native:native/interface instead)
  Do something with the interface dictionary in a Python module (see Lab 24, but pass in restconf_result['json'] instead), return the interface dict to Ansible
  Update the interface list/description using RESTCONF with the returned interface dict
  3 "extra" tasks could be "view result" tasks between each of your main tasks, for easier debugging
Task 3: Create the Python module
  Use the example in the Ansible docs "Developing modules", or the module from the previous lab as an example https://docs.ansible.com/ansible/latest/dev_guide/developing_modules_general.html
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab25_Ansible-RESTCONF-python$ source ~/ansible-venv/bin/activate
  (ansible-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab25_Ansible-RESTCONF-python$ ansible --version

## Slide 42: Ansible – Using RESTCONF + Python-module - Hints for Task 1
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
Example on using YANG Suite to find the correct path

## Slide 43: Ansible – Using RESTCONF + Python-module - Hints for Task 1
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
Check in Postman:
Then we choose only a couple of fields, and try again

## Slide 44: Ansible – Using RESTCONF + Python-module - Hints for Task 2
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
We start by creating the task that gets the data from WLC, using the RESTCONF path we have tested in Postman
We create a simple "view" task, to easier understand and debug what we have got out. Only if the status code = 200.

## Slide 45: Ansible – Using RESTCONF + Python-module - Hints for Task 2
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
Then we create a task that will send the interface dictionary (in JSON format) to our Python module for processing
We only do this if (when: ) the status code from our RESTCONF call equals 200 ("OK")
Again, we create a simple "view" task to view the results/output of the Python module processing, which we have registered in the variable "update_description_result"
And again, only if the result of the original RESTCONF call was "200 OK"

## Slide 46: Ansible – Using RESTCONF + Python-module - Hints for Task 2
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
The last part of the playbook, you might want to write after or in parallel with writing the Python module as it includes using the output from the module
We create the final of our three primary tasks for this playbook, updating the WLC interface description using RESTCONF
Notice that the use of the uri module is similar to the read task, only using PATCH instead of GET, and actually having some data in the "body" field. What we put in there is based on what we got out, only modified in the Python module which we will look into next
As usual, we have a "view" task to check the output

## Slide 47: Ansible – Using RESTCONF + Python-module - Hints for Task 3
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
Now we are ready to write the Python module "update_description.py". Lots of it will be identical to the previous Lab, but we have only one input parameter now. This will be the dictionary with the output from the RESTCONF call.
Then we do the actual reading and manipulation of the input
Put the input dictionary in a variable
Extract the description text. An intermediate step here could be to do a print() of the interface_dict
Check if the text "Uplink" is in the description. If it is, we do nothing
If there is no "Uplink" text in the description, we create a new description text, including a timestamp
Then, we put the updated interface dictionary into the "result" dictionary, so Ansible can use it. Note here, that we put it under the key ['new_interface_dict'] which is where we extract it from in the Ansible playbook (line 53)

## Slide 48: Ansible – Using RESTCONF + Python-module - Hints for Task 3
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
You can test the writing part in Postman
Change "GET" to "PATCH"
Put the modified body field in the "body" section

## Slide 49: Ansible – Using RESTCONF + Python-module - Hints for Task 3
Using the variable that was updated with the Python module
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
This is the same part we tested in Postman, only in Ansible

## Slide 50: Ansible – Using RESTCONF + Python-module - Example solution
---
- name: Interface Playbook
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: Get Interface list with RESTCONF
ansible.builtin.uri:
url: "https://{{ ansible_host }}/restconf/data/Cisco-IOS-XE-native:native/interface?fields=GigabitEthernet/name;GigabitEthernet/description"
user: "{{ ansible_user }}"
password: "{{ ansible_password }}"
method: GET
headers:
Content-Type: 'application/yang-data+json'
Accept: 'application/yang-data+json'
body_format: json
body:
validate_certs: false
status_code:
- 200
- 204
- 404
register: restconf_result
- name: Do something with the interface list in a Python module
update_description:
interface_dict: "{{ restconf_result['json'] }}"
register: update_description_result
when: restconf_result.status == 200
- name: View result
ansible.builtin.debug:
msg: "{{ update_description_result }}"
when: restconf_result.status == 200
- name: Update Interface list with RESTCONF
ansible.builtin.uri:
url: "https://{{ ansible_host }}/restconf/data/Cisco-IOS-XE-native:native/interface"
user: "{{ ansible_user }}"
password: "{{ ansible_password }}"
method: PATCH
headers:
Content-Type: 'application/yang-data+json'
body_format: json
body: "{{ update_description_result.new_interface_dict }}"
validate_certs: false
status_code:
- 200
- 204
- 404
register: restconf_write_result
- name: View result from RESTCONF write
ansible.builtin.debug:
msg: "{{ restconf_write_result }}"
when: restconf_write_result.status == 204
interface-playbook.yaml
# Written by Andreas Koksrud, based on framework from Erik Rongved and Espen Frøstrup.
from ansible.module_utils.basic import AnsibleModule
from datetime import datetime
def run_module():
# Define available arguments/parameters available to pass to the module from Ansible
module_args = dict(
interface_dict=dict(type='dict', required=True),
)
# Define the result object (which is passed back to Ansible)
result = dict(
changed=False
)
# Define the AnsibleModule object that will be instatiated when the module runs
module = AnsibleModule(
argument_spec=module_args,
supports_check_mode=True
)
# From this point and down, is where the actual "doing" of the module takes place
interface_dict = module.params['interface_dict']
timestamp = datetime.now().strftime('%D %H:%M:%S')
description = interface_dict['Cisco-IOS-XE-native:interface']['GigabitEthernet'][0]['description']
# If the description field contains "Uplink" we will do nothing. If not, we will change the description including a timestamp just for fun
if "Uplink" in description:
result['Gi1_old_description'] = description
result['Gi1_new_description'] = description
result['new_interface_dict'] = interface_dict
result['comments'] = f"Unchanged"
else:
result['Gi1_old_description'] = description
result['Gi1_new_description'] = f"Uplink - modified {timestamp}"
interface_dict['Cisco-IOS-XE-native:interface']['GigabitEthernet'][0]['description'] = f"Uplink - modified {timestamp}"
result['new_interface_dict'] = interface_dict
result['changed'] = True
result['comments'] = f"Changed {timestamp}"
# After doing the work, return the result back to Ansible as JSON
module.exit_json(**result)
def main():
run_module()
if __name__ == '__main__':
main()
update_description.py
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
hosts.yml
wlc:
hosts:
192.168.10.9:
192.168.10.30:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2024!
ansible_password: ChangeMe2024!
ansible_user: devnet-adm
ansible_host_key_checking: False
WLC before changes
wlc9#show run int g1
Building configuration...
Current configuration : 164 bytes
!
interface GigabitEthernet1
description Test123
switchport trunk native vlan 10
switchport trunk allowed vlan 10,11
switchport mode trunk
negotiation auto
end
WLC after changes
wlc9#show run int g1
Building configuration...
Current configuration : 194 bytes
!
interface GigabitEthernet1
description Uplink - modified 10/15/24 20:25:40
switchport trunk native vlan 10
switchport trunk allowed vlan 10,11
switchport mode trunk
negotiation auto
end

## Slide 51: Ansible – Using RESTCONF + Python-module - Example output
Lab Exercise #25: Ansible - Using RESTCONF + Python-module
One of the WLCs were not available
The Python module did something to the input. Since we put result['changed']=True, it will report that the task did change something
View result from the Python module, here we can see the full "result", including the new interface dict which we use in the RESTCONF task to write to the WLC next
Here we have written to WLC using RESTCONF
And print the write result

## Slide 52: Organizing projects using import_playbook - Intro
Lab Exercise #26: Ansible - Organizing projects using import_playbook
Reference: https://docs.ansible.com/ansible/latest/tips_tricks/sample_setup.html#sample-directory-layout
For larger projects, there are several ways to organize stuff
I like to break projects down into as small parts as possible
  Each part will be easy to both maintain and understand
  Code will be easier to reuse, change and troubleshoot
A playbook can run other playbooks by using the import_playbook module, which we will do in this exercise
A playbook can also call tasks by using the roles module, which is what we will do in the next exercise
General best practices (for Ansible and everything else…)
  Try to keep each part as simple as possible
  Use whitespace and comments to break things up and explain generously. What is obvious to you will probably not be obvious to everyone
In the following task we will create a (somewhat constructed) example using some of these techniques

## Slide 53: Organizing projects using import_playbook - Tasks
Lab Exercise #26: Ansible - Organizing projects using import_playbook
Task 0: Set up the files and folders and VS Code
  Create directories according to this example
  Create playbook files according to this example
Task 1: Create an extended variant of our hosts.yml file
  The inventory should include
    Shared switch (192.168.10.2)
    Your WLC (192.168.10.{YOUR_WLC_IP})
    Shared WLC (192.168.10.9)
Task 2: Create the three playbooks in the "audit_playbooks" folder
  They should be simple playbooks, use what you have learned. The example use two tasks:
    Gather IOS facts (using cisco.ios.ios_facts module)
    Output hostname and version (using ansible.builtin.debug module and prints text from the facts)
Task 3: Create the audit-network-playbook.yml playbook which is used to run the other three playbooks using the ansible.builtin.import_playbook module

## Slide 54: Organizing projects using import_playbook - Hints for Task 1
Lab Exercise #26: Ansible - Organizing projects using import_playbook
To accommodate for more than only WLCs, we create a slightly more advanced structure for our inventory file than we have done until now
Top-level group is "all"
Under "all" we have "children"
Under the children we have "wlc" and "switch"
The "vars" are common for all devices, so we have it directly under the "all" group, on the same level as "children"
It is also possible to have "vars" under each child group (on the same level as "hosts"). This is not used here.
It is also possible to have vars under each host. This is not used here.

## Slide 55: Organizing projects using import_playbook - Hints for Task 2
Lab Exercise #26: Ansible - Organizing projects using import_playbook
This is the "audit-wlcs-playbook.yml". The others in the example will be identical except the task name
For real-world the tasks for each device type would probably differ, else they don't need to be separate 
We start with the usual playbook opening we have used in the previous tasks
Then we have a "Gather IOS facts" task using the "cisco.ios.ios_facts" module: Register the result in a variable for later use
Lastly we have a output task, using "ansible.builtin.debug" module to output parts of the registered results.
Notice we use Jinja2 here. To see the full contents of "facts1" you could run this using only msg: {{ facts1 }} to see what is contained within the results. Then expand to msg: {{ facts1.ansible_facts }} before using the single values in your text
Copy-paste this playbook to similar variants for router and switch (change hosts: wlc to hosts: switch and hosts: router)

## Slide 56: Organizing projects using import_playbook - Hints for Task 3
Lab Exercise #26: Ansible - Organizing projects using import_playbook
In the main playbook "audit-network-playbook.yml" we have 3 tasks with only one line in each. They simply run the other playbooks (from the subfolder)

## Slide 57: Organizing projects using import_playbook - Example solution
Lab Exercise #26: Ansible - Organizing projects using import_playbook
---
- name: Audit WLCs
ansible.builtin.import_playbook: audit_playbooks/audit-wlcs-playbook.yml
- name: Audit switches
ansible.builtin.import_playbook: audit_playbooks/audit-switches-playbook.yml
- name: Audit routers
ansible.builtin.import_playbook: audit_playbooks/audit-routers-playbook.yml
audit-network-playbook.yml
---
- name: Audit routers
hosts: router
connection: network_cli
gather_facts: false
tasks:
- name: Gather IOS facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Output hostname and version
ansible.builtin.debug:
msg: "Hostname: {{ facts1.ansible_facts.ansible_net_hostname }} (version {{ facts1.ansible_facts.ansible_net_version }})"
audit-routers-playbook.yml
all:
children:
wlc:
hosts:
192.168.10.9:
192.168.10.30:
switch:
hosts:
192.168.10.2:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2024!
ansible_password: ChangeMe2024!
ansible_user: devnet-adm
ansible_host_key_checking: False
hosts.yml
---
- name: Audit switches
hosts: switch
connection: network_cli
gather_facts: false
tasks:
- name: Gather IOS facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Output hostname and version
ansible.builtin.debug:
msg: "Hostname: {{ facts1.ansible_facts.ansible_net_hostname }} (version {{ facts1.ansible_facts.ansible_net_version }})"
audit-switches-playbook.yml
---
- name: Audit WLCs
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: Gather IOS facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Output hostname and version
ansible.builtin.debug:
msg: "Hostname: {{ facts1.ansible_facts.ansible_net_hostname }} (version {{ facts1.ansible_facts.ansible_net_version }})"
audit-wlcs-playbook.yml

## Slide 58: Organizing projects using import_playbook - Example output
Lab Exercise #26: Ansible - Organizing projects using import_playbook
Since we do not have a "router" group in our hosts.yml file, we get a warning when we run the playbook since it does not match any host groups

## Slide 59: Organizing projects using Roles - Intro
Lab Exercise #27: Ansible - Organizing projects using Roles
Reference: https://docs.ansible.com/ansible/latest/network/getting_started/network_roles.html
Instead of using a master playbook to run other playbooks, in this exercise we will use "roles" to call tasks on each device that has that role
The example will still be somewhat constructed and simplified to primarily show the concept of roles rather than being super-useful in the real world by itself
This example contains two roles
  get_version: This role gets and prints the current version of the device, and is applied to all our devices (reuse some of the playbook from Lab 5)
  get_max_aps: This gets the maximum number of APs on a WLC, it is applied only to the WLC (reuse playbook from Lab 20)

## Slide 60: Organizing projects using Roles - Tasks
Lab Exercise #27: Ansible - Organizing projects using Roles
Task 0: Set up the files and folders and VS Code
  Create directory get_max_aps and subdirectory tasks, wherein you create main.yml
  Create directory get_version and subdirectory tasks, wherein you create main.yml
  Create the audit-network-playbook.yml
  Copy the hosts.yml file from the previous exercise
Task 1: Create the audit-network-playbook.yml content
  Playbook task 1: Get version from all Cisco devices, for "all" hosts, using the roles "get_version"
  Playbook task 2: Get max APs from WLCs, for "wlc" hosts, using the roles "get_max_aps"
Task 2: Create the role get_version
  Edit the main.yml in the get_version/tasks folder. It should have two tasks:
    Gather IOS facts. Reuse from Lab 5, but only the task, not the playbook stuff before the task. You will need to de-indent this to avoid indentation errors since you drop the "outer layer" in the yaml file
    Ouput task, use the ansible.builtin.debug module instead of writing to file as you did in Lab 5. You can narrow down the output to only ansible_net_hostname and ansible_net_version with some enclosing text
Task 3: Create role get_max_aps
  Edit the main.yml in the get_max_aps/tasks folder. It should have two tasks:
    Gather Max APs supported. Reuse from Lab 20, but only the task, not the playbook stuff before the task. You will need to de-indent this to avoid indentation errors since you drop the "outer layer" in the yaml file
    Ouput task, use the ansible.builtin.debug module, you can print the {{ result.stdout }} message

## Slide 61: Organizing projects using Roles - Hints for Task 1
Lab Exercise #27: Ansible - Organizing projects using Roles
We start with creating the audit-network-playbook.yml content
It consists of two tasks, as you can see there is not any explicit "doing" in these tasks, they just have some roles assigned
To expand this example, you could have more roles under the relevant tasks for the different device groups. For instance, the roles under the first task could also include roles "get_restconf_status", "backup_run_config" etc. The WLC specific task could have roles for "get_ap_summary", "get_wireless_clients" etc
Our reusable roles are entered under the "roles" section in each task

## Slide 62: Organizing projects using Roles - Hints for Task 2
Lab Exercise #27: Ansible - Organizing projects using Roles
To "create" the role get_version we have created the subfolder "get_version" with another subfolder "tasks", in where there is a file named "main.yml". This structure is identical for all roles, just change the upper folder name
As you can see from the example below, the role itself does just contain the same tasks that we create in Lab5, except that we output the results to the terminal using debug, instead of writing to a file

## Slide 63: Organizing projects using Roles - Hints for Task 3
Lab Exercise #27: Ansible - Organizing projects using Roles
The "get_max_aps" role is created in the same way as the previous role. You just have to have the folder named after your role, create a "tasks" folder inside that, and the "main.yml" file in the tasks folder
The tasks in the role main.yml are copy-paste from Lab20, just remember to de-indent them one level, since they are on their own and not under a "tasks:" statement

## Slide 64: Organizing projects using Roles - Example solution
Lab Exercise #27: Ansible - Organizing projects using Roles
---
- name: Get version from all Cisco devices
hosts: all
connection: network_cli
gather_facts: false
roles:
- get_version
- name: Get max APs
hosts: wlc
connection: network_cli
gather_facts: false
roles:
- get_max_aps
audit-network-playbook.yml
---
- name: "Get Max APs supported with CLI command"
cisco.ios.ios_command:
commands: "show wireless summary | include Max APs"
register: result
- name: "View result"
ansible.builtin.debug:
msg: "{{ result.stdout }}"
get_max_aps/tasks/main.yml
all:
children:
wlc:
hosts:
192.168.10.9:
192.168.10.30:
switch:
hosts:
192.168.10.2:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2024!
ansible_password: ChangeMe2024!
ansible_user: devnet-adm
ansible_host_key_checking: False
hosts.yml
---
- name: Gather IOS facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Output hostname and version
ansible.builtin.debug:
msg: "Hostname: {{ facts1.ansible_facts.ansible_net_hostname }} (version {{ facts1.ansible_facts.ansible_net_version }})"
get_version/tasks/main.yml

## Slide 65: Organizing projects using Roles - Example output
Lab Exercise #27: Ansible - Organizing projects using Roles

## Slide 66: Next steps suggestions
A possible next step after doing these labs, would be to look into AWX
  Web based GUI, great for organizing and orchestrating
  Task engine for scheduling playbooks etc
Using NetBox for inventory management and single source of truth
  Ansible playbooks can run based on an inventory in NetBox
  Ansible playbooks can populate fields in NetBox
  Fields (standard or custom) in NetBox can decide stuff in Ansible
    E.g.: is it a WLC? -> Run this task
Any ideas for new exercises to add to this deep dive? What would you like to see in the next version?
In-depth: Ansible - Next steps

## Slide 67: In-depth: Python
This part of the Day 2 labs will focus on using Python
Python for automation can be used directly, or as a building block in other tools/solutions
!!! As you progress through the script and tasks, you will come across missing packages !!!
  Install them in your VENV (python-lab-venv) with the following command (netmiko used as example)
  If you are not in your venv, you enter using this command. It will be repeated in the Task 0 of each exercise.
  You will see which venv you are in by the (python-lab-venv) at the beginning of each line
  To "get out" of your venv, you can run the "deactivate" command, or restart the terminal/SSH
In-depth: Python
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/ Lab40_Python_Netmiko$ pip install netmiko
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab40_Python_Netmiko$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/ Lab40_Python_Netmiko$
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/ Lab40_Python_Netmiko$ deactivate
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab40_Python_Netmiko$

## Slide 68: Python - Using Netmiko - Intro
In this exercise, we will write a python script that connects to the WLC using SSH
The script will
  Take the WLC IP as input
  Do a user/pass prompt before connecting
  Have a menu with these choices
    Show AP summary
    Show client summary
    Show CDP neighbors
    Save run-config to a timestamped file
You can extend the script as you like, be creative
There is not much error checking, you can put in stuff like checking if it is really a WLC, etc
Reference: https://github.com/ktbyers/netmiko/blob/develop/README.md
Lab Exercise #40: Python - Netmiko

## Slide 69: Python - Using Netmiko - Tasks
Task 0: Set up the files and folders and VS Code
  Create a working directory
  Create a Python file called "netmiko-script.py"
  Activate the python-lab-venv
Task 1: Write a python script that
  Take the WLC IP as input
  Prints the WLC IP with some text as output, then quits
Task 2: Extend the script, so it will
  Ask for username and password
  Connect to the IP using the username and password
  Do a show command (show ip interfaces brief or something), then quits
(optional) Task 3: Extend the script, so it will
  Present a menu with the 4 choices from previous slide
  Run the commands, then quit
Lab Exercise #40: Python - Netmiko
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab40_Python_Netmiko$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/ Lab40_Python_Netmiko$ python --version

## Slide 70: Python - Using Netmiko - Hints: Task 1
Start with the print command, printing a static text
Then add the input, which is saved to a variable "wlc_ip"
Notice the "f-string" formatting of the printed text. This is widely used in Python to use variables inside strings.
To keep this short and simple, we have no error checking. So the "IP" you enter could just as well be "blablabla"
This will be the case in most of these labs, it is by design
Depending on the usage of your script, you should probably add some error checking, especially if used by others. One example would be to use regex to check if the value is a correct IP address, so the output could be like this
Lab Exercise #40: Python - Netmiko
  40_Python_Netmiko$ python netmiko-script.py
  WLC IP:
  40_Python_Netmiko$ python netmiko-script.py
  Enter WLC IP: 1.2.3.4
  The WLC IP is: 1.2.3.4
  40_Python_Netmiko$ python netmiko-script.py
  Enter WLC IP: blablabla
  The WLC IP is: blablabla
  40_Python_Netmiko$ python netmiko-script.py
  Enter WLC IP: blablabla
  Invalid IP address, exiting...

## Slide 71: Python - Using Netmiko - Hints: Task 2
Building on the work from Task 1, we add user/pass input
Now, we will make Netmiko connect and run a command
  import the ConnectHandler function from Netmiko
  Create a "cisco_wlc" dictionary which ConnectHandler use as input
  Create a "command" variable, which we print, and send to the WLC
Lab Exercise #40: Python - Netmiko
  40_Python_Netmiko$ python netmiko-script.py
  Enter WLC IP: 192.168.10.9
  Username: devnet-adm
  Password:
  Command: show ip int brief
  Interface IP-Address OK? Method
  GigabitEthernet1 unassigned YES unset
  GigabitEthernet2 unassigned YES unset
  GigabitEthernet3 unassigned YES unset
  Vlan1 unassigned YES NVRAM
  Vlan10 192.168.10.10 YES NVRAM
Example output from running the script so far

## Slide 72: Python - Using Netmiko - Hints: Task 3
To accomplish this you should separate the tasks into functions
You write a function this way
To use the function, use the function name
An example structure for Task3 can be:
  imports (same as Task2)
  Define functions for each menu choice (hints on next page)
  Setup netmiko
  Create a while loop with a menu
Lab Exercise #40: Python - Netmiko

## Slide 73: Python - Using Netmiko - Hints: Task 3
Example of functions
Lab Exercise #40: Python - Netmiko

## Slide 74: Python - Using Netmiko - Example solution
import getpass
import datetime
from netmiko import ConnectHandler
wlc_ip = input('WLC IP: ')
username = input('Username: ')
password = getpass.getpass('Password: ')
# Use netmiko to connect to the WLC
cisco_wlc = {
'device_type': 'cisco_ios',
'ip': wlc_ip,
'username': username,
'password': password
}
net_connect = ConnectHandler(**cisco_wlc)
# Define functions
def show_ap_summary():
print(net_connect.send_command("show ap summary"))
def show_client_summary():
print(net_connect.send_command("show wireless client summary"))
def show_cdp_neighbors():
print("WLC CDP neighbors:\n-------------------------------------")
print(net_connect.send_command("show cdp neighbors"))
print("AP CDP neighbors:\n-------------------------------------")
print(net_connect.send_command("show ap cdp neighbors"))
def save_config_to_file():
output=net_connect.send_command("show run")
now = datetime.datetime.now()
filename = f"{wlc_ip}-run-conf ({now.strftime('%Y-%m-%d %H:%M:%S')}).txt"
with open(filename, 'w') as f:
f.write(output)
print(f"Config saved to {filename}")
# Text menu with 4 options that run each of the functions, or quit
while True:
print("\nText Menu:")
print("1. Show AP summary")
print("2. Show client summary")
print("3. Show CDP neighbors")
print("4. Save run-config to file")
print("5. Quit")
choice = input("Enter choice: ")
if choice == "1":
show_ap_summary()
elif choice == "2":
show_client_summary()
elif choice == "3":
show_cdp_neighbors()
elif choice == "4":
save_config_to_file()
elif choice == "5":
net_connect.disconnect()
break
else:
print("Invalid choice. Please choose again.")
netmiko-script.py
Lab Exercise #40: Python - Netmiko
Here is an example solution
Runtime output should be like this
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab40_Python_Netmiko$0_Python_Netmiko$ python netmiko-script.py
  WLC IP: 192.168.10.9
  Username: devnet-adm
  Password:
  Text Menu:
  1. Show AP summary
  2. Show client summary
  3. Show CDP neighbors
  4. Save run-config to file
  5. Quit
  Enter choice: 4
  Config saved to 192.168.10.9-run-conf (2024-09-10 19:44:50).txt
  Text Menu:
  1. Show AP summary
  2. Show client summary
  3. Show CDP neighbors
  4. Save run-config to file
  5. Quit
  Enter choice:

## Slide 75: Get client table using RESTCONF - Intro
Get client table from WLC using RESTCONF call
Put client table in pandas dataframe
Export to Excel
Very similar to getting the AP table from Day 1
You can try recreating this using the hints in this exercise
Alternatively you can copy and modify the get-ap-table.py from day 1
Lab Exercise #41: Python - Get clients using RESTCONF

## Slide 76: Get client table using RESTCONF - Tasks
Lab Exercise #41: Python - Get clients using RESTCONF
Task 0: Set up the files and folders and VS Code
  Create a working directory
  Create a Python file called "get-client-table.py"
  Activate the python-lab-venv
Task 1: Use Postman to find and test an URL that gives you the connected clients
Task 2: Write a Python script that
  Ask for WLC IP, username and password
  Connects to the WLC using RESTCONF with the URL created in Task 1
  Print the results
(optional) Task 3: Extend the script, so it will
  Check if response status code is 200, if not, show the status code and message
  Flatten the JSON of the response to a table, store in a pandas dataframe
  Save the dataframe to Excel
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab40_Python_Netmiko$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/ Lab40_Python_Netmiko$ python --version

## Slide 77: Get client table using RESTCONF - Hints - Task 1
Task 1: Use Postman to find and test an URL that gives you the connected clients
Use YANG Suite, search for modules with the text "client"
The module we will use in this exercise is "Cisco-IOS-XE-wireless-client-oper"
Look at the request we created in the Day 1 exercise 9 "Exploring Postman"'. It contains the info that you need, and how to get there
Lab Exercise #41: Python - Get clients using RESTCONF

## Slide 78: Get client table using RESTCONF - Hints - Task 2
Task 2: Write a Python script that
  Ask for WLC IP, username and password
  Connects to the WLC using RESTCONF with the URL created in Task 1
  Print the results
The input part of this script you can reuse from the netmiko script in Lab 40
The RESTCONF connection will use the "requests" module. You should be able to get some hints from Postman, "output to code" and choose Python
To create the URL including the WLC IP, you can use f-strings, like this:
You can end/check this task by using a print statement after the requests call
Remember the imports (and maybe you need some pip installs along the way)
Lab Exercise #41: Python - Get clients using RESTCONF

## Slide 79: Get client table using RESTCONF - Solution
This example solution also includes the Task3 optional parts
Lab Exercise #41: Python - Get clients using RESTCONF
import requests
import getpass
import pandas as pd
wlc = input("Enter WLC IP: ")
user = input("Enter user: ")
password = getpass.getpass("Enter password: ")
url = f"https://{wlc}/restconf/data/Cisco-IOS-XE-wireless-client-oper:client-oper-data/common-oper-data"
payload = {}
headers = {
'Accept': 'application/yang-data+json',
'Content-Type': 'application/yang-data+json'
}
response = requests.get(url, auth=(user, password), headers=headers, data=payload, verify=False)
if (response.status_code==200):
ap_table = pd.json_normalize(response.json()['Cisco-IOS-XE-wireless-client-oper:client-oper-data'])
print(ap_table)
ap_table.to_excel('ap_table.xlsx')
else:
print(f"Status code: {response.status_code}: {response.reason}")
get-client-table.py
Create the API URL
Do the actual RESTCONF call
Check if response status code is 200, if not, show the status code and message
Flatten the JSON of the response to a table, store in a pandas dataframe
Save the dataframe to Excel

## Slide 80: Get metrics and draw a graph - Intro
Poll some metrics from WLC using RESTCONF
Draw a graph of the metrics
We will
  Get data using RESTCONF
  Put the data in an array
  Use the library matplotlib for plotting the graph
You will probably see that for pure monitoring, other tools (like Grafana) are way better 
Notice: To get this plot to show on your screen, in Task 3 you will need to use a local installation of Python (on your laptop). This was not part of the preparations, so if you do not have it (or want to install now), just look at the provided screenshot
Lab Exercise #42: Python - Get metrics and draw a graph

## Slide 81: Get metrics and draw a graph - Tasks
Lab Exercise #42: Python - Get metrics and draw a graph
Task 0: Set up the files and folders and VS Code
  Create a working directory "Lab42_Python-draw-metrics"
  Create a Python file "draw-metrics.py"
  Activate the python-lab-venv
Task 1: Use Postman to find and test an URL that gives you the 5-second CPU%
Task 2: Write a Python script that
  Ask for WLC IP, username and password
  Connects to the WLC using RESTCONF with the URL created in Task 1
  Loops and print the results every 2 seconds
Task 3: Use matplotlib and get the script to plot the results
  Store results in an array
  Print the array using matplotlib
(optional) Task 4: You can change the script to gather other data (#APs, #Clients, traffic)
  devnet-adm@ubuntu-devnet:~$ cd ~/wifi-automation/Lab42_Python-draw-metrics
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab42_Python-draw-metrics$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab42_Python-draw-metrics$ python --version

## Slide 82: Get metrics and draw a graph - Task 1 hints
Task 1: Use Postman to find and test an URL that gives you the 5-second CPU%
You can use YANG Suite to explore any module with "cpu"
Then test in Postman
Lab Exercise #42: Python - Get metrics and draw a graph

## Slide 83: Get metrics and draw graph - Task 2 hints
Task 2: Write a Python script that
  Ask for WLC IP, username and password
  Connects to the WLC using RESTCONF with the URL created in Task 1
  Loops and print the results every second
You can use the script from Lab 41 as a base
  Change the URL to the one you found in task 1
  Remove the pandas dataframe and write to Excel parts
  Start by printing response.json(), you can see how the JSON is built up
  Then print response.json['Cisco-IOS-XE-process-cpu-oper:five-seconds']
  Notice how you can reference keys inside a JSON using square brackets
  Create a "while True:" loop of the last part, starting before the response = requests.... line
  import time (at the top) and use time.sleep(1) inside the while-loop to pause for 1 second each iteration
  By using a while loop with no exit condition, you exit the loop by pressing Ctrl+C
  To suppress the InsecureRequestWarning, import urllib3 and use urllib3.disable_warnings()
Lab Exercise #42: Python - Get metrics and draw a graph
import time
import requests
import getpass
import urllib3
urllib3.disable_warnings()
wlc = input("Enter WLC IP: ")
user = input("Enter user: ")
password = getpass.getpass("Enter password: ")
url = f"https://{wlc}/restconf/data/Cisco-IOS-XE-process-cpu-oper:cpu-usage/cpu-utilization/five-seconds"
payload = {}
headers = {
'Accept': 'application/yang-data+json',
'Content-Type': 'application/yang-data+json'
}
while True:
response = requests.get(url, auth=(user, password), headers=headers, data=payload, verify=False)
if (response.status_code==200):
print(response.json()['Cisco-IOS-XE-process-cpu-oper:five-seconds'])
else:
print(f"Status code: {response.status_code}: {response.reason}")
time.sleep(1)
draw-metrics.py (Task 2)

## Slide 84: Get metrics and draw a graph - Task 3 hints
Task 3: Use matplotlib and get the script to plot the results
  Store results in an array
  Print the array using matplotlib
  You will notice that "nothing happens". This is because matplotlib is running the plot on your Ubuntu server
  To show this, you must store the script on your computer, and run using your local Python installation
Lab Exercise #42: Python - Get metrics and draw a graph

## Slide 85: Get metrics and draw a graph - Solution
Importing neccessary modules
Input section for IP, user, pass
Craft the RESTCONF URL and headers
Initialize a table with the first value
Initialize the plot
Endless loop
Request to WLC
Append the value to the table
Plot and draw the table
Alternative if status is not 200 "OK"
Pause before repeating the loop
Lab Exercise #42: Python - Get metrics and draw a graph
import time
import requests
import getpass
import urllib3
import matplotlib.pyplot as plt
urllib3.disable_warnings()
wlc = input("Enter WLC IP: ")
user = input("Enter user: ")
password = getpass.getpass("Enter password: ")
url = f"https://{wlc}/restconf/data/Cisco-IOS-XE-process-cpu-oper:cpu-usage/cpu-utilization/five-seconds"
payload = {}
headers = {
'Accept': 'application/yang-data+json',
'Content-Type': 'application/yang-data+json'
}
cpu_values = [0]
plt.ion()
while True:
response = requests.get(url, auth=(user, password), headers=headers, data=payload, verify=False)
if (response.status_code==200):
cpu_values.append(response.json()['Cisco-IOS-XE-process-cpu-oper:five-seconds'])
plt.plot(cpu_values)
plt.draw()
plt.pause(1)
else:
print(f"Status code: {response.status_code}: {response.reason}")
time.sleep(1)
draw-metrics.py

## Slide 86: Get to know your AI companion - Intro and tasks
Did you install Codeium? Or do you have GitHub Copilot? One very useful example of what they are really good at, is documenting your stuff!
It can also help you get your ideas started. Beware that generative AI will not always make error-free code, or code that does what you intended. But it will often be a good start, and you can fix the rest yourself
In this exercise, you will open some of the previous scripts, and check out different AI stuff, using Codeium
Task 1: Document the code
Task 2: Generate inline comments
Task 3: See how generative AI would solve a previous task
Task 4: Use AI to add or improve parts of the script
Lab Exercise #43: Python - Get to know your AP companion

## Slide 87: AI - Task 1 - Document the code
Open one of the previous lab exercises. In this example we use the "get-client-table.py"
Select all text in the .py file, click Ctrl+I, and write "create detailed documentation"
Press "Accept" (or Alt+A) to accept
The results will vary, when running this script now I got this
The documentation is before the script
Lab Exercise #43: Python - Get to know your AP companion

## Slide 88: AI - Task 2 - Generate inline comments
To improve readability, we can get AI to create inline comments
Select all text in the .py file, click Ctrl+I, and write "create descriptive inline comments"
Press "Accept" (or Alt+A) to accept
The results will vary, when running this script now I got this
The comments are inline
Lab Exercise #43: Python - Get to know your AP companion

## Slide 89: AI - Task 2 - Follow-up
You can also do follow-ups to alter or specify the results
Press Ctrl+Z to undo, or do the last task again
Instead of Accept, choose "Follow-up"
Then, write "more detailed"
Press "Accept" (or Alt+A) to accept
The results will vary, when running this script now I got this
The comments are a bit more detailed
Lab Exercise #43: Python - Get to know your AP companion

## Slide 90: AI - Task 3 - Get AI to solve the task
Check how AI would solve the task
Create a new file "get-client-table-ai.py"
In the empty file, Click Ctrl+I
Press "Accept" (or Alt+A) to accept
Notice it is pretty similar to your script? Probably because it use your files to train(?)
Lab Exercise #43: Python - Get to know your AP companion

## Slide 91: AI - Task 4 - Use AI to add or improve parts
Find some part to improve/change
One example, enforce the user to input a valid IP address in the input part
Mark the "Enter WLC IP" line, press Ctrl+I
Press "Accept" (or Alt+A) to accept
Notice it adds "ipaddress" which is yellowed out by pylance. Try to import it.
Lab Exercise #43: Python - Get to know your AP companion

## Slide 92: Use .env file for variables - Intro
As an alternative to typing the WLC IP, username and password every time, they can be placed in a local file with the name ".env". By using this you can safely share the python script without including sensitive material in the script itself
We will modify the "netmiko-script.py" from Lab 40, by adding support for reading the .env file. The contents of the script (except for those modifications), are already explained in Lab 40
Remember that the .env file should be located in the same directory as you run the file from
!!! Note !!! .env files are NOT synced by Git, they are included in a ".gitignore" file. This is by purpose, and is WHY we are using .env files instead of writing stuff in cleartext in the code. So if you look in the "solutions" folder, there will be no .env files in this or any other directory, you must create your own.
Lab Exercise #44: Python - Use .env file for variables

## Slide 93: Use .env file for variables - Tasks
Lab Exercise #44: Python - Use .env file for variables
Task 0: Set up the files and folders and VS Code
  Create a working directory "Lab44_Python-use-env-variables"
  Create a file ".env"
  Copy the file "netmiko-script.py" from the previous exercise, or from the solutions folder
  Activate the python-lab-venv
Task 1: Take a look at https://pypi.org/project/python-dotenv/ and try implementing that in your script
(optional) Task 2: Add a text showing which WLC you are connected to
  devnet-adm@ubuntu-devnet:~$ cd ~/wifi-automation/Lab44_Python-use-env-variables
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab44_Python-use-env-variables$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab44_Python-use-env-variables$ python --version

## Slide 94: Use .env file for variables - Hints
Enter the variables you need in the .env file
Install dotenv for python, using PIP
!!! Notice the pip package name is not "dotenv" but "python-dotenv" !!!
Import dotenv in the python file
Load the env variables from file to a variable
Modify the code to use the variables
There is a line a way down also, referencing the WLC IP. Change that as well to use the env
Lab Exercise #44: Python - Use .env file for variables
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab44_Python-use-env-variables$ pip install python-dotenv
WLC_IP='192.168.10.{YOUR_WLC_IP}'
USERNAME='devnet-adm'
PASSWORD='ChangeMe2024!'
.env

## Slide 95: Use .env file for variables - Example solution
import getpass
import datetime
from netmiko import ConnectHandler
from dotenv import dotenv_values
# Import variables from the .env file
env = dotenv_values('.env')
# Use netmiko to connect to the WLC
cisco_wlc = {
'device_type': 'cisco_ios',
'ip': env['WLC_IP'],
'username': env['USERNAME'],
'password': env['PASSWORD']
}
net_connect = ConnectHandler(**cisco_wlc)
# Define functions
def show_ap_summary():
print(net_connect.send_command("show ap summary"))
def show_client_summary():
print(net_connect.send_command("show wireless client summary"))
def show_cdp_neighbors():
print("WLC CDP neighbors:\n-------------------------------------")
print(net_connect.send_command("show cdp neighbors"))
print("AP CDP neighbors:\n-------------------------------------")
print(net_connect.send_command("show ap cdp neighbors"))
def save_config_to_file():
output=net_connect.send_command("show run")
now = datetime.datetime.now()
filename = f"{env['WLC_IP']}-run-conf ({now.strftime('%Y-%m-%d %H:%M:%S')}).txt"
with open(filename, 'w') as f:
f.write(output)
print(f"Config saved to {filename}")
# Text menu with 4 options that run each of the functions, or quit
while True:
print('\nYou are connected to WLC: ' + env['WLC_IP'])
print("Menu:")
print("1. Show AP summary")
print("2. Show client summary")
print("3. Show CDP neighbors")
print("4. Save run-config to file")
print("5. Quit")
choice = input("Enter choice: ")
if choice == "1":
show_ap_summary()
elif choice == "2":
show_client_summary()
elif choice == "3":
show_cdp_neighbors()
elif choice == "4":
save_config_to_file()
elif choice == "5":
net_connect.disconnect()
break
else:
print("Invalid choice. Please choose again.")
netmiko-script.py
Lab Exercise #44: Python - Use .env file for variables
Here is an example solution
Runtime output should be like this
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab44_Python-use-env-variables$ python netmiko-script.py
  You are connected to WLC: 192.168.10.9
  Menu:
  1. Show AP summary
  2. Show client summary
  3. Show CDP neighbors
  4. Save run-config to file
  5. Quit
  Enter choice: 4
  Config saved to 192.168.10.9-run-conf (2024-09-10 19:44:50).txt
  You are connected to WLC: 192.168.10.9
  Menu:
  1. Show AP summary
  2. Show client summary
  3. Show CDP neighbors
  4. Save run-config to file
  5. Quit
  Enter choice:
Notice how you do not have to type in IP, user and password every time
The example output includes the optional task 2

## Slide 96: Using Nornir - Intro
Lab Exercise #45: Python - Using Nornir
Nornir is an automation framework written in Python
You use Python code to use Nornir (compared to Ansible where you use YAML files)
As with Ansible you will have
  Inventory
  Runbook (similar to Ansible "playbook")
  Plugins
There are pros and cons to every automation framework, test some variants and make up your own mind
As a consultant, you might be bound to what your customer use
Nornir vs Ansible pros: Speed, debugging, logging and "all-Python" approach
Ansible vs Nornir pros: Idempotency, simplicity, YAML approach and community
References:
  https://nornir.readthedocs.io/en/latest/
  https://developer.cisco.com/codeexchange/github/repo/neelimapp/nornir-sample-scripts/
  https://theworldsgonemad.net/2021/nornir-tasks/

## Slide 97: Using Nornir - Tasks
Lab Exercise #45: Python - Using Nornir
Task 0: Set up the files and folders and VS Code
  Create a working directory "Lab45_Python-Nornir"
  Create a file ".env" (similar to Lab 44)
  Create a file "hosts.yaml"
  Create a file "python-nornir-runbook.py". You can reuse the dotenv parts from Lab 44
  Activate the python-lab-venv
  Install Nornir and some additional packages we will use, in your venv, using pip
Task 1: Create inventory file
  This exercise will use a very simple hosts.yaml file for inventory, with only the devices and the device type. Username and password will come from the .env file
Task 2: Write a runbook that
  Connects to all devices in the inventory
  Do a "show ap summary"
  Print the results on screen
  devnet-adm@ubuntu-devnet:~$ cd ~/wifi-automation/Lab45_Python-Nornir
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab45_Python-Nornir$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab45_Python-Nornir$ python --version
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab45_Python-Nornir$ pip install nornir nornir-utils nornir-netmiko

## Slide 98: Using Nornir - Hints
Lab Exercise #45: Python - Using Nornir
In the .env file, we only put the username and password this time
In the hosts.yml we put the WLC IP, you can easily scale this to multiple devices
For the runbook "python_nornir_runbook.py"
  Reuse the dotenv import and env = dotenv_values('.env') from Lab 44
  Import some Nornir stuff that we need
  Initialize Nornir (nr = InitNornir())
  Set some Nornir defaults (nr.inventory.defaults.{blablabla})
    username, get this from env['USERNAME']
    password, get this from env['PASSWORD']
    platform, just set this to the string "ios"
  Run commands and save the output in "results"
    nr.run( task = netmiko_send_command command_string = "show ap summary" )
  Print "results" using Nornir: print_result(results)
USERNAME='devnet-adm'
PASSWORD='ChangeMe2024!'
.env
---
your_wlc:
hostname: 192.168.10.{YOUR_WLC_IP}
shared_wlc:
hostname: 192.168.10.9
hosts.yaml

## Slide 99: Using Nornir - Example solution
Lab Exercise #45: Python - Using Nornir
Here is an example solution
Runtime output should be similar to this
As long as you use "hosts.yaml" you don't have to point to this anywhere, as it is the default inventory file that Nornir will look for, in the folder you run the script from
You can use a dynamically created inventory, here are some examples
  Service-Now can pass an inventory when you run stuff based on something you pass from there
  You can use Netbox for inventory, and filter/pass/extract what you want from there. Like, if you get an action because an AP is down, run some checks on the switch and the WLC the AP was connected last. And some checks on all APs on the same location. Etc.
USERNAME='devnet-adm'
PASSWORD='ChangeMe2024!'
.env
---
your_wlc:
hostname: 192.168.10.{YOUR_WLC_IP}
shared_wlc:
hostname: 192.168.10.9
hosts.yaml
from dotenv import dotenv_values
from nornir import InitNornir # Initialize Nornir
from nornir_utils.plugins.functions import print_result # Print results
from nornir_netmiko.tasks import netmiko_send_command # Send Netmiko command
# Import variables from the .env file
env = dotenv_values('.env')
# Initialize Nornir
nr = InitNornir()
# Set defaults for all devices
nr.inventory.defaults.username = env['USERNAME'] # Username from .env
nr.inventory.defaults.password = env['PASSWORD'] # Password from .env
nr.inventory.defaults.platform="ios" # Platform set to Cisco IOS
# Run command on all devices
results = nr.run(
task=netmiko_send_command, # Use the task "netmiko_send_command"
command_string="show ap summary" # Command to run
)
# Print results
print_result(results)
python-nornir-runbook.py

## Slide 100: Nornir extended example - Intro
Lab Exercise #46: Python - Nornir extended example
In this task, we will combine our Nornir knowledge from the previous lab, with the script we created in the first Python exercise using Netmiko, as well as the Python exercise using .env file
In short, the single-WLC script using Netmiko will be changed so it runs on all WLCs in a Nornir inventory
You can easily expand the inventory to
  Your own WLC
  The shared WLC
  Other students' WLCs that you have access to

## Slide 101: Nornir extended example - Tasks
Lab Exercise #46: Python - Nornir extended example
Task 0: Set up the files and folders and VS Code
  Create a working directory "Lab46_Python-Nornir-extended"
  Create a file ".env" (copy from Lab 45)
  Create a file "hosts.yaml" (copy from Lab 45)
  Create a file "python-nornir-extended-runbook.py". Start by copy-pasting the "netmiko-script.py" from Lab 44
  Activate the python-lab-venv
  Nornir and required packages should already be installed from the previous lab
Task 1: Merge the necessary Nornir components from Lab 45 into the new runbook
  Add Nornir imports, set Nornir defaults, initialize Nornir
  Remove the Netmiko imports, definition of cisco_wlc object and initializing net_connect = ConnectHandler()
Task 2: Rewrite the functions that are called from the menu, to be run using nornir_netmiko and use the Nornir inventory
  All lines referring to "net_connect" will need to be changed
Task 3: Rewrite the menu with "You are connected to", to show all devices from the inventory that you will issue the commands to
  devnet-adm@ubuntu-devnet:~$ cd ~/wifi-automation/Lab46_Python-Nornir-extended
  devnet-adm@ubuntu-devnet:~/wifi-automation/Lab46_Python-Nornir-extended$ source ~/python-lab-venv/bin/activate
  (python-lab-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab46_Python-Nornir-extended$ python --version

## Slide 102: Nornir extended example - Task 1 hints
Lab Exercise #46: Python - Nornir extended example
In the .env file, we only put the username and password
In the hosts.yml we put the WLC IP, you can easily scale this to multiple devices
Add the Nornir imports, remove the Netmiko imports
Initialize Nornir and set the defaults. Remove the Netmiko initialization
USERNAME='devnet-adm'
PASSWORD='ChangeMe2024!'
.env
---
your_wlc:
hostname: 192.168.10.{YOUR_WLC_IP}
shared_wlc:
hostname: 192.168.10.9
hosts.yaml

## Slide 103: Nornir extended example - Task 2 hints
Lab Exercise #46: Python - Nornir extended example
Change all lines referring to "net_connect". That will be in each of the 4 functions
  show_ap_summary()
  Change:
  To:
  show_client_summary()
    Do the same changes as in previous function
  show_cdp_neighbors()
    Do the same changes as in previous functions
  save_config_to_file()
    Firstly, do the same changes as in previous functions:
      In the existing script, we saved the output from netmiko to "output"
      Now, change this to the same format as the previous functions, saving the results in "results". Exactly the same as the previous functions. The rest of this function (saving of the file) will follow on next slide
print(net_connect.send_command("show ap summary"))
results = nr.run(
task=netmiko_send_command,
command_string="show ap summary"
)
print_result(results)
output=net_connect.send_command("show run")

## Slide 104: Nornir extended example - Task 2 hints continued
Lab Exercise #46: Python - Nornir extended example
Continuing on the save_config_to_file() function, we are now ready to save the results to a file
  The results object is actually an object of type "AggregatedResult", containing results for each object that tasks has been run on, as a "MultiResult" object. Each MultiResult object is accessed by the name of the host. So for our example host file you would have two MultiResult objects:
  Each of these contains a list with the results of each task run on that object, starting from 0. So with one task run for the "your_wlc" host, the output (e.g. the "show run") will be stored in:
  This object will also have a status (boolean value) telling if the task failed. We will use this to only save the run-config if the command has NOT failed. Failed tasks can be if login failed, host unreachable, etc.
  So, the rest of the function can be something like this:
Reference and more info: https://nornir.readthedocs.io/en/v2.5.0/tutorials/intro/task_results.html
results['your_wlc'] # Object of type MultiResult
results['shared_wlc'] # Object of type MultiResult
results['your_wlc'][0] # Output of the first task. Use str() to change this to a text object.
results['your_wlc'][0].failed # Boolean value, True or False
for host in nr.inventory.hosts: # Loop over all hosts in the Nornir inventory
if results[host][0].failed: # Check if the first task have status failed, if failed print an error message
print(f'Save run-config for {host} ({nr.inventory.hosts[host].hostname}) failed. See nornir.log for details.')
else: # Else (if the task is NOT failed), run the file writing part
now = datetime.datetime.now() # Get the current timestamp
filename = f"{nr.inventory.hosts[host].hostname}-run-conf ({now.strftime('%Y-%m-%d %H:%M:%S')}).txt" # Make a filename
with open(filename, 'w') as f: # Write the actual file
f.write(str(results[host][0]))
print(f"Config saved to {filename}")

## Slide 105: Nornir extended example - Task 3 hints
Lab Exercise #46: Python - Nornir extended example
Task 3 was to rewrite the menu elements. The old menu started by showing the (one) WLC you were connected to. For the Nornir variant we can be connected to lots of WLCs, so we have to adjust the menu accordingly
  Old WLC connection info:
  New WLC connection info:
  In this example, you loop over the hosts found in the Nornir inventory (nr.inventory.hosts), and call the element in each of your loop interations "host"
  In the next line you use an f-string, and print the text of the host, along which the hostname found in the Nornir inventory, in our case the "hostname" will be the IP address of the device
  This info corresponds to what you have written in the hosts.yaml file
print('\nYou are connected to WLC: ' + env['WLC_IP'])
print('\nYou are connected to these devices: ')
for host in nr.inventory.hosts:
print(f'-> {host}: {nr.inventory.hosts[host].hostname}')
---
your_wlc:
hostname: 192.168.10.10
shared_wlc:
hostname: 192.168.10.9
Output in my example

## Slide 106: Nornir extended example - Example solution
Lab Exercise #46: Python - Nornir extended example
Here is an example solution
Runtime output should be similar to this
USERNAME='devnet-adm'
PASSWORD='ChangeMe2024!'
.env
---
your_wlc:
hostname: 192.168.10.{YOUR_WLC_IP}
shared_wlc:
hostname: 192.168.10.9
hosts.yaml
import datetime
from dotenv import dotenv_values
from nornir import InitNornir # Initialize Nornir
from nornir_utils.plugins.functions import print_result # Print results
from nornir_netmiko.tasks import netmiko_send_command # Send Netmiko command
# Import variables from the .env file
env = dotenv_values('.env')
# Initialize Nornir
nr = InitNornir()
# Set defaults for all devices
nr.inventory.defaults.username = env['USERNAME'] # Username from .env
nr.inventory.defaults.password = env['PASSWORD'] # Password from .env
nr.inventory.defaults.platform="ios" # Platform set to Cisco IOS
# Define functions
def show_ap_summary():
results = nr.run(
task=netmiko_send_command,
command_string="show ap summary"
)
print_result(results)
def show_client_summary():
results = nr.run(
task=netmiko_send_command,
command_string="show wireless client summary"
)
print_result(results)
def show_cdp_neighbors():
print("WLC CDP neighbors:\n-------------------------------------")
results = nr.run(
task=netmiko_send_command,
command_string="show cdp neighbors"
)
print_result(results)
print("AP CDP neighbors:\n-------------------------------------")
results = nr.run(
task=netmiko_send_command,
command_string="show ap cdp neighbors"
)
print_result(results)
def save_config_to_file():
print("Saving config to file...")
results = nr.run(
task=netmiko_send_command,
command_string="show run"
)
for host in nr.inventory.hosts:
if results[host][0].failed:
print(f'Save run-config for {host} ({nr.inventory.hosts[host].hostname}) failed. See nornir.log for details.')
else:
now = datetime.datetime.now()
filename = f"{nr.inventory.hosts[host].hostname}-run-conf ({now.strftime('%Y-%m-%d %H:%M:%S')}).txt"
with open(filename, 'w') as f:
f.write(str(results[host][0]))
print(f"Config saved to {filename}")
# Text menu with 4 options that run each of the functions, or quit
while True:
print('\nYou are connected to these devices: ')
for host in nr.inventory.hosts:
print(f'-> {host}: {nr.inventory.hosts[host].hostname}')
print("Menu:")
print("1. Show AP summary")
print("2. Show client summary")
print("3. Show CDP neighbors")
print("4. Save run-config to file")
print("5. Quit")
choice = input("Enter choice: ")
if choice == "1":
show_ap_summary()
elif choice == "2":
show_client_summary()
elif choice == "3":
show_cdp_neighbors()
elif choice == "4":
save_config_to_file()
elif choice == "5":
break
else:
print("Invalid choice. Please choose again.")
python-nornir-extended-runbook.py

## Slide 107: In-depth: Grafana / TIG-stack
Grafana
This part of the Day 2 labs will focus on using Grafana, Telegraf and InfluxDB
The following lab exercises are included in this part
  Lab Exercise #30: Grafana – Syslog from WLC and APs

## Slide 108: Lab Exercise #30: Grafana - Syslog
We will use rsyslog that is usually enabled by default on our Ubuntu VM
  Check if rsyslog is installed and enabled
  (Conditional) If rsyslog is not installed, run these commands
Create a new config file for rsyslog
Then restart rsyslog with the new config
Grafana
# /etc/rsyslog.conf configuration file for rsyslog
#################
#### MODULES ####
#################
module(load="imuxsock") # provides support for local system logging
module(load="imudp") # provides UDP syslog reception
module(load="imtcp") # provides TCP syslog reception
module(load="imklog") # provides kernel logging support
# Provides UDP syslog reception
input(type="imudp" port="514")
# Provides TCP syslog reception
input(type="imtcp" port="514")
###########################
#### GLOBAL DIRECTIVES ####
###########################
$ActionFileDefaultTemplate RSYSLOG_TraditionalFileFormat
$RepeatedMsgReduction on
$FileOwner syslog
$FileGroup adm
$FileCreateMode 0640
$DirCreateMode 0755
$Umask 0022
$PrivDropToUser syslog
$PrivDropToGroup syslog
$WorkDirectory /var/spool/rsyslog
$ActionQueueType LinkedList
$ActionQueueFileName srvrfwd
$ActionResumeRetryCount -1
$ActionQueueSaveOnShutdown on
# Filter messages based on source IP
if $fromhost-ip startswith '192.168.10.' then {
*.* @@(o)127.0.0.1:6514;RSYSLOG_SyslogProtocol23Format
}
else {
stop
}
# Include all config files in /etc/rsyslog.d/
$IncludeConfig /etc/rsyslog.d/*.conf
devnet-adm@ubuntu-devnet:~$ sudo systemctl status rsyslog
● rsyslog.service - System Logging Service
Loaded: loaded (/usr/lib/systemd/system/rsyslog.service; enabled; preset: enabled)
Active: active (running) since Fri 2024-09-06 13:43:01 UTC; 3 days ago
TriggeredBy: ● syslog.socket
Docs: man:rsyslogd(8)
(...cut for brevity...)
devnet-adm@ubuntu-devnet:~$ sudo apt update && sudo apt install rsyslog
devnet-adm@ubuntu-devnet:~$ sudo systemctl start rsyslog
devnet-adm@ubuntu-devnet:~$ sudo mv /etc/rsyslog.conf /etc/rsyslog.conf.bak
devnet-adm@ubuntu-devnet:~$ sudo nano /etc/rsyslog.conf
# Paste the following lines to the file
devnet-adm@ubuntu-devnet:~$ sudo systemctl restart rsyslog
cli-playbook.yaml

## Slide 109: Lab Exercise #30: Grafana - Syslog
In this lab we will send syslog (including all config-commands) from our controller, and access-points to Grafana, and to do so we need to repeat a few tasks from day 1.
Log in to InfluxDB (http://192.168.10.x:8086)
Add a new bucket to InfluxDB and name it syslog
Grafana
Hint! Bucket-ID can be found in the bucket list

## Slide 110: Lab Exercise #30: Grafana - Syslog
Create a new token to be used with Grafana and Telegraf
  We will create a new telegraf docker so we will create new tokens
Grafana
Copy this token, and paste it in a lab30_notes.txt file

## Slide 111: Lab Exercise #30: Grafana - Syslog
We need to query this bucket using InfluxQL
  Same as we did at day.1
We need to access your InfluxDB instance, so find the container ID (see day 1 lab_notes)
  If your dockers are down, start them with: docker start telegraf influxdb grafana
Grafana
devnet-adm@ubuntu-devnet:~/tig-stack$ docker ps -a --filter name=influxdb
CONTAINER ID IMAGE COMMAND CREATED STATUS PORTS NAMES
71b07ba58958 influxdb:2.7.10 "/entrypoint.sh infl…" 2 minutes ago Up 2 minutes 0.0.0.0:8086->8086/tcp, :::8086->8086/tcp influxdb
devnet-adm@ubuntu-devnet:~/tig-stack$
  devnet-adm@ubuntu-devnet:~/tig-stack$ docker exec -it <your_container-id> bash
  root@71b07ba58958:/# influx v1 dbrp list
  Error: must specify org ID or org name
  root@71b07ba58958:/# influx v1 dbrp list --org-id <your_org-id> --token <your_admin_token>
  ID Database Bucket ID Retention Policy Default Organization ID
  VIRTUAL DBRP MAPPINGS (READ-ONLY)
  ----------------------------------
  ID Database Bucket ID Retention Policy Default Organization ID
  574c74f705d86be2 syslog 574c798323d86be2 autogen true 6a6f13e3a65de450
  root@71b07ba58958:/# influx v1 dbrp create --db syslog-db --rp syslog-rp --bucket-id 574c798323d86be2 --default --org-id <your_org-id> --token <your_admin_token>
  ID Database Bucket ID Retention Policy Default Organization ID
  0d9420b52628000 syslog-db bc926b463de1d39a syslog-rp true 6a6f13e3a65de450
  root@71b07ba58958:/# exit
  devnet-adm@ubuntu-devnet:~/tig-stack$
Insert YOUR container-id
Insert YOUR org-id
Insert YOUR admin token

## Slide 112: Lab Exercise #30: Grafana - Syslog
We need to make sure to change the docker-compose file.
  Telegraf needs to listen to the correct ports
    Add "6514:6514/tcp"
Bring the containers down, then up, to read the new docker-compose-yml
Grafana
telegraf:
container_name: telegraf
image: telegraf:1.32.0
restart: always
ports:
- "6514:6514/tcp"
- 57000:57000
devnet-adm@ubuntu-devnet:~$ cd ~/tig-stack/
devnet-adm@ubuntu-devnet:~/tig-stack$ nano docker-compose.yml
docker-compose.yml
devnet-adm@ubuntu-devnet:~/tig-stack$ docker compose down
[+] Running 4/4
✔ Container grafana Removed
✔ Container telegraf Removed
✔ Container influxdb Removed
✔ Network tig-stack_default Removed
devnet-adm@ubuntu-devnet:~/tig-stack$ docker compose up -d
[+] Running 4/4
✔ Container grafana Created
✔ Container telegraf Started
✔ Container influxdb Started
✔ Network tig-stack_default Started
devnet-adm@ubuntu-devnet:~/tig-stack$ docker ps | grep "telegraf"
73aafadd0c91 telegraf:1.32.0 "/entrypoint.sh tele…" 7 minutes ago Up 6 minutes 8092/udp, 0.0.0.0:6514->6514/tcp, :::6514->6514/tcp, 0.0.0.0:57000->57000/tcp, :::57000->57000/tcp, 8125/udp, 8094/tcp
Should show the new TCP port we are listening to

## Slide 113: Lab Exercise #30: Grafana - Syslog
We also need to edit the telegraf.conf file from day 1.
  We will update with a new input-plugin, syslog and a new output plugin so the syslog ends up in the same databases
We will use tags in the telegraf file to make sure the data ends up in the correct docker.
Paste in the follwing under output plugins and input plugins
Restart the telegraf docker
(Optional) make it more secure, by making a different token by Telegraf for each output
  We will use the standard admin token token for all RW in this deepdive.
Grafana
###############################################################################
# OUTPUT PLUGINS #
###############################################################################
# Output for Syslog data
[[outputs.influxdb_v2]]
urls = [ "http://influxdb:8086" ]
token = "${INFLUXDB_ADMIN_TOKEN}"
organization = "${INFLUXDB_ORG}"
bucket = "${INFLUXDB_BUCKET}"
bucket = "syslog-bucket"
tagexclude = ["c9800-bucket"]
[outputs.influxdb_v2.tagpass]
influxdb_database = ["syslog-bucket"]
[outputs.influxdb_v2.namedrop]
namedrop = ["Cisco-IOS-XE-wireless*"]
###############################################################################
# INPUT PLUGINS #
###############################################################################
# Syslog input configuration
[[inputs.syslog]]
## Specify the address to listen on
server = "tcp://0.0.0.0:6514" # Bind to all interfaces on port 6514 for TCP
## Alternatively, you can listen on UDP
# server = "udp://0.0.0.0:6514"
## Parse data from RFC5424 or RFC3164 format
best_effort = true
## Data format to extract metrics from syslog messages
data_format = "syslog"
[inputs.syslog.tags]
influxdb_database = "syslog-bucket"
devnet-adm@ubuntu-devnet:~$ cd ~/tig-stack/
devnet-adm@ubuntu-devnet:~/tig-stack$ nano telegraf/conf/telegraf.conf
telegraf.conf
devnet-adm@ubuntu-devnet:~$ docker restart telegraf

## Slide 114: Lab Exercise #30: Grafana - Syslog
Log into your lab_WLC and add the following config
  Change IP to your pod-WLC-IP
Create syslog of all configuration commands
Grafana
  9800CL-Proxmox(config)# conf t
  !
  9800CL-Proxmox(config)# logging host <your_Ubuntu_IP>
  !
  9800CL-Proxmox(config)# wireless client syslog-detailed
  !
  9800CL-Proxmox(config)# logging syslog-events informational
  !
  9800CL-Proxmox(config)# ap profile default-ap-profile
  9800CL-Proxmox(config-ap-profile)#syslog host <your_Ubuntu_IP>
  9800CL-Proxmox(config-ap-profile)#syslog level informational
  9800CL-Proxmox(config-ap-profile)#exit
  9800CL-Proxmox(config)#
  9800CL-Proxmox(config)# archive
  9800CL-Proxmox(config-archive)# log config
  9800CL-Proxmox(config-archive-log-cfg)# logging enable
  9800CL-Proxmox(config-archive-log-cfg)# logging size 200
  9800CL-Proxmox(config-archive-log-cfg)# notify syslog contenttype plaintext
  9800CL-Proxmox(config-archive-log-cfg)# end
  9800CL-Proxmox# wr

## Slide 115: Lab Exercise #30: Grafana - Syslog
Set a name for your database, f.ex syslog
Set Query language to InfluxQL
URL: http://influxdb:8086
Grafana
Add a new data source -> InfluxDB

## Slide 116: Lab Exercise #30: Grafana - Syslog
Use the token from your lab_10 notes (grafana RO token)
  Add a the custom HTTP Headers
    Header: Authorization
    Value: Token <API-TOKEN>
    There is a space between Token and <token>
Grafana
  Database: syslog-db
    User/Pass: devnet-adm / ChangeMe2024!​
    Value: Token <API-TOKEN>

## Slide 117: Lab Exercise #30: Grafana - Syslog
Import dashboard
Grafana
Import dashboard: 12433
Give it a name

## Slide 118: Lab Exercise #30: Grafana - Syslog
Grafana

## Slide 119: Lab Exercise #30: (Optional) Grafana – Syslog (row)
Grafana
We can move the syslog panels in a drop-down, row. Useful is you want multiple panels in your Grafana dashboard, and you want a hide a section.
Add a row from the top-menu
Change the Title by selecting gear icon.
  All panels below row will now be inside the row section

## Slide 120: Lab Exercise #30: Grafana - Syslog
Search for syslogs here
Grafana
All config-commands

## Slide 121: Lab Exercise #31: Grafana – C9800 data
Let us add some data from our 9800 WLC?
Lab Exercise #31: Grafana – C9800 data
Do not want to do this lab? You can download the syslog and 9800 Dashboard here:
You will need to change the datasource variable in GUI or in json, but quicker than lab 

## Slide 122: Lab Exercise #31: Grafana – C9800 data
Add the following telemetry data to your lab WLC
  The lab WLC have these configured already.
Lab Exercise #31: Grafana – C9800 data
telemetry ietf subscription 301
encoding encode-kvgpb
filter xpath /ios:native/version
stream yang-push
update-policy periodic 30000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
!
telemetry ietf subscription 302
encoding encode-kvgpb
filter xpath /platform-sw-ios-xe-oper:cisco-platform-software/platform-sw-ios-xe-oper:control-processes/platform-sw-ios-xe-oper:control-process/platform-sw-ios-xe-oper:per-core-stats
stream yang-push
update-policy periodic 5000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
!
telemetry ietf subscription 303
encoding encode-kvgpb
filter xpath /platform-sw-ios-xe-oper:cisco-platform-software/platform-sw-ios-xe-oper:control-processes/platform-sw-ios-xe-oper:control-process/platform-sw-ios-xe-oper:memory-stats
update-policy periodic 5000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
!
telemetry ietf subscription 304
encoding encode-kvgpb
filter xpath /device-hardware-xe-oper:device-hardware-data/device-hardware-xe-oper:device-hardware/device-hardware-xe-oper:device-system-data
update-policy periodic 10000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
telemetry ietf subscription 305
encoding encode-kvgpb
filter xpath /device-hardware-xe-oper:device-hardware-data/device-hardware-xe-oper:device-hardware/device-hardware-xe-oper:device-inventory
update-policy periodic 30000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
!
telemetry ietf subscription 306
encoding encode-kvgpb
filter xpath /wireless-ap-global-oper:ap-global-oper-data/wireless-ap-global-oper:ap-join-stats
stream yang-push
update-policy periodic 30000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
!
telemetry ietf subscription 307
encoding encode-kvgpb
filter xpath /wireless-ap-global-oper:ap-global-oper-data/wireless-ap-global-oper:wlan-client-stats
stream yang-push
update-policy periodic 5000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
!
!

## Slide 123: Lab Exercise #31: Grafana – C9800 data (CPU)
Use your Syslog Dasbhoard and create a new visualization
Select pie chart and name it:
  CPU 0: (Platform/Control/Service Plane)
Lab Exercise #31: Grafana – C9800 data

## Slide 124: Lab Exercise #31: Grafana – C9800 data (CPU)
Add the following query
Alternative you can paste in the query raw, but that you cannot og back to editor mode.
Lab Exercise #31: Grafana – C9800 data
SELECT mean("user") AS "User", mean("system") AS "System", mean("idle") AS "Idle" FROM "Cisco-IOS-XE-platform-software-oper:cisco-platform-software/control-processes/control-process/per-core-stats/per-core-stat" WHERE ("name"::tag = '0') AND $timeFilter GROUP BY time($__interval) fill(null)

## Slide 125: Lab Exercise #31: Grafana – C9800 data (CPU)
Change the following panel options
  Pie Chart Label: Value and name
  Tooltip is set to All
Lab Exercise #31: Grafana – C9800 data
  Legend: Table, Bottom, Value
  Standard Options: Percent

## Slide 126: Lab Exercise #31: Grafana – C9800 data (CPU)
Change the name::tag in the query to 1
Save and Apply
Duplicate the panel you just made
Edit the duplicated panel
Rename it to: CPU 1: (Data Plane)
Lab Exercise #31: Grafana – C9800 data

## Slide 127: Lab Exercise #31: Grafana – C9800 data (CPU)
Resize them to be a bit smaller and place them to the left.
  Seen these before? ;)
(Optional) These can also be made to a time-graph
  See the CPU spike I had for a few seconds
Lab Exercise #31: Grafana – C9800 data

## Slide 128: Lab Exercise #31: Grafana – C9800 data (Memory)
Add a new panel, this time Bar Gauge (or Pie Chart)
Give the panel a name
  Control Plane Memory
Lab Exercise #31: Grafana – C9800 data

## Slide 129: Lab Exercise #31: Grafana – C9800 data (Memory)
Add the following query
Alternative you can paste in the query raw, but that you cannot og back to editor mode.
Lab Exercise #31: Grafana – C9800 data
SELECT last("used_number") AS "Used", last("free_number") AS "Free" FROM "Cisco-IOS-XE-platform-software-oper:cisco-platform-software/control-processes/control-process/memory-stats" WHERE $timeFilter GROUP BY time($__interval) fill(null)

## Slide 130: Lab Exercise #31: Grafana – C9800 data (Memory)
Change some settings in the Bar Gauge panel options
  Selelect the Horizontal orientation (or vertical) whatever you prefer.
  Set Bar Size to Manual and change it to fit inside your panel.
  Place this panel below the CPU panel.
Lab Exercise #31: Grafana – C9800 data
Vertical orientation

## Slide 131: Lab Exercise #31: Grafana – C9800 data (Memory)
Add a new panel for Device Info.
Name the first panel «WLC Device Info»
Lab Exercise #31: Grafana – C9800 data

## Slide 132: Lab Exercise #31: Grafana – C9800 data (Memory)
Add the following queries
Select, format as Table.
Lab Exercise #31: Grafana – C9800 data

## Slide 133: Lab Exercise #31: Grafana – C9800 data (Memory)
Change the Value option to Last* and Fields to All Fields.
Change the Stat styles to Horizontal
Your panel should now look like this.
Lab Exercise #31: Grafana – C9800 data
On the next slide we will remove time variabel

## Slide 134: Lab Exercise #31: Grafana – C9800 data (Memory)
Add a transformation
Search for filter, and select «Filter fields by name»
Remove time
Lab Exercise #31: Grafana – C9800 data

## Slide 135: Lab Exercise #31: Grafana – C9800 data (Memory)
Add the panel next to the CPU panel, or wherever you like to place it 
Make the Control Plane Memory wider.
  When we add more device info variables, we can shrink it again, this is what makes Grafana so useful.
Lab Exercise #31: Grafana – C9800 data

## Slide 136: Lab Exercise #31: Grafana – C9800 data (reload, config)
Add a new panel for Last Reboot Reason and Unsaved Config.
  Select tabel panel.
Do not add any name for this panel.
Lab Exercise #31: Grafana – C9800 data

## Slide 137: Lab Exercise #31: Grafana – C9800 data (reload, config)
Add the following queries
Select, format as Table and remove Group By.
Lab Exercise #31: Grafana – C9800 data

## Slide 138: Lab Exercise #31: Grafana – C9800 data (reload, config)
Add a transformation
Search for filter, and select «Filter fields by name»
Remove time
Lab Exercise #31: Grafana – C9800 data

## Slide 139: Lab Exercise #31: Grafana – C9800 data (reload, config)
Change the Cell option to Colored Background
Grafana will select «false» as red, but false here is positive since the config is saved 
Change false to green and true to red.
  Add a two Value mappings
  False to green (config is saved)
  Ture to red (config is not saved)
  (Optional) change the display text
Lab Exercise #31: Grafana – C9800 data

## Slide 140: Lab Exercise #31: Grafana – C9800 data (reload, config)
Add this panel below like this
Lab Exercise #31: Grafana – C9800 data

## Slide 141: Lab Exercise #31: Grafana – C9800 data (AP Join Stats)
Add a new panel for Last Reboot Reason and Unsaved Config.
  Select tabel panel.
Name the panel AP Join Stats.
Lab Exercise #31: Grafana – C9800 data

## Slide 142: Lab Exercise #31: Grafana – C9800 data (AP Join Stats)
Add the following queries
Select, format as Table and Group by tag(ap_join_info/ap_name::field)
Lab Exercise #31: Grafana – C9800 data

## Slide 143: Lab Exercise #31: Grafana – C9800 data (AP Join Stats)
Add a one transformations
Search for filter, and select «Filter fields by name»
Remove time Time and ap_join-info/ap_name
Lab Exercise #31: Grafana – C9800 data

## Slide 144: Lab Exercise #31: Grafana – C9800 data (AP Join Stats)
Add a second transformations
Search for filter, and select «Group By»
  AP Name = Group By
  All others = Last
Lab Exercise #31: Grafana – C9800 data

## Slide 145: Lab Exercise #31: Grafana – C9800 data (AP Join Stats)
Enable Table Column filter
  Under table in panel options
Under Cell Options, select Colored Background
Under Standard Options, select Shades of color
  Select a color that you like 
(Optional) Make an override (at the bottom or top of panel) to change color of variables
  Filed with name (AP Name)
  Change color scheme
Lab Exercise #31: Grafana – C9800 data

## Slide 146: Lab Exercise #31: Grafana – C9800 data (AP Join Stats)
Add this panel to the right of all your other panels
Lab Exercise #31: Grafana – C9800 data

## Slide 147: Lab Exercise #31: Grafana – C9800 data (WLAN Stats)
Add a new panel for Last Reboot Reason and Unsaved Config.
  Select tabel panel.
Name the panel WLAN Stats
Lab Exercise #31: Grafana – C9800 data

## Slide 148: Lab Exercise #31: Grafana – C9800 data (WLAN Stats)
Add the following queries
Select, format as Table and Group by tag(wlan_profile_name::field)
Lab Exercise #31: Grafana – C9800 data

## Slide 149: Lab Exercise #31: Grafana – C9800 data (WLAN Stats)
Add a one transformations
Search for filter, and select «Filter fields by name»
Remove time Time and wlan_profile_name
Lab Exercise #31: Grafana – C9800 data

## Slide 150: Lab Exercise #31: Grafana – C9800 data (WLAN Stats)
Add a second transformations
Search for filter, and select «Group By»
  wlan_profile_name = Ignored
  wlan profile = Group by
  All others = Last*
Lab Exercise #31: Grafana – C9800 data

## Slide 151: Lab Exercise #31: Grafana – C9800 data (WLAN Stats)
Add this panel to the right of all your other panels
Lab Exercise #31: Grafana – C9800 data

## Slide 152: Lab Exercise #31: Grafana – C9800 data (WLAN Stats)
Add a new row
Give it a name like Cisco Catalyst 9800 General Info
  Move all your panels below this panel.
Lab Exercise #31: Grafana – C9800 data

## Slide 153: Want to make Grafana – Slack Bot alarms?
Ask Kjetil Teigen Hansen to give you a Demo and explanation 

## Slide 154: Meraki programmability
In this exercise we will explore some variants of Meraki programmability/automation
Postman: How to use the Meraki Postman API collection
Python: simple script
Meraki API?
Eksempler fra Automation Bootcamp for Meraki
git clone https://github.com/CiscoDevNet/abc-meraki
https://github.com/CiscoDevNet/abc-meraki/blob/main/solution/discovery-2/get_organization.py
Lab Exercise #60: Meraki programmability

## Slide 155: Obtaining API key
Your API key is generated under Organization -> Configure ->API & Webhooks
Then click "Generate API Key"
!!! Notice that the API key is bound to your user (email) and will have the same access as your user. So it is not for the specific Organization or Network, it is the key for your user !!!
Write down your API key in your password manager. If you lose it you will have to revoke it and create a new
You can get Read access to the organization that the Meraki router in this lab belong, so you can follow the examples. You can also do the same examples using your own organization of course :)
Lab Exercise #60: Meraki programmability

## Slide 156: Postman Meraki API Collection
There is a very nice Collection for Postman to use the Meraki Dashboard API
https://www.postman.com/meraki-api?tab=collections
Click the "Meraki Dashboard API - vv1.51.1" or whatever version is out when you do this exercise
Go to the "three dots menu" and choose "Export"
Choose "Collection v2.1" and "Export"
In Postman, create a new Workspace (or use an existing)
Lab Exercise #60: Meraki programmability

## Slide 157: Postman Meraki API Collection
You import the Meraki API Collection by just drag-drop'ing the JSON file you downloaded, into the "Collections" in Postman
Start by creating an Environment for your Meraki account. If you have multiple Meraki users, you can have an Environment for each of them. I will create an env for my user "meraki_lab@koksrud.no"
In that environment, create a variable with name "apiKey" and put YOUR token in "Current Value", then Save.
Reference: https://www.postman.com/meraki-api/cisco-meraki-s-public-workspace/overview
Lab Exercise #60: Meraki programmability

## Slide 158: Postman Meraki API Collection
You can now try out the "getOrganizations" API call
For further queries to that organization, you can save another environment variable with your organization ID
Lab Exercise #60: Meraki programmability

## Slide 159: Postman Meraki API Collection
After getting your Org ID, you can get the Networks
Save the network ID of your choice (if you have more than one) to an env variable "networkId" as well
With this, you can continue to run the other API calls included in the Collection
Lab Exercise #60: Meraki programmability

## Slide 160: Python - Use the Postman API
Try using one of the APIs from the Postman collection. In this example we will get the DHCP info from the firewall in this lab. For this request to work you will need to have gathered the serial number of the FW, and you need your API key
Then click the "code" button and select "Python - Requests" to get an example
Lab Exercise #60: Meraki programmability

## Slide 161: Python - Use the Postman API
Create a new folder "Lab60-Meraki-get-dhcp"
  Copy the "get-client-table.py" from Lab44 where we have a simple menu structure, and use a .env file. Rename it to "meraki-script.py"
  Create a .env file, and fill inn your values from the Postman part of the lab
Get the values from the .env file into variables
Modify the script to use some modified functions, and show some modified text
Here is an example of a "empty" script. All the functions are just printing the headline. Next we will write the RESTCONF calls to the Meraki cloud
Lab Exercise #60: Meraki programmability
apiKey='{YOUR TOKEN}'
orgId='{YOUR Org ID}'
networkId='{YOUR Network ID}'
serial='{YOUR DEVICE SERIAL}
.env
from dotenv import dotenv_values
# Import variables from the .env file
env = dotenv_values('.env')
apiKey = env['apiKey']
organizationId=env['organizationId']
networkId=env['networkId']
serial=env['serial']
# Define functions
def show_device_summary():
print('Device summary:\n-------------------------------------')
def show_client_summary():
print('Client summary:\n-------------------------------------')
def show_cdp_neighbors():
print(f"CDP neighbors for device {serial}:\n-------------------------------------")
def get_device_dhcp_subnets():
print(f"DHCP subnets for device {serial}:\n-------------------------------------")
# Text menu with 4 options that run each of the functions, or quit
while True:
print(f'\nYou are connected to organization {organizationId} and network {networkId}')
print("Menu:")
print("1. Show Device summary")
print("2. Show client summary")
print("3. Show CDP neighbors")
print("4. Show DHCP subnets")
print("5. Quit")
choice = input("Enter choice: ")
if choice == "1":
show_device_summary()
elif choice == "2":
show_client_summary()
elif choice == "3":
show_cdp_neighbors()
elif choice == "4":
get_device_dhcp_subnets()
elif choice == "5":
break
else:
print("Invalid choice. Please choose again.")
meraki-script.py

## Slide 162: Python - Use the Postman API
Merge the code snippet from Postman into the function show_device_dhcp_subnets()
  Import the requests package
  Write the rest into the get_device_dhcp_subnets() function
  We change the url with an f-string and put in the variable "serial" from the .env file instead
  Instead of the Authorization in the Postman example, we use the key "X-Cisco-Meraki-API-Key" and use apiKey from the .env file as the value
Lab Exercise #60: Meraki programmability
Postman:

## Slide 163: Python - Use the Postman API
Do the same for show_device_summary() Use getOrganizationDevices from Postman Change the OrgId from Postman with {organizationId} from .env
Do the same for show_client_summary() Use getNetworkClients from Postman Change the Network ID from Postman with {networkId} from .env
Do the same for show_cdp_neighbors() Use getDeviceLldpCdp from Postman Change the S/N from Postman with {serial} from .env
Lab Exercise #60: Meraki programmability

## Slide 164: Python - Use the Postman API
Some suggestions for next steps could be
  Print the JSON output more pretty, you can use pretty-print (from pprint import pprint)
  Save the JSON to a JSON file (use the method from Lab 40/44 where you saved run-config)
  Flatten the JSON output to a pandas dataframe and save to CSV or Excel (From Lab 41)
Lab Exercise #60: Meraki programmability

## Slide 165: In-depth: MIST programmability
MIST programmability document
MIST

## Slide 166: In-depth: Aruba programmability
Aruba API?
Meraki