## Slide 1: Wi-Fi automation lab Lab Guide - Day 1
Andreas Koksrud / Telenor Bedrift
Co-authors:
Kjetil Teigen Hansen & François Vergès

## Slide 2: References / inspiration
https://github.com/CiscoDevNet/yangsuite/
https://postman.com
https://docs.ansible.com/ansible/latest/collections/cisco/ios/ios_facts_module.html
https://www.wifireference.com/2020/01/14/viewing-network-telemetry-from-the-catalyst-9800-with-grafana/
https://grafana.com/grafana/dashboards/13462-device-health-monitoring/
https://grafana.com/grafana/dashboards/12468-catalyst-9800-client-stats/
https://wirelessisfun.wordpress.com/2020/12/10/network-telemetry-data-and-grafana-part-1-the-advanced-netconf-explorer/
https://python.org
https://codeium.com
References

## Slide 3: Copyright
© Andreas Koksrud 2025. All rights reserved. This presentation is provided for educational and informational purposes only. You may distribute and learn from this presentation, but commercial use or any form of monetization is strictly prohibited without prior written consent
Any slides marked Kjetil Teigen Hansen or the Conscia logo will also have full or co-ownership by Kjetil
Any slides marked François Vergès or the SemFio logo will also have full or co-ownership by François
Copyright

## Slide 4: Prerequisites
Cisco Meraki account (https://dashboard.meraki.com)
Juniper MIST account (https://manage.mist.com)
Postman account (https://postman.com)
Complete the pre-lab exercises before the deep dive labs
Bring an Ethernet dongle if you don't have built-in port
(optional) Bring an extra screen to show lab guide (or prepare to Alt-Tab)
Prerequisites

## Slide 5: Communications
WebEx space: Wi-Fi automation lab
Please help each other
Sharing is caring 
Communications

## Slide 6: Agenda
Pre-lab
Choose your hypervisor
Install Ubuntu Server w/Docker
Install Postman
Install VS Code
Day 1
Day 2
In-depth explore a topic of choice
Sort out pre-lab task problems
Grafana / TIG-stack
Grafana Cloud
Ansible
Python
Cloud vendor automation (MIST or Meraki)
Get to know the lab environment
Connect VS Code to Ubuntu
Install and explore Ansible
Explore Python automation
Install and explore YANG Suite
Explore Postman
Install and explore Grafana
(optional) install 9800-CL
Agenda

## Slide 7: Scope
In scope
  Getting started with various systems/languages/solutions for lab purposes
  Set up your own Ubuntu Linux server on your own laptop. It will be possible to use a shared server if you do not want or have possibility to install an Ubuntu VM on your laptop
  Some nice examples to try various aspects of automation
  Inspiring you to explore deeper on your own
Out of scope topics
  Git
  Learning the languages (Ansible, Python, InfluxQL, etc)
  Learning Linux
  Deploying the systems for production use
  Troubleshooting WLC/AP connection
Scope

## Slide 8
Lab topology
Each student have an assigned Pod number. When using static IP, their Ubuntu Server should have the same last octet as the Pod#
2 students share a preconfigured WLC, as assigned in the topology map
Everyone is connected to VLAN 10
All switchports on all switches are trunk ports with VLAN 10 as native, and allowed vlan as VLAN 10 and 11
For Wi-Fi clients on your SSIDs you can use VLAN 11 to not fill up VLAN 10

## Slide 9: Notes for Mac users - TextEdit
TextEdit (the default text editor on OS X) use rich text formatting by default. This is not a great idea when copy-pasting stuff to the command line, so there is a couple of things you must keep in mind
  If you want, you can change a setting in TextEdit to make all new documents plain text
  To change the current document to plain text go to Format -> Make Plain Text
  Shortcut is: Shift-Cmd-T
Notes for Mac users

## Slide 10: Notes for WSL users (alternative, untested yet)
You can use WSL (Windows Subsystem for Linux) instead of a Ubuntu VM running in a hypervisor, for Python and Ansible stuff
TIG stack and other docker stuff is not tested (yet)
No instructions for using WSL or adopting the lab guide to WSL is included at this moment
Install WSL (start Powershell as administrator)
Check WSL version
Upgrade WSL
Install Ubuntu, run "wsl --install -d Ubuntu
List installed WSL VMs, run "wsl --list"
Notes for WSL users
  PS C:\> wsl --install
Fix network connectivity (from Powershell. Restart WSL)
You might have to create some FW-openings and/or do some port forwarding to get the external devices (like the 9800 WLC) to communicate into your WSL Telegraf etc
  PS C:\> wsl --version
  WSL version: 2.3.24.0
  (... if this command is not showing version, you must upgrade)
  PS C:\> wsl --update
  PS C:\> wsl --install -d Ubuntu
  PS C:\> wsl --list
  PS C:\> echo '[wsl2]' > ~\.wslconfig
  PS C:\> echo 'networkingMode=mirrored' >> ~\.wslconfig

## Slide 11: Building your own lab
Based on feedback from running this deep dive on previous events, if you are going to build and troubleshoot the full lab setup, it will take most or all of the time (2x 3h)
The deep dive itself will have pre-built and pre-configured+tested WLAN Controllers (1 WLC per 2-4 students) for you to use. If you want to install your own WLC by following the optional part of this pre-lab guide that is OK, but we strongly encourage you to use the deep dive time to do actual automation exercises and not troubleshooting your WLC
There will also be pre-built Ubuntu servers to use, running on our servers, for those who want to use that instead of their own laptop.
If you have a mini computer or an old laptop to spare, you could install Proxmox on that and use for your VMs. Unfortunately it is outside the scope of this deep dive and this pre-lab guide to give detailed instructions on the Proxmox installation itself, outside what is described in task 1d. It is also outside the scope of the deep dive to help troubleshoot your Proxmox. But our servers run on that, so we are somewhat familiar with it and might answer some simple questions 
We will also provide pre-built images with a finished installation of Ubuntu Server for Hyper-V and Virtualbox
We encourage you to install your own Ubuntu Server, since it will give you more experience building the items yourself when you get home or need it in some other situation.
Building your own lab

## Slide 12: Tentative schedule for day 1
Hour 1
  Introductions and getting started
  Finish the pre-lab tasks
  Get to know the lab environment
  Install and explore Ansible
Hour 2
  Explore Python automation
  Explore YANG models
  Explore Postman
Hour 3
  Install and explore TIG-stack / Grafana
Tentative schedule

## Slide 13: Lab exercise #0: Finish the pre-lab tasks
Get help to whatever you did not finish
There will probably (always) be some cases which falls outside what is tested
Lab exercise #0: Finish the pre-lab tasks

## Slide 14: Lab exercise #1: Connect your laptop and Ubuntu
Connect your laptop to the wired network
  Ensure you get DHCP in the range 192.168.10.71-250 /24
  Ensure you get internet access through the wired connection
Boot up your Ubuntu VM
  If using Multipass - Check that the bridged network is correct. Choose your USB dongle or ethernet port etc
  Follow the next slide to change it to static IP
Lab exercise #2: Configure the AP
  akoksrud:MacOS ~$ multipass networks
  Name Type Description
  en0 wifi Wi-Fi
  en4 ethernet Ethernet Adapter (en4)
  en5 ethernet Ethernet Adapter (en5)
  en8 usb USB 10/100/1000 LAN
  akoksrud:MacOS ~$ multipass set local.bridged-network=en8
  akoksrud:MacOS ~$ multipass restart ubuntu-devnet

## Slide 15
Change from DHCP to static IP - MULTIPASS only
network:
version: 2
ethernets:
default:
match:
macaddress: "52:54:00:cb:dc:82"
dhcp-identifier: "mac"
dhcp4: true
extra0:
match:
macaddress: "52:54:00:8f:54:67"
optional: true
dhcp-identifier: "mac"
dhcp4: true
dhcp4-overrides:
route-metric: 200
It looks like this (ish):
Pre-lab task #2: Ubuntu Server
If you are using Multipass, it creates two network adapters. Please follow this guide if you are using Multipass. If NOT using multipass, follow the next slide
This will show one method to permanently change the IP of your server
  Copy the netplan config file to a new file (remember sudo here)
  Delete the auto-created /etc/netplan/50-cloud-init.yaml
  Run "sudo netplan apply" to use the new config file
  Check that you have the new IP
  Reboot the server and you're good to go 
devnet-adm@ubuntu-devnet:~$ sudo netplan apply
network:
version: 2
ethernets:
default:
match:
macaddress: "52:54:00:cb:dc:82"
dhcp-identifier: "mac"
dhcp4: true
extra0:
match:
macaddress: "52:54:00:8f:54:67"
dhcp4: false
addresses:
- 192.168.10.{YOUR_POD_IP}/24
routes:
- to: default
via: 192.168.10.1
nameservers:
addresses:
- 1.1.1.1
  ~$ sudo cp /etc/netplan/50-cloud-init.yaml /etc/netplan/99_config.yaml
~$ sudo nano /etc/netplan/99_config.yaml
~$ sudo chmod 600 /etc/netplan/99_config.yaml
devnet-adm@ubuntu-devnet:~$ sudo rm /etc/netplan/50-cloud-init.yaml
devnet-adm@ubuntu-devnet:~$ sudo netplan status
devnet-adm@ubuntu-devnet:~$ sudo reboot now
Change to YOUR Ubuntu IP
Change the "extra0" part

## Slide 16
Change from DHCP to static IP
network:
ethernets:
ens18:
# dhcp4: true
dhcp6: false
dhcp4: false
addresses:
- 192.168.10.{YOUR_POD_IP}/24
routes:
- to: default
via: 192.168.10.1
nameservers:
addresses:
- 1.1.1.1
/etc/netplan/99_config.yaml
Pre-lab task #2: Ubuntu Server
When you come to WLPC you would need to use a static IP in the lab range. Before WLPC you might just keep the server in DHCP mode, and come back to this slide during the deep dive.
This will show one method to permanently change the IP of your server
  Check your adapter name
  Create a new file /etc/netplan/99_config.yaml
  Delete the auto-created /etc/netplan/50-cloud-init.yaml
  Run "sudo netplan apply" to use the new config file
  Check that you have the new IP
  Reboot the server and you're good to go 
To easily change between static and DHCP, I just comment/uncomment the lines. To change this to DHCP, just unncomment the "dhcp4: true" line, and comment the rest
Get this value from "netplan status". Enter it into 99_config.yaml
Probable values: - Proxmox: ens18 - Hyper-V: eth0 - VirtualBox: enp0s3
devnet-adm@ubuntu-devnet:~$ sudo netplan apply
!!! In YAML, indentation is REALLY important !!!
In this file I use 2, 4, 6 or 8 spaces (multiple of 2). It would be valid to use multiple of 3 or 4 instead.
  devnet-adm@ubuntu-devnet:~$ netplan status | grep network
  2: ens18 ethernet UP (networkd: ens18)
  devnet-adm@ubuntu-devnet:~$ sudo nano /etc/netplan/99_config.yaml
devnet-adm@ubuntu-devnet:~$ sudo chmod 600 /etc/netplan/99_config.yaml
devnet-adm@ubuntu-devnet:~$ sudo rm /etc/netplan/50-cloud-init.yaml
devnet-adm@ubuntu-devnet:~$ sudo netplan status
devnet-adm@ubuntu-devnet:~$ sudo reboot now
Most Common errors:
Wrong file permissions (step 2)
Errors in the indentation in the YAML file
Change to YOUR Ubuntu IP

## Slide 17: Lab exercise #2: Test the lab environment
Access from your computer to the devices
  SSH to one or more of the shared Ubuntu servers (192.168.10.11 up to .18)
  SSH and HTTPS to your designated WLC (192.168.10.51, 53, 55, etc) shared with 3 other students
  You have admin access to all shared devices, please don't mess up for each other 
Access from your Ubuntu Server to the devices
  Ping from your Ubuntu VM to your designated WLC
  Ping from your Ubuntu VM to the Internet
Access in to your Ubuntu Server
  Ping from your designated WLC to your Ubuntu VM
Lab exercise #1: Get to know the lab environment

## Slide 18: Lab exercise #3: Explore VS Code
We will now use our VS Code installation to open a directory on the Ubuntu server
Instructions will follow to
  Open the "Remote-SSH" extension
  Create new host
  Connect current window to remote host
  Install local extensions in remote host
  Open a remote folder as workspace
  Open some example files from the downloaded GIT repository
Lab exercise #3: Explore VS Code

## Slide 19: VS Code - Connect to... Remote SSH
Command Palette (F1)
  Type "remote-ssh", select "Add New SSH Host...", type "devnet-adm@192.168.10.7"
Connect to the new Host, either using lower left corner of VS Code window or Command Palette (F1)
When asked about platform type, select Linux
Lab exercise #3: Explore VS Code
Replace with your Ubuntu IP

## Slide 20: VS Code - Install Extensions in Remote SSH
The extensions have to be installed in each remote environment
Lab exercise #3: Explore VS Code
When asked which ones to install, you can select everything, or select some of them if you have a lot of extensions
It will take a minute or so to install the extensions in the server

## Slide 21: VS Code
Open Folder
Trust authors
Lab exercise #3: Explore VS Code

## Slide 22
Using Explorer in VS Code, open the example file python-hello-world.py
Detected language for active file
(can be manually overridden)
Active Python environment
for active file. Press here, and
for now select one of the options,
like /bin/python3
Lab exercise #3: Explore VS Code

## Slide 23
If you open the Ansible file ansible-first-playbook.yml some errors will show. We will fix this later in the lab, after installing Ansible
Lab exercise #3: Explore VS Code

## Slide 24: Terminal in VS Code
VS Code has an integrated terminal you can use. In many cases this is a convenient way to SSH to your server when working on projects in VS Code
Select "Terminal" and "New Terminal" You can also use the shortcut (sorry again for the stupid Norwegian characters )
The code window will split, and you will have a terminal in the lower half (I usually use a larger window than in this screenshot, it's just resized to show it all on the same screenshot
Lab exercise #3: Explore VS Code

## Slide 25: Lab exercise #4: Install Ansible
In this exercise, we will
  Create a Python virtual environment to use for Ansible stuff
  Install Ansible on the Ubuntu Server
  Configure VS Code to use Ansible on the remote server
The first couple of slides will explain briefly about Ansible (for your reference)
Then the installation process is explained step by step, before re-opening the first playbook example
Lab exercise #4: Install Ansible

## Slide 26: What is Ansible
Automation using "playbooks" written in YAML format
Agent-less architecture
  No installation on the managed nodes
Idempotency
  Does not change/write if target is already in state described by playbook
Control node
  System where Ansible is installed and runs the playbooks
Inventory
  List of managed nodes where the playbook will affect
Managed nodes
  Remote systems that are the targets of your playbooks
Lab exercise #4: Install Ansible

## Slide 27: Plugins and modules
Plugins
  Extends the core functionality of Ansible
  Examples
    cisco.ios.ios cliconf - To run CLI commands on Cisco IOS device
    Become plugins, how to get write access on various systems ("sudo", "enable" etc)
    Connection plugins, like SSH
Modules
  Built-in or custom code snippets to perform various tasks
  A special type of plugin
  Examples
    cisco.ios.ios_config
    cisco.ise.endpoint
Lab exercise #4: Install Ansible

## Slide 28: Ansible installation
Installing in a Python VENV (Virtual Environment)
(optional info) Ansible could be installed globally. But by using VENV we can control the environment more closely. Most projects will have some dependencies, and by controlling the environment you ensure that the packages in the environment are ones that is tested to be compatible with the project. Here we just use the latest, but it is shared to list ("freeze") the currently installed packages and versions from an environment when tested OK, and use this as a requirements input when reproducing the environment
Lab exercise #4: Install Ansible
  devnet-adm@ubuntu-devnet:~$ sudo apt install pip python3-venv
  devnet-adm@ubuntu-devnet:~$ mkdir ~/automation-venv
  devnet-adm@ubuntu-devnet:~$ python3 -m venv ~/automation-venv/
  devnet-adm@ubuntu-devnet:~$ source ~/automation-venv/bin/activate
  (automation-venv) devnet-adm@ubuntu-devnet:~$ pip install ansible ansible-lint
  (automation-venv) devnet-adm@ubuntu-devnet:~$ ansible --version
  ansible [core 2.17.1]
  config file = None
  configured module search path = ['/home/devnet-adm/.ansible/plugins/modules', '/usr/share/ansible/plugins/modules']
  ansible python module location = /home/devnet-adm/automation-venv/lib/python3.12/site-packages/ansible
  ansible collection location = /home/devnet-adm/.ansible/collections:/usr/share/ansible/collections
  executable location = /home/devnet-adm/automation-venv/bin/ansible
  python version = 3.12.3 (main, Apr 10 2024, 05:33:47) [GCC 13.2.0] (/home/devnet-adm/automation-venv/bin/python3)
  jinja version = 3.1.4
  libyaml = True
  (automation-venv) devnet-adm@ubuntu-devnet:~$

## Slide 29: Ansible Collections
Lab exercise #4: Install Ansible
A collection is a premade collection of playbooks, roles, modules and plugins, usually for a specific purpose or type of devices
  https://docs.ansible.com/ansible/latest/collections/index.html#list-of-collections
This is how to look up which collections you have installed in your environment

## Slide 30: Ansible Collections
Navigating the documentation
https://docs.ansible.com/ansible/latest/collections/index.html#list-of-collections
Lab exercise #4: Install Ansible

## Slide 31: VS Code - Python environment for Ansible
Check which Python environment is used by Ansible
Select python environment (VS Code, bottom line)
Select «Enter interpreter path...»
Enter the python environment that Ansible use, into this line and press Enter
Bottom line should now show the Ansible version (2.18.1) and Python version and venv
  devnet-adm@ubuntu-devnet:~$ source ~/automation-venv/bin/activate
  (automation-venv) devnet-adm@ubuntu-devnet:~$ ansible --version | grep "python version"
  python version = 3.12.3 (main, Apr 10 2024, 05:33:47) [GCC 13.2.0] (/home/devnet-adm/automation-venv/bin/python3)
Lab exercise #4: Install Ansible
/home/devnet-adm/automation-venv/bin/python3
!! Common mistake: !!
Do not type here…
Press here.
Then type here…

## Slide 32: VS Code - Choose file type
If not auto detected, file type can be changed for open files
Pro tip: If the file name contains the word «playbook», it will automatically be recognized as Ansible by VS Code (and not general YAML)
  interface-playbook.yaml
  demo-playbook.yaml
There are also other ways to get VS Code to auto recognize playbooks, like putting them in a "playbooks" subfolder
Lab exercise #4: Install Ansible

## Slide 33: Ansible-lint
Linting (syntax checking) is done on file save
The «ansible-first-playbook.yml» should have an error that shows on first save, when ansible-lint runs in the background
Try to fix this yourself 
(optional info) You can also specify ansible-lint to exclude certain errors, like the "line too long" error.
  Open Settings (Ctrl-,) and search for "ansible-lint" Enter -x yaml[line-length]
Lab exercise #4: Install Ansible

## Slide 34: Lab exercise #5: Explore Ansible
In this lab, you will be given a simple example to get you started with Ansible
The Ansible section of Day2 will include more exercises for you to do, including example solutions
Lab exercise #5: Explore Ansible

## Slide 35: Gather facts
Create a folder
Shows up automatically in VS Code
Create files and folders in VS Code, right click to get menu
Create the file "gather_facts-playbook.yml"
Copy-paste from this textbox to VS Code
Lab exercise #5: Explore Ansible
---
- name: IOS Facts
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: Gather all legacy facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Show facts
ansible.builtin.debug:
msg: "{{ facts1 }}"
gather_facts-playbook.yml
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation$ mkdir Lab5_Ansible-gather_facts

## Slide 36: Ansible hosts file
Let’s create a file named hosts.yml
It shows up in the folder as well
Lab exercise #5: Explore Ansible
wlc:
hosts:
192.168.10.{WLC-IP}:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2025!
ansible_password: ChangeMe2025!
ansible_user: devnet-adm
hosts.yml
Change to YOUR
WLC IP

## Slide 37: Fix dependencies
Try to run the playbook with the following command. Something is missing.
Lab exercise #5: Explore Ansible
  (automation-venv) devnet-adm@ubuntu-devnet:~$ pip install ansible-pylibssh
  Collecting ansible-pylibssh
  Downloading ansible_pylibssh-1.2.2-cp312-cp312-manylinux_2_28_x86_64.whl.metadata (36 kB)
  Downloading ansible_pylibssh-1.2.2-cp312-cp312-manylinux_2_28_x86_64.whl (2.9 MB)
  ━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━ 2.9/2.9 MB 7.1 MB/s eta 0:00:00
  Installing collected packages: ansible-pylibssh
  Successfully installed ansible-pylibssh-1.2.2
  (automation-venv) devnet-adm@ubuntu-devnet:~$
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab5_Ansible-gather_facts$ ansible-playbook -i hosts.yml gather_facts-playbook.yml
  PLAY [IOS Facts] ***************************************************************************************************************************************
  TASK [Gather all legacy facts] *************************************************************************************************************************
  [WARNING]: ansible-pylibssh not installed, falling back to paramiko
  fatal: [192.168.10.30]: FAILED! => {"changed": false, "msg": "paramiko is not installed: No module named 'paramiko'"}
  PLAY RECAP *********************************************************************************************************************************************
  192.168.10.30 : ok=0 changed=0 unreachable=0 failed=1 skipped=0 rescued=0 ignored=0
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab5_Ansible-gather_facts$
Let's install "ansible-pylibssh"
  First, make sure you are in your automation-venv
  If it is not showing (automation-venv) at the start of the line, enter source ~/automation-venv/bin/activate
  Then install the package in your venv by using "pip install {package name}

## Slide 38: SSH host key checking
Try running again. The SSH connection is failing
Update the hosts.yml file
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab5_Ansible-gather_facts$ ansible-playbook -i hosts.yml gather_facts-playbook.yml
  PLAY [IOS Facts] ***************************************************************************************************************************************
  TASK [Gather all legacy facts] *************************************************************************************************************************
  fatal: [192.168.10.30]: FAILED! => {"changed": false, "msg": "\nlibssh: The authenticity of host '192.168.10.30' can't be established due to 'Host is unknown: 41:86:3e:e4:fb:9f:de:06:5b:72:f3:ce:75:f1:da:ad:e7:a5:13:c0'.\nThe ssh-rsa key fingerprint is SHA1:QYY+5Puf3gZbcvPOdfHareelE8A."}
  PLAY RECAP *********************************************************************************************************************************************
  192.168.10.30 : ok=0 changed=0 unreachable=0 failed=1 skipped=0 rescued=0 ignored=0
Lab exercise #5: Explore Ansible
hosts.yml
wlc:
hosts:
192.168.10.{WLC-IP}:
vars:
ansible_connection: network_cli
ansible_network_os: ios
ansible_ssh_pass: ChangeMe2025!
ansible_password: ChangeMe2025!
ansible_user: devnet-adm
ansible_host_key_checking: False
Change to YOUR
WLC IP

## Slide 39: Gather facts
Successful play
Lab exercise #5: Explore Ansible

## Slide 40: Use parts of return values
The returned facts1 is a dictionary
  You can use dot notation
  Edit the "Show facts" task, to show only some subset of the info
Lab exercise #5: Explore Ansible
- name: Show facts
debug:
msg: "{{ facts1.ansible_facts.ansible_net_interfaces }}"

## Slide 41: Use return values
We will use the returned facts, to write the run-config to a file
Remove the "Show facts" task, and replace it with a new task
Lab exercise #5: Explore Ansible
gather_facts-playbook.yml
---
- name: IOS Facts
hosts: wlc
connection: network_cli
gather_facts: no
tasks:
- name: Gather all legacy facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Write run-config to file
ansible.builtin.copy:
content: "{{ facts1.ansible_facts.ansible_net_config }}"
dest: "{{ './' + facts1.ansible_facts.ansible_net_hostname + '-run-conf.txt' }}"
Using the "copy" module
Content is using parts of the return values, this time we use "ansible_net_config"
Dest is where to write the content. Here are some simple examples on Jinja syntax
(optional info)
Jinja2 is integrated in Ansible and widely used
"Everything inside double curly brackets" = Jinja2

## Slide 42: Linting errors, and fixing them
When saving this file you should get two linting errors
Lab exercise #5: Explore Ansible
gather_facts-playbook.yml
---
- name: IOS Facts
hosts: wlc
connection: network_cli
gather_facts: false
tasks:
- name: Gather all legacy facts
cisco.ios.ios_facts:
gather_subset: all
register: facts1
- name: Write run-config to file
ansible.builtin.copy:
content: "{{ facts1.ansible_facts.ansible_net_config }}"
dest: "{{ './' + facts1.ansible_facts.ansible_net_hostname + '-run-conf.txt' }}"
mode: "0600"
When writing files (like using the "copy" module), you should always explicitly specify the file permissions
We add the line: mode: "0600"
We fix this with using "false" instead of "no"
Both will work, but correct YAML syntax is "false"

## Slide 43: Run the playbook
List the files, and you can see the file that was created
You can view the file contents in the Linux terminal by running "cat", "more", "nano" or similar
You will also see the file in VS Code explorer and can open it from there
Lab exercise #5: Explore Ansible

## Slide 44: Lab exercise #6: Explore YANG models
First there will be a couple of slides to explain what YANG models are
Then you will explore some of the YANG models of the 9800 WLAN Controller by using the https://yangcatalog.org website
Lab 7 will explore YANG models using another tool (YANG Suite)
Some of the later labs will have optional parts where you can look up RESTCONF paths that you need using one of these tools
Lab exercise #6: Explore YANG models

## Slide 45: What is a YANG-model?
Structured representation of cfg og oper data
Used primarily with NETCONF & RESTCONF
Do you recognize what the tree is showing?
Reference/download: https://github.com/YangModels/yang/tree/main/vendor/cisco/xe/1751
Lab exercise #6: Explore YANG models

## Slide 46: yangcatalog
Open the following website: https://www.yangcatalog.org/
Select "Module Detail Viewer"
Here you can start typing parts of available YANG modules. Start by typing "IOS-XE-wireless". It is not case sensitive by the way
Select the AP oper module "Cisco-IOS-XE-wireless-access-point-oper" and click "Get details"
Then click "Tree View"
Lab exercise #6: Explore YANG models

## Slide 47: YANG Catalog - Navigating the Tree View
Expand/collapse all nodes
Expand/collapse this branch
This is a container/list node
  Contains other nodes
Hover the mouse over an element name to get the description popup
This is a leaf node
  Contains a single value
!! There are lots of info to the right of this screenshot. Sometimes the horizontal scroll bar is trying to hide, scroll down to the bottom to find it !!
Lab exercise #6: Explore YANG models

## Slide 48: Using values from YANG Catalog
Lab exercise #6: Explore YANG models
Use this for WLC telemetry config
Use this for RESTCONF path
no telemetry ietf subscription 4
telemetry ietf subscription 4
encoding encode-kvgpb
filter xpath /wireless-access-point-oper:access-point-oper-data/wireless-access-point-oper:radio-oper-data
stream yang-push
update-policy periodic 500
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
do show telemetry ietf subscription 4
When navigating the tree view, here is where you find the values you will typically use, with examples
  "Path": Used when configuring 9800 to send values as streaming telemetry. We will use this in lab 10 & 11 to configure WLC to send specific data to be visualized in Grafana
  "Sensor Path": Used when you need a RESTCONF path. We will use this in the labs 8 (Postman), 9 (Python) and in many of the Day 2 labs (both Python and Ansible labs)

## Slide 49: yangcatalog
You can also get the tree view in a text form like this
Go to YANG Module Detail Viewer again, Search and find your module, and select "Get details"
A way down in the details table you will find "yang-tree", click the link there
The tree will open in a separate page
Lab exercise #6: Explore YANG models

## Slide 50: Lab exercise #7: Explore YANG Suite
Lab exercise #7: Explore YANG Suite
YANG Suite is an installable tool that can be used to pull supported YANG models directly from the actual devices
You can also use it to test communication to your device using RESTCONF and more

## Slide 51: Lab exercise #7: Explore YANG Suite
!!! NOTE !!! You will explore YANG Suite using one of the servers where it is pre-installed. The installation has some bindings to the IP of the server, so it should be installed when you have the permanent static IP of your server
If you want to install it on your own VM, the instructions are included in the optional Lab Exercise #12, beware that it will take a little while so you might want to do it later instead of during the deep dive
In the pre-installed servers, YANG models will already be pulled from one of the pre-installed WLCs
To get an even distribution, you can spread so that if you have the following WLC, use the following Ubuntu Servers to explore YANG Suite:
If YANG-Suite is not running on any of those machines, start it with the following commands
Lab exercise #7: Explore YANG Suite
Shared WLC | Shared Ubuntu Server | YANG Suite URL
wlc51 (192.168.10.51) | ubuntu11 (192.168.10.11) | https://192.168.10.11:8443
wlc53 (192.168.10.53) | ubuntu12 (192.168.10.12) | https://192.168.10.12:8443
wlc55 (192.168.10.55) | ubuntu13 (192.168.10.13) | https://192.168.10.13:8443
wlc57 (192.168.10.57) | ubuntu14 (192.168.10.14) | https://192.168.10.14:8443
wlc59 (192.168.10.59) | ubuntu15 (192.168.10.15) | https://192.168.10.15:8443
wlc61 (192.168.10.61) | ubuntu16 (192.168.10.16) | https://192.168.10.16:8443
devnet-adm@ubuntu-devnet:~$ cd ~/yangsuite/docker
devnet-adm@ubuntu-devnet:~$ docker compose up -d

## Slide 52: YANG Suite
Log in to a YANG Suite (URL on previous slide)
Go to Explore -> YANG -> Select a YANG. Select a YANG model and click the "Load module(s)" button
«oper» -> Operational data
«cfg» -> Configuration and config data
Lab exercise #7: Explore YANG Suite

## Slide 53: Lab exercise #7: Explore YANG Suite
Explore YANG Models
Lab exercise #7: Explore YANG Suite
This is the info you typically use to craft RESTCONF calls (Postman, Python, Ansible, etc) or streaming telemetry subscriptions (from WLC)

## Slide 54: Lab exercise #7: Explore YANG Suite
Over the next pages is examples on a couple more YANG models you can check out
  Get AP summary
  Get Clients
Just get somewhat familiar, you will use these in the next lab exercises (Postman, Python, Ansible, Grafana)
This will show you the model, not pull the actual data
To pull data we will use these models i Postman and Grafana later
(optional) You can also do RESTCONF and NETCONF calls to the device from YANG Suite
  Protocols -> RESTCONF -> Find your module -> Generate API(s) -> Authorize -> Try it out -> Execute
Lab exercise #7: Explore YANG Suite

## Slide 55: Get AP summary
Lab exercise #7: Explore YANG Suite

## Slide 56: Get Client summary
Lab exercise #7: Explore YANG Suite

## Slide 57: Lab exercise #8: Explore Postman
In this lab exercise we will
  Create a Workspace
  Create an Environment
  Create a Collection
  Test some queries found from yangcatalog.org or YANG Suite (any of your choice)
  Output to CURL or Python
Lab exercise #8: Explore Postman

## Slide 58: Overview
Here is an example view of Postman and how the YANG modules from previous exercises can look here. We will test and explain this in more detail in this exercise
RESTCONF path
YANG module
Xpath
Postman is a "go-to" tool for RESTCONF APIs. Some examples for automation is testing and validating RESTCONF calls to IOS-XE devices before implementing in Python, Ansible, etc.
1
2
3
Lab exercise #8: Explore Postman

## Slide 59: Launching Postman
Start by launching Postman. You should already be logged in from the pre-lab task. If not, log in now. It might look something like this
Lab exercise #8: Explore Postman

## Slide 60: Create Workspace
Lab exercise #8: Explore Postman

## Slide 61: Create Environment
Activate the new environment ... and create some variables
Lab exercise #8: Explore Postman
Values in this column are synced to your Postman account
Values in this column are stored locally in Postman on your PC
!! Remember to save !!

## Slide 62: A word about saving
Lab exercise #8: Explore Postman
This little orange dot means the file/tab/whatever is not saved
Use Ctrl+S to save the current tab, or click this icon
An example: When you run a RESTCONF call with variables from an environment, like {{host}} or {{password}} it will use the value from your SAVED file. So if you do changes in the environment, remember to save the tab

## Slide 63: Create Collection
Select "Collections"
Click the +, create a Blank collection
Rename the collection
Click "Authorization" select "Basic Auth" Enter Username and Password like this
Creating the variables like this will make Postman get them from the current active environment (that we just created)
Lab exercise #8: Explore Postman
!! Remember to save !!

## Slide 64: Creating your first Request
Lab exercise #8: Explore Postman
In the "Collections" tab and on the "Cisco C9800" collection you created in last step, Add a new request by either
  Right clicking "Cisco C9800"
  Clicking "Add a request" if you haven't created any before
  Clicking the three dots on the "Cisco C9800" line
Then select "Add request"
Name the new request "Get config"
Write your Request on the top line, default starting with "GET" and empty line
The next slides will give example of creating requests using yangcatalog and YANG Suite, with some alternative slide layouts/explanations

## Slide 65: Get config
Lab exercise #8: Explore Postman
Create the Request based on the information explored from https://yangcatalog.org
  Expand the tree until you find your module
  Base restconf path: https://{{host}}/restconf/data
  Add the "Sensor Path" to the base path
  Write the path in Postman
  Go to "Headers" and enter the following
  Press "Send" and you should get a response similar to this
  https://{{host}}/restconf/data/Cisco-IOS-XE-native:native

## Slide 66: Get config (YANG Suite alternative)
Lab exercise #8: Explore Postman
Here is an example of how to craft the same Request based on info you find in YANG Suite
  Base Restconf path: https://{{host}}/restconf/data/
  YANG-module: Cisco-IOS-XE-native
  Xpath: native
  Combined request path for copy-paste:
  Write the path in Postman
  Go to "Headers" and enter the following
  Press "Send" and you should get a response similar to this
Use colon (:) instead of forward slash (/) in the Xpath
  https://{{host}}/restconf/data/Cisco-IOS-XE-native:native
You may get some line breaks at the end. Remove them before sending the request

## Slide 67: Get AP Summary (yangcatalog)
Lab exercise #8: Explore Postman
Create the Request based on the information explored from https://yangcatalog.org
  Expand the tree until you find your module
  The middle of the webside is cut away, since it is too wide to show on this slide
  Base restconf path: https://{{host}}/restconf/data
  Copy the Sensor Path after the base restconf path, then create the rest of the query as the instructions from the previous slides
  https://{{host}}/restconf/data/Cisco-IOS-XE-wireless-access-point-oper:access-point-oper-data/capwap-data

## Slide 68: Get AP summary (YANG Suite)
Lab exercise #8: Explore Postman
Here is an example of how to craft the same Request based on info you find in YANG Suite
  Restconf path: https://{{host}}/restconf/data/
  YANG-module: Cisco-IOS-XE-wireless-access-point-oper
  Xpath: access-point-oper-data/capwap-data
  Combined request path for copy-paste:
  https://{{host}}/restconf/data/Cisco-IOS-XE-wireless-access-point-oper:access-point-oper-data/capwap-data

## Slide 69: Get Client Summary (yangcatalog)
Lab exercise #8: Explore Postman
Create the Request based on the information explored from https://yangcatalog.org
  Expand the tree until you find your module
  Base restconf path: https://{{host}}/restconf/data
  Copy the Sensor Path after the base restconf path, then create the rest of the query as the instructions from the previous slides
  https://{{host}}/restconf/data/Cisco-IOS-XE-wireless-client-oper:client-oper-data/common-oper-data

## Slide 70: Get client summary (YANG Suite)
Lab exercise #8: Explore Postman
Here is an example of how to craft the same Request based on info you find in YANG Suite
  Restconf path: https://{{host}}/restconf/data/
  YANG-module: Cisco-IOS-XE-wireless-client-oper
  Xpath: client-oper-data/shared-oper-data
  Combined request path for copy-paste:
RESTCONF path
YANG module
Xpath
If no users are connected, the return is "No Content" (status code 204)
  https://{{host}}/restconf/data/Cisco-IOS-XE-wireless-client-oper:client-oper-data/common-oper-data

## Slide 71: Output to Python
Lab exercise #8: Explore Postman
You can output the RESTCONF call as various code snippets by clicking the "Code" button
This can be used in your favorite Python editor, or just run it to test
You get this by hovering the mouse over the **** text in the Code snippet
Add "verify= False" to skip certificate checking on the host

## Slide 72: Lab exercise #9: Explore Python automation
In this exercise we will
  Use the virtual environment "automation-venv" created in Lab 4
  Connect VS Code to the Ubuntu server
  Create a Python script that
    Connects to the WLC using RESTCONF
    Gets a table of currently connected APs on the WLC
    Saves the AP list as an Excel file
Lab exercise #9: Explore Python automation

## Slide 73: Create Python venv
This lab will use the same venv for Python and Ansible automation. It could be different, and scaling to production and prototyping could often mean having a venv per project
If you did not do Lab 4, here is a copy of the commands where we created the venv. If you have created and activated your venv already these commands will not do anything (except throw some error messages)
Lab exercise #9: Explore Python automation
  devnet-adm@ubuntu-devnet:~$ source ~/automation-venv/bin/activate
  (automation-venv) devnet-adm@ubuntu-devnet:~$ python --version
  Python 3.12.3
  (automation-venv) devnet-adm@ubuntu-devnet:~$ cd wifi-automation
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation$
  devnet-adm@ubuntu-devnet:~$ sudo apt install pip python3-venv
  devnet-adm@ubuntu-devnet:~$ mkdir ~/automation-venv
  devnet-adm@ubuntu-devnet:~$ python3 -m venv ~/automation-venv/
  devnet-adm@ubuntu-devnet:~$ source ~/automation-venv/bin/activate
  (automation-venv) devnet-adm@ubuntu-devnet:~$ python --version

## Slide 74: Connect VS Code to the Ubuntu Server
Use VS Code remote to the Ubuntu Server (if you are not connected already)
  Press the Remote SSH icon (lower left corner)
  Then, in the top line, select "Connect current window to Host..."
  Select your host, or configure a new (see Lab 3)
  Select "Open Folder" in the Explorer section
  Select "/home/devnet-adm/wifi-automation/" and click OK
  Open the "examples/python-hello-world.py"
  Select the "automation-venv" venv: Click the Python version area on the bottom line
Lab exercise #9: Explore Python automation

## Slide 75: Create the Python file
Create a folder "Lab9_Python-get-ap-table" and a python file "get-ap-table.py"
The new file will automatically open in the editor window
Lab exercise #9: Explore Python automation

## Slide 76: Prepare the RESTCONF calls
Using Postman, test the RESTCONF calls to get this info from your WLC
  This is the URL of the RESTCONF call we will be using in this exercise
    https://{{host}}/restconf/data/Cisco-IOS-XE-wireless-access-point-oper:access-point-oper-data/capwap-data
  You can try specifying some fields to reduce the data size
    https://{{host}}/restconf/data/Cisco-IOS-XE-wireless-access-point-oper:access-point-oper-data/capwap-data?fields=wtp-mac;wtp-ip;name;ap-state;device-detail/static-info/board-data/wtp-serial-num;device-detail/static-info/board-data/wtp-enet-mac;device-detail/static-info/ap-models/model;tag-info/tag-source;tag-info/policy-tag-info;tag-info/site-tag;tag-info/rf-tag;tag-info/filter-info/filter-name;ap-time-info/boot-time;ap-time-info/join-time
Lab exercise #9: Explore Python automation

## Slide 77: Prepare Python packages
For this exercise, we will use the following modules
  requests
  pandas
  openpyxl
To install these, use the command "pip install requests pandas openpyxl"
If you want, you can wait installing these until you see the errors highlighted in VS Code when we try to use them
Lab exercise #9: Explore Python automation
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation$ cd Lab9_Python-get-ap-table
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab9_Python-get-ap-table$ pip install requests pandas openpyxl
  Collecting requests
  Downloading requests-2.32.3-py3-none-any.whl.metadata (4.6 kB)
  Collecting pandas
  Downloading pandas-2.2.2-cp312-cp312-manylinux_2_17_x86_64.manylinux2014_x86_64.whl.metadata (19 kB)
  Collecting openpyxl
  (...)
  Successfully installed certifi-2024.7.4 charset-normalizer-3.3.2 et-xmlfile-1.1.0 idna-3.8 numpy-2.1.0 openpyxl-3.1.5 pandas-2.2.2 python-dateutil-2.9.0.post0 pytz-2024.1 requests-2.32.3 six-1.16.0 tzdata-2024.1 urllib3-2.2.2
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab9_Python-get-ap-table$
Make sure you are in the "automation-venv", indicating by the text (automation-venv) before each line in the terminal. If not, you will get an error message

## Slide 78: Get AP table
Import the modules we will use
WLC IP, username and password as input fields, it will be asked when running the script
Create the RESTCONF call using the IP of your WLC, and the path you tested with Postman
Make the call and save the response
Some very basic error checking
The response is given as JSON. We use a pandas function "json_normalize" to flatten parts of the JSON object to present it in a table
Print the table in the terminal
Save the table to Excel and CSV
Lab exercise #9: Explore Python automation
import requests
import pandas as pd
import getpass
wlc = input("Enter WLC IP: ")
user = input("Enter user: ")
password = getpass.getpass("Enter password: ")
url = f"https://{wlc}/restconf/data/Cisco-IOS-XE-wireless-access-point-oper:access-point-oper-data/capwap-data?fields=wtp-mac;wtp-ip;name;ap-state;device-detail/static-info/board-data/wtp-serial-num;device-detail/static-info/board-data/wtp-enet-mac;device-detail/static-info/ap-models/model;tag-info/tag-source;tag-info/policy-tag-info;tag-info/site-tag;tag-info/rf-tag;tag-info/filter-info/filter-name;ap-time-info/boot-time;ap-time-info/join-time"
payload = {}
headers = {
'Accept': 'application/yang-data+json',
'Content-Type': 'application/yang-data+json'
}
response = requests.get(url, auth=(user, password), headers=headers, data=payload, verify=False)
if (response.status_code==200):
ap_table = pd.json_normalize(response.json()['Cisco-IOS-XE-wireless-access-point-oper:capwap-data'])
print(ap_table)
ap_table.to_excel('ap_table.xlsx')
ap_table.to_csv('ap_table.csv')
else:
print(f"Status code: {response.status_code}: {response.reason}")
get-ap-table.py

## Slide 79: Running the Python script from terminal
One way to run a Python script, is by using the terminal. When in the folder of the script, run using "python" and the filename
Lab exercise #9: Explore Python automation
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation$ cd Lab9_Python-get-ap-table
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab9_Python-get-ap-table$ ls -l
  total 4
  -rw-rw-r-- 1 devnet-adm devnet-adm 978 Aug 25 19:24 get-ap-table.py
  (automation-venv) devnet-adm@ubuntu-devnet:~/wifi-automation/Lab9_Python-get-ap-table$ python get-ap-table.py
  Enter WLC IP: 192.168.10.30
  Enter user: devnet-adm
  Enter password:
If there are no APs on the WLC it will have status code 204 (No Content). So it will not print the table etc, if it tried it would produce an error on the "json()[blablabla] part"
  Status code: 204: No Content
  wtp-mac name wtp-ip ... ap-state.ap-operation-state ap-time-info.boot-time ap-time-info.join-time
  0 4c:a6:4d:65:f9:40 9120E-ekms 192.168.10.182 ... registered 2024-07-25T00:28:12+00:00 2024-07-25T00:30:04.335182+00:00
  1 d4:2c:44:d9:24:40 APD42C-44D8-2F38 192.168.10.177 ... registered 2024-07-31T19:22:07+00:00 2024-07-31T19:23:42.643078+00:00
Successful run will look something like this:
Wrong username/password will look something like this:
  Status code: 401: Unauthorized
Use YOUR WLC IP

## Slide 80: Running the Python script from VS Code
Press Ctrl+F5 to run the script in VS Code
  Select "Python Debugger" if asked
Lab exercise #9: Explore Python automation
The Excel file will contain the info, but will be otherwise unformatted. You can download the file by right-clicking it and selecting "Download…" and save to a folder of your choice on your local machine.
You can open the CSV file in VS Code, or in the terminal using "cat ap_table.csv" (or several alternatives)

## Slide 81: Lab exercise #10: Install TIG stack (optional)
!!! NOTE !!!
  This exercise is marked as optional. However, if you plan on doing more Grafana stuff on day to we highly recommend that you do this, even if it will take some extra time today, or continue on to day 2
  If you plan doing primarily Python or Ansible stuff on day 2, you can skip exercise 10 (installing TIG stack) and skip to Lab exercise 11. You can then use the installation on one of the pre-installed Ubuntu Servers.
In this lab exercise, we will install "TIG Stack" as a Docker container on the Ubuntu Server
As part of the installation we will
  Create .env file containing variables
  Ensure persistant storage
  Create new bucket and adapt it so we can use InfluxDB
The next slides will give some basic overview of the TIG Stack, and how all fits together
  T = Telegraf
  I = InfluxDB
  G = Grafana
Lab exercise #10: Install TIG stack

## Slide 82: TIG Stack overview
gRPC / TCP 57000
C9800
metrics goes to the database
Grafana to visualize
TCP 8086
TCP 3000
WebUI - server:3000
Wow!
Lab exercise #10: Install TIG stack

## Slide 83: The TIG in the TIG stack
Open Source Agent: Collects and sends metrics from databases, systems, and IoT devices
Versatile Monitoring: Works with databases, systems, and IoT sensors
Lab exercise #10: Install TIG stack
Time Series Data at Scale: Store and query large volumes of time-stamped data
Real Time Analytics: Fast processing for immediate insights
Seamless Integration: Compatible with various tools and platforms
Visualize Anything: Create dashboards for any data
Real Time Insights: Customizable, interactive visuals
Flexible Integration: Connects to multiple data sources

## Slide 84: Different flavours of Influx
InfluxDB 1.x - InfluxQL
Lab exercise #10: Install TIG stack
InfluxDB 2.x - FLUX
InfluxDB 3.x – InfluxQL (v2)
We will use InfluxDB 2.x but query data using InfluxQL

## Slide 85: Make some notes
Lab exercise #10: Install TIG stack
There are some variables that need to be typed later, so to save time you can make a .txt file while we continue in this lab
Even better, you could use your favorite password manager (KeePass etc)
  Admin token: {we will fill in this later}
  Org ID: {we will fill in this later}
  Container ID: {we will fill in this later}
Lab10_Notes.txt

## Slide 86: TIG stack installation
Create a .env file to store variables
  Add the INFLUXDB_ADMIN_TOKEN to your .txt file
Create persistent storage
Create the Telegraf config file
  devnet-adm@ubuntu-devnet:~$ cd ~
  devnet-adm@ubuntu-devnet:~$ mkdir tig-stack
  devnet-adm@ubuntu-devnet:~$ cd tig-stack
  devnet-adm@ubuntu-devnet:~/tig-stack$ nano .env
!
#add the following, and change the variables if needed
!
Lab exercise #10: Install TIG stack
  devnet-adm@ubuntu-devnet:~/tig-stack$ docker volume create grafana-data
  devnet-adm@ubuntu-devnet:~/tig-stack$ docker volume create influxdb-data
  devnet-adm@ubuntu-devnet:~/tig-stack$ mkdir -p telegraf/conf
  devnet-adm@ubuntu-devnet:~/tig-stack$ nano telegraf/conf/telegraf.conf
[global_tags]
host = "My-Telegraf"
[agent]
interval = "10s"
round_interval = true
metric_batch_size = 1000
metric_buffer_limit = 10000
collection_jitter = "0s"
flush_interval = "10s"
flush_jitter = "0s"
precision = ""
debug = false
quiet = false
logfile = ""
hostname = "My-Telegraf"
omit_hostname = false
###############################################################################
# OUTPUT PLUGINS #
###############################################################################
# Configuration for influxdb server to send metrics to
[[outputs.influxdb_v2]]
urls = [ "http://influxdb:8086" ]
token = "${INFLUXDB_ADMIN_TOKEN}"
organization = "${INFLUXDB_ORG}"
bucket = "${INFLUXDB_BUCKET}"
# tagexclude = ["influxdb_database"] ### Optional: Exclude specific tags if needed
[outputs.influxdb_v2.tagpass]
influxdb_database = ["${INFLUXDB_BUCKET}"]
###############################################################################
# INPUT PLUGINS #
###############################################################################
[[inputs.cisco_telemetry_mdt]]
transport = "grpc"
service_address = ":57000"
[inputs.cisco_telemetry_mdt.tags]
influxdb_database = "${INFLUXDB_BUCKET}"
telegraf.conf
INFLUXDB_ADMIN_USER=devnet-adm
INFLUXDB_ADMIN_PASSWORD=ChangeMe2025!
INFLUXDB_ORG=devnet
INFLUXDB_BUCKET=c9800-bucket
INFLUXDB_ADMIN_TOKEN=ChangeMe2025!
GF_SECURITY_ADMIN_USER=devnet-adm
GF_SECURITY_ADMIN_PASSWORD=ChangeMe2025!
.env

## Slide 87: TIG stack installation
Configure docker-compose.yml
  Add the following config to docker-compose.yml
Docker compose
  This will take a few seconds to download all images.
  To view logs from a service (telegraf, influxdb, grafana) use this
Connect to Grafana using web browser
  Notice we use HTTP, not HTTPS for this lab install
  http://192.168.10.{your Ubuntu IP}:3000
  For now, just test that you can log in using the username and password from the .env file we created earlier. For this lab it will be the same as everywhere else unless you changed it 
Lab exercise #10: Install TIG stack
  devnet-adm@ubuntu-devnet:~$ cd ~/tig-stack
  devnet-adm@ubuntu-devnet:~$ nano ./docker-compose.yml
  devnet-adm@ubuntu-devnet:~$ docker compose up -d
services:
influxdb:
container_name: influxdb
image: influxdb:2.7.10
expose:
- 8086
restart: always
volumes:
- influxdb-data:/var/lib/influxdb2
ports:
- 8086:8086
environment:
- DOCKER_INFLUXDB_INIT_MODE=setup
- DOCKER_INFLUXDB_INIT_USERNAME=${INFLUXDB_ADMIN_USER}
- DOCKER_INFLUXDB_INIT_PASSWORD=${INFLUXDB_ADMIN_PASSWORD}
- DOCKER_INFLUXDB_INIT_ORG=${INFLUXDB_ORG}
- DOCKER_INFLUXDB_INIT_BUCKET=${INFLUXDB_BUCKET}
- DOCKER_INFLUXDB_INIT_RETENTION=2w
- DOCKER_INFLUXDB_INIT_ADMIN_TOKEN=${INFLUXDB_ADMIN_TOKEN}
telegraf:
container_name: telegraf
image: telegraf:1.32.0
restart: always
ports:
- 57000:57000
env_file:
- .env
environment:
- INFLUXDB_TOKEN=${INFLUXDB_ADMIN_TOKEN}
- INFLUXDB_ORG=${INFLUXDB_ORG}
- INFLUXDB_BUCKET=${INFLUXDB_BUCKET}
volumes:
- ./telegraf/conf/telegraf.conf:/etc/telegraf/telegraf.conf:ro
- /var/run/docker.sock:/var/run/docker.sock
depends_on:
- influxdb
grafana:
container_name: grafana
image: grafana/grafana:11.1.4
expose:
- 3000
restart: always
ports:
- 3000:3000
environment:
- GF_SECURITY_ADMIN_USER=${GF_SECURITY_ADMIN_USER}
- GF_SECURITY_ADMIN_PASSWORD=${GF_SECURITY_ADMIN_PASSWORD}
- GF_INSTALL_PLUGINS=
volumes:
- grafana-data:/var/lib/grafana
#- ./grafana/grafana.ini:/etc/grafana/grafana.ini:ro
depends_on:
- influxdb
- telegraf
volumes:
grafana-data:
external: true
influxdb-data:
external: true
docker-compose.yml
  devnet-adm@ubuntu-devnet:~$ docker logs telegraf

## Slide 88: InfluxDB 2.X
http://192.168.10.{your Ubuntu IP}:8086
Username/password from .env file (same as always unless changed)
Notice that we here also use HTTP, not HTTPS
Change retention on your bucket to f.ex 31 days.
Lab exercise #10.1: Install TIG stack, InfluxDB

## Slide 89: InfluxDB 2.X
http://192.168.10.{your Ubuntu IP}:8086
Create a an additonal bucket
  Name it: syslog-bucket
Set retention to 30 days
You can find the bucket-ID here
Lab exercise #10.1: Install TIG stack, InfluxDB

## Slide 90: A word about tokens (optional / info)
Lab exercise #10.1: Install TIG stack, InfluxDB
In a production environment you should have several tokens
Admin token
  Made in the .env file
  All access (RW to everything)
  Used for InfluxDB integration
Bucket or DB specific tokens
  RO or RW access to specified resources
Read-only tokens
  RO access to specified resources
On the right is shown how to create a new token (you do not need to do this in this deep dive lab)

## Slide 91: Locate your Organization ID
InfluxDB > About
Note this down in the Lab10_notes.txt file
Lab exercise #10.1: Install TIG stack, InfluxDB

## Slide 92: Locate your InfluxDB Docker container ID
Note this down in the Lab10_notes.txt file
In the notes, you will then have
  Admin token
  Org ID
  Container ID
For a live installation you should have at least one RO token, or separate tokens for each bucket. Not use the admin token for everything like we do here 
Lab exercise #10.1: Install TIG stack, InfluxDB
  devnet-adm@ubuntu-devnet:~/tig-stack$ docker ps -a --filter name=influxdb
  CONTAINER ID IMAGE COMMAND CREATED STATUS PORTS NAMES
  71b07ba58958 influxdb:2.7.10 "/entrypoint.sh infl…" 2 minutes ago Up 2 minutes 0.0.0.0:8086->8086/tcp, :::8086->8086/tcp influxdb
  devnet-adm@ubuntu-devnet:~/tig-stack$

## Slide 93: InfluxDB 2.X: Query data in Grafana with InfluxQL
We will use the values from our lab notes
  In v1 mode, it is called a "database"
What we have done here, is create a db which point to the same Bucket ID as the c9800-bucket
We now have
  a c9800-bucket where we can query using FLUX
  a c9800-db where we can query the same data, using InfluxQL
  See earlier slide "Different flavors of InfluxDB"
Lab exercise #10.1: Install TIG stack, InfluxDB
  devnet-adm@ubuntu-devnet:~/tig-stack$ docker exec -it <your_container-id> bash
  root@71b07ba58958:/# influx v1 dbrp list
  Error: must specify org ID or org name
  root@71b07ba58958:/# influx v1 dbrp list --org-id <your_org-id> --token <your_admin_token>
  ID Database Bucket ID Retention Policy Default Organization ID
  VIRTUAL DBRP MAPPINGS (READ-ONLY)
  ----------------------------------
  ID Database Bucket ID Retention Policy Default Organization ID
  b53d2ec9d932635a _monitoring b53d2ec9d932635a autogen true 6a6f13e3a65de450
  09aac3a6cee8ab99 _tasks 09aac3a6cee8ab99 autogen true 6a6f13e3a65de450
  574c74f705d86be2 syslog-bucket 294c74f678d86ab3 autogen true 6a6f13e3a65de450
  574c74f705d86be2 c9800-bucket 574c74f705d86be2 autogen true 6a6f13e3a65de450
  root@71b07ba58958:/# influx v1 dbrp create --db c9800-db --rp c9800-rp --bucket-id 574c74f705d86be2 --default --org-id <your_org-id> --token <your_admin_token>
  root@71b07ba58958:/# influx v1 dbrp create --db syslog-db --rp syslog-rp --bucket-id 294c74f678d86ab3 --default --org-id <your_org-id> --token <your_admin_token>
  ID Database Bucket ID Retention Policy Default Organization ID
  0d94a420be168000 c9800-db bc926b463de1d39a c9800-rp true 6a6f13e3a65de450
  root@71b07ba58958:/# exit
  devnet-adm@ubuntu-devnet:~/tig-stack$
Insert YOUR container-id
Insert YOUR org-id
Insert YOUR admin token
Repeat this step for the syslog-bucket

## Slide 94: A bit about telemetry subscriptions
Below are a couple of sample "telemetry subscriptions"'
Telemetry subscriptions are the same as Catalyst Center use to get telemetry data from IOS-XE devices
We will use telemetry subscriptions to get data from the 9800 over to our TIG stack (9800 -> Telegraf -> InfluxDB -> Grafana)
The syntax is inside configuration mode (conf t) on 9800
  Each subscription has an ID
  The filter is built from the YANG model
  Update policy decide how often 9800 will push this to Telegraf (in 100ths of a second -> 500 = 5 sec)
  Receiver IP is the IP of Telegraf (in this lab: your Ubuntu server)
You will not configure these now, they are only examples. We will use some other data 
telemetry ietf subscription 101
encoding encode-kvgpb
filter xpath /ios:native/version
stream yang-push
update-policy periodic 30000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
telemetry ietf subscription 102
encoding encode-kvgpb
filter xpath /process-cpu-ios-xe-oper:cpu-usage/cpu-utilization/five-seconds
stream yang-push
update-policy periodic 500
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
Lab exercise #10: Install TIG stack

## Slide 95: Lab exercise #11: Build your first Grafana Dashboard
In this exercise you will be hand-held to build your first dashboard in Grafana
The dashboard will be an AP Dashboard
More dashboards to be explored on day 2
!!! A word of caution when making your first dashboards... don't use "Esc" key without saving, you might have to do some work again. You will probably do just that, and THEN learn it the hard way  !!!
If you are doing this lab exercise using TIG Stack on a shared server, use your shared Ubuntu Server referring to the Lab topology:
Lab exercise #11: Build your first Grafana Dashboard
Students | Shared Ubuntu Server | Grafana URL | InfluxDB URL
Harsha, Craig, Sean, Raheel | ubuntu11 (192.168.10.11) | http://192.168.10.11:3000 | http://192.168.10.11:8086
Kenneth, Daniel J, Biruk | ubuntu12 (192.168.10.12) | http://192.168.10.12:3000 | http://192.168.10.12:8086
Joseph, Matt, Jason | ubuntu13 (192.168.10.13) | http://192.168.10.13:3000 | http://192.168.10.13:8086
Jack, Daniel W, Harsh, Chris | ubuntu14 (192.168.10.14) | http://192.168.10.14:3000 | http://192.168.10.14:8086
Brian, James, Szymon, Todd | ubuntu15 (192.168.10.15) | http://192.168.10.15:3000 | http://192.168.10.15:8086
Terry, Eddie, Sitarama, Francois | ubuntu16 (192.168.10.16) | http://192.168.10.16:3000 | http://192.168.10.16:8086

## Slide 96: Add the following telemetry subscriptions on the WLC
Lab exercise #11: Build your first Grafana Dashboard
telemetry ietf subscription 105
encoding encode-kvgpb
filter xpath /wireless-access-point-oper:access-point-oper-data/wireless-access-point-oper:ap-name-mac-map
stream yang-push
update-policy periodic 30000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
do show telemetry ietf subscription 105
telemetry ietf subscription 106
encoding encode-kvgpb
filter xpath /wireless-rrm-oper:rrm-oper-data/wireless-rrm-oper:rrm-measurement/wireless-rrm-oper:load
stream yang-push
update-policy periodic 5000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
do show telemetry ietf subscription 106
telemetry ietf subscription 107
encoding encode-kvgpb
filter xpath /wireless-access-point-oper:access-point-oper-data/wireless-access-point-oper:radio-oper-data/wireless-access-point-oper:phy-ht-cfg
stream yang-push
update-policy periodic 5000
receiver ip address 192.168.10.7 57000 protocol grpc-tcp
do show telemetry ietf subscription 107
Change this to your Ubuntu IP (or IP of the TIG stack you are using)
Change this to your Ubuntu IP (or the IP of the TIG stack you are using)
wlc9# conf t
wlc9# show run | sec telemetry ietf
For shared servers, check if the subscriptions exist!

## Slide 97: Grafana (http://{Ubuntu-IP}:3000)
Set a name for your database
Set Query language to InfluxQL
URL: http://influxdb:8086
Lab exercise #11: Build your first Grafana Dashboard
Add your first data source -> InfluxDB

## Slide 98: Grafana (http://{Ubuntu-IP}:3000)
Lab exercise #11: Build your first Grafana Dashboard
Grafana needs to use a token to be able to read from the database, and InfluxDB password.
  For this lab we will use the Admin token
  In a live system, create a RO token and use it here
Add a custom HTTP Headers
  Header: Authorization
  Value: Token <API-TOKEN>
  There is a space between Token and <token>
  Database: c9800-db
  User/Pass: devnet-adm / ChangeMe2025!
!!! You should have 3 measurements found !!!
Token ChangeMe2025!
ChangeMe2025!

## Slide 99: Create your first dashboard
Go to "Dashboards" in the left menu, then create a new dashboard
!!! Don't press the very tempting "+Add Visualization" button yet, we will do some pre-work first 
Start by giving the new dashboard a name
Lab exercise #11: Build your first Grafana Dashboard

## Slide 100: Grafana
We will create a variable that gets all AP names
Go to Dashboard settings -> Variables
Lab exercise #11: Build your first Grafana Dashboard
Name: APName
Query:
SHOW TAG VALUES WITH KEY = "wtp_name"
When copy-pasting this, make sure to remove the extra line break if it occurs

## Slide 101: Grafana
We create a second variable, the AP MAC address
Name: APMac
Show on dashboard: Nothing
Query: (when copy-pasting, make sure to remove the extra line-break if it occurs)
Check if it is working with Run query
Press Apply
Then save your dashboard
Lab exercise #11: Build your first Grafana Dashboard
SELECT distinct("wtp_mac") FROM "Cisco-IOS-XE-wireless-access-point-oper:access-point-oper-data/ap-name-mac-map" WHERE ("wtp_name" =~ /^$APName$/)

## Slide 102: Grafana
Go back to the Dashboard main page
Add visualization and make one using time series
"Time series" is automatically selected. If not, select it here
Lab exercise #11: Build your first Grafana Dashboard

## Slide 103: Grafana
In the lower part of the screen, edit the query
Click "select measurement", you will get a menu of all measurements
Choose the Cisco-IOS-XE-wireless-rrm-oper:rrm-oper-data/rrm-measurement/load
(Optional) You can enter yangcatalog.org, find the Cisco-IOS-XE-wireless-rrm-oper module and explore which values you could get from this YANG model
Lab exercise #11: Build your first Grafana Dashboard

## Slide 104: Grafana
Add another row
To create an alias, choose "alias" and click the alias(alias) button
Type the name and press Enter
To get the options, click the "+" signs, like here
You can search in the "Choose" field over the options
To specify the value inside the "field(value)" click it
Try to make the screen match this image
Lab exercise #11: Build your first Grafana Dashboard

## Slide 105: Grafana
Set the panel title
Under graph styles you can make it look like you want  Set Connect null values to always
Fix values to percent
In the field to the right, you have lots of options
Lab exercise #11: Build your first Grafana Dashboard

## Slide 106: Grafana
Lab exercise #11: Build your first Grafana Dashboard
You do not want number of clients to show as percent
We use an override for the Clients graph
Select the regex-override
Standard options > Unit
Standard options > Unit = short

## Slide 107: Grafana
(Optional) Tooltip -> Tooltip mode: All
(Optional) Legend
  Mode: Table
  Placement: Right
  Values: Last*, Min & Max
(Optional) Thresholds
  35% (Red)
  Percentage
  As lines (dashed)
(Optional) Graph styles
  Fill opacity: 10
Remember to apply changes
Lab exercise #11: Build your first Grafana Dashboard
Graph colors
Time range
Select variable

## Slide 108: Duplicate dashboards
You can duplicate the visualization, then edit the second one to create a 5GHz variant
Edit the duplicated visualization
Lab exercise #11: Build your first Grafana Dashboard

## Slide 109: Edit the values for the 5GHz visualization
Lab exercise #11: Build your first Grafana Dashboard
Panel Options: Title
FROM in Query: radio_slot_id::tag =1
  If the AP is dual 5GHz (for example 9136, 9166) 5GHz is at 1 and 2
Apply to go back to the Dashboard
Save the Dashboard

## Slide 110: Grafana
Add a new visualization to your AP Dashboard
Press the field where it defaults to "Time series"
Search for and select "State timeline "
Lab exercise #11: Build your first Grafana Dashboard

## Slide 111: Grafana
First we create this visualization for 2.4GHz. To do this we select radio_slot_id 0
It doesn't look impressive yet:
Lab exercise #11: Build your first Grafana Dashboard

## Slide 112: Grafana
We will edit the options Start by giving it a name
Merge consecutive values
Align to text to center
Change row hight and fill opacity
Conect null values
Remember to save
Lab exercise #11: Build your first Grafana Dashboard

## Slide 113: Grafana
The current color scheme derive colors from thresholds. The values also look a bit weird. We will change this to a scheme which give each bar a separate fixed color
Naviagate to Standard Options
  At the bottom you will find Color scheme
  Change it to f.ex classic palette
Lab exercise #11: Build your first Grafana Dashboard

## Slide 114: Grafana
Apply to get back to your Dashboard
Duplicate the panel (top right corner and duplicate) and make one for 2.4, 5 and 6GHz (radio-slot)
Lab exercise #11: Build your first Grafana Dashboard
Slot 0 = 2.4GHz
Slot 1 = 5GHz
Slot 2 (if AP is dual 5GHz) = 5GHz
Slot 3 = 6GHz

## Slide 115: My first AP Dashboard (example)
Lab exercise #11: Build your first Grafana Dashboard
Select AP
2.4GHz
5GHz
6GHz
Time window
Auto refresh interval

## Slide 116: My first AP Dashboard (example 2)
Lab exercise #11: Build your first Grafana Dashboard

## Slide 117: Save your dashboard to JSON
Lab exercise #11: Build your first Grafana Dashboard

## Slide 118: Lab exercise #12: Install YANG Suite (optional)
This exercise shows how to install YANG Suite yourself, as a Docker container
After successful installation, you can connect to YANG Suite on
  https://{your Ubuntu IP}:8443
Note that there is a binding to the servers IP that you specify as part of the installation script. So if you change IP you will have to reconfigure (or just delete and reinstall)
Lab exercise #12: Install YANG Suite (optional)

## Slide 119: YANG Suite installation
Installation (requires Docker installed)
(...appx 4-5min depending on your VM speed)
While waiting, please carry on to the next slides 
Reference: https://developer.cisco.com/yangsuite/
  devnet-adm@ubuntu-devnet:~$ cd ~
  devnet-adm@ubuntu-devnet:~$ git clone https://github.com/CiscoDevNet/yangsuite
  devnet-adm@ubuntu-devnet:~$ cd yangsuite/docker/
  devnet-adm@ubuntu-devnet:~/yangsuite/docker$ ./start_yang_suite.sh
  Hello, please setup YANG Suite admin user.
  username: devnet-adm
  password: ChangeMe2025!
  confirm password: ChangeMe2025!
  Will you access the system from a remote host? (y/n): y
  Enter local host FQDN or IP: 192.168.10.7
  Setup test certificates? (y/n): y
  ##################################################
  ## Generating self-signed certificates ##
  (....)
  email: devnet-adm@test.com
  Setup test certificates? (y/n): y
  (...blah blah blah)
Lab exercise #12: Install YANG Suite (optional)
Change this to your Ubuntu IP
From here you can just press Enter-Enter-Enter
!!! Note: This will create problems if you try to use YANG Suite if you have changed the IP of your Ubuntu server to something else. In that case, delete YANG Suite and reinstall !!!
To delete, use rm -R ~/yangsuite

## Slide 120: Run in detached mode
When you get this output, it is ready to run
To "free up" the command line, press Ctrl+C to stop YANG Suite
Then, to start the container in "detached" mode:
Access via HTTPS: https://{Your Ubuntu IP}:8443
Lab exercise #12: Install YANG Suite (optional)
  devnet-adm@ubuntu-devnet:~$ cd ~/yangsuite/docker/
  devnet-adm@ubuntu-devnet:~/yangsuite/docker/$ docker compose up -d

## Slide 121: YANG Suite EULA
Lab exercise #12: Install YANG Suite (optional)
devnet-adm
ChangeMe2025!

## Slide 122: Create new device
Create new device
Lab exercise #12: Install YANG Suite (optional)
8

## Slide 123: Create new device
Create new device
Use your WLC IP
Lab exercise #12: Install YANG Suite (optional)

## Slide 124: Create repository and Yangset
Create default repository and Yangset
(this will take a couple of minutes, so just be patient)
Lab exercise #12: Install YANG Suite (optional)