## Slide 1: Build your own Wi-Fi automation lab Pre-lab tasks
Andreas Koksrud / Telenor Bedrift
Kjetil Teigen Hansen / Conscia

## Slide 2: References / inspiration
https://github.com/CiscoDevNet/yangsuite/
https://postman.com
https://docs.ansible.com/ansible/latest/collections/cisco/ios/ios_facts_module.html
https://www.wifireference.com/2020/01/14/viewing-network-telemetry-from-the-catalyst-9800-with-grafana/
https://grafana.com/grafana/dashboards/13462-device-health-monitoring/
https://grafana.com/grafana/dashboards/12468-catalyst-9800-client-stats/
https://wirelessisfun.wordpress.com/2020/12/10/network-telemetry-data-and-grafana-part-1-the-advanced-netconf-explorer/
https://python.org
https://codeium.com
References

## Slide 3: Copyright
© Andreas Koksrud 2024. All rights reserved. This presentation is provided for educational and informational purposes only. You may distribute and learn from this presentation, but commercial use or any form of monetization is strictly prohibited without prior written consent.
Any slides marked Kjetil Teigen Hansen or the Conscia logo will also have full or co-ownership by Kjetil.
Copyright

## Slide 4: Prerequisites
Cisco.com account with access to downloading WLC (9800-CL at https://software.cisco.com)
Postman account (https://postman.com)
Windows laptop with administrative privileges
Complete the pre-lab exercises (this document) before the deep dive labs
Without these, parts of the Deep Dive might be difficult to complete, or steps might differ severely
Communications

## Slide 5: Communications
WebEx space: Wi-Fi automation lab
Please help each other
Sharing is caring 
Communications

## Slide 6: Agenda
Pre-lab
Install VirtualBox
Install Cisco 9800-CL
Install Ubuntu Server w/Docker
Install Postman
Install VS Code
Day 1
Day 2
In-depth explore a topic of choice
Sort out pre-lab task problems
Grafana / TIG-stack
Grafana Cloud
Ansible
Python
Other vendors (MIST/Meraki/Aruba)
Get to know the lab environment
Configure your AP
Connect VS Code to Ubuntu
Install and explore Ansible
Explore Python automation
Install and explore YANG Suite
Explore Postman
Install and explore Grafana
Agenda

## Slide 7: Scope
In scope
  Getting started with various systems/languages/solutions for lab purposes
  Get a lab environment up and running on your own laptop
  Some nice examples to try various aspects of automation
  Inspiring you to explore deeper on your own
Out of scope topics
  Git
  Learning the languages (Ansible, Python, InfluxQL, etc)
  Learning Linux
  Deploying the systems for production use
Scope

## Slide 8: Topology
Lab topology

## Slide 9: Pre-lab task #1: VirtualBox
In this task we will install VirtualBox
This lab will use VirtualBox to run virtual machines (VMs) on your laptop
  Cisco C9800-CL Wireless LAN Controller
  Ubuntu Linux with Docker to run some different containers
The Python-based exercises can also be run directly on your host OS Python-environment. But a VM give flexibility to test stuff without messing with your production OS. Ansible can not (currently) be run on Windows so it needs a Linux VM to run. The TIG-stack could also be run on the host OS, but again for lab purposes a VM is much easier to just wipe if (when) you test some weird stuff that breaks everything.
You can also use WSL (Windows Subsystem for Linux), which might be just as good or better in many situations. But this lab covers the use of a VM on VirtualBox 
Pre-lab task #1: VirtualBox

## Slide 10: Alternative solutions
VirtualBox installation needs admin privileges
  If you do not have that, give me a hint and I will install an Ubuntu Server for you on the common Proxmox server (see topology)
  For 9800-CL you can use the common installation wlc9 (see topology)
If you are using a newer MacOS
  No VirtualBox version available for MacOS with Apple silicon (only for x86), as of Oct 2024
  You can run Ubuntu in Parallels, you will need the ARM64 version of Ubuntu
  Detailed instructions will not be provided, but in general it will be the same, including network adapter in bridged mode
  For 9800-CL you can use the common installation wlc9 (see topology)
Weak laptops
  If you have a weak laptop, you can run only the Ubuntu server, and use a common 9800
Common servers
  Since I do not bring with me a portable datacenter, the resources of common servers are limited
  1x 9800 and 3-4 Ubuntu servers should run fine
  We might test with more, or you will have to share
Pre-lab task #1: VirtualBox

## Slide 11: VirtualBox installation
Needs admin privileges
Not all steps are shown here, it is mostly "Next-next-next"
As default folder for VMs, I use "C:\Virtual Machines", you can use whatever, but screenshots here will show this path
Pre-lab task #1: VirtualBox
  https://virtualbox.org/

## Slide 12: VM Networking
In this lab we use bridged network adapters
  Each VM gets an IP alongside your host, directly on the network
  Switchports must accept multiple mac addresses from each host
  For APs connect to 9800, I prefer this, rather than NAT'ing through your host
  Also, for WLC connect to Ubuntu (for telemetry), I also prefer this over NAT'ing
Alternative using NAT Networks
  Host IP is shared as outside IP
  VirtualBox networking NATs each machine to the outside network
  Configure this in VirtualBox -> File -> Tools -> Network Manager -> NAT Networks
  Then assign the NAT Network to the VMs Network adapter
  Notice the difference in VirtualBox on
    NAT: The VM will have access to the outside network via the hosts IP. But not to other VMs, and not to or from the host.
    NAT Network: All clients connected to the same NAT Network can access each other. To get access from your laptop (example, for SSH), create a Port Forwarding rule with 127.0.0.1 as the source address. You can then do SSH from your laptop to 127.0.0.1:8022 in this example
Pre-lab task #1: VirtualBox

## Slide 13: Pre-lab task #2: Ubuntu Server
Download Ubuntu Server 24.04
  https://ubuntu.com/download/server
If using MacOS, download the ARM64 version, and use Parallels
  https://ubuntu.com/download/server/arm
If using MacOS, see slide 10 "Alternative solutions" for network interface config on the Parallels side
Pre-lab task #2: Ubuntu Server

## Slide 14: Installing Ubuntu Server
Start PowerShell (alternatively, you can follow GUI instructions on next page)
Go to folder where you have your VMs
  The example uses 'c:\Virtual Machines', change to your directory accordingly
  cd ‘c:\Virtual Machines\’
  Create and start the VM, follow these instructions
  (copy-paste is possible from this box)
Pre-lab task #2: Ubuntu Server
  PS C:\> cd 'Virtual Machines'
  PS C:\Virtual Machines>
  PS C:\Virtual Machines> VBoxManage createvm --name "ubuntu-devnet" --ostype Ubuntu_64 --register
  PS C:\Virtual Machines> VBoxManage modifyvm "ubuntu-devnet" --cpus 1 --memory 4096 --vram 30 --graphicscontroller vmsvga --usbohci on --mouse usbtablet --pae off --boot1 disk --boot2 dvd --boot3 none --audio-enabled off
  PS C:\Virtual Machines> VBoxManage createhd --filename ".\ubuntu-devnet\ubuntu-devnet.vdi" --size 40000 --variant Standard
  PS C:\Virtual Machines> VBoxManage storagectl "ubuntu-devnet" --name "SATA Controller" --add sata --bootable on
  PS C:\Virtual Machines> VBoxManage storageattach "ubuntu-devnet" --storagectl "SATA Controller" --port 0 --device 0 --type hdd --medium ".\ubuntu-devnet\ubuntu-devnet.vdi"
  PS C:\Virtual Machines> VBoxManage storagectl "ubuntu-devnet" --name "IDE Controller" --add ide
  PS C:\Virtual Machines> VBoxManage storageattach "ubuntu-devnet" --storagectl "IDE Controller" --port 0 --device 0 --type dvddrive --medium ".\ubuntu-24.04-live-server-amd64.iso"
  PS C:\Virtual Machines> ipconfig /all
  <<< Copy the "Description" for the NIC you will use. For me it is "Intel(R) Ethernet Connection (7) I219-LM" >>>
  PS C:\ Virtual Machines> VBoxManage modifyvm "ubuntu-devnet" --nic1 bridged --cable-connected1 on --bridgeadapter1 "Intel(R) Ethernet Connection (7) I219-LM"
  PS C:\ Virtual Machines> VBoxManage startvm "ubuntu-devnet"

## Slide 15: Create Ubuntu server (VirtualBox GUI screenshots)
Pre-lab task #2: Ubuntu Server
As an alternative to the PowerShell creation from last page, here are some screenshots
Then, enter settings and edit the rest

## Slide 16: Ubuntu server install
Pre-lab task #2: Ubuntu Server
Frequent updates to Ubuntu can make the following pages somewhat different, but the basics should be recognizable

## Slide 17: Ubuntu server install - Network configuration
For pre-lab install you can use DHCP or static IP in your own environment. When in the lab environment, you can change to (another) static IP. See later slide on static vs DHCP.
Pre-lab task #2: Ubuntu Server
Leave this blank

## Slide 18: Ubuntu server install - Disk usage
Pre-lab task #2: Ubuntu Server
When you encounter the disk usage screen, please take a little care and follow these steps
If not, you will only use about 50% of the allocated disk
In the first screen, choose "Use an entire disk" (default)
At the next screen, select the "ubuntu-lv" option
Press Enter, select Edit
Change the "Size" to the max value and save
IF you have forgotten this, here are the commands to extend the size later
  devnet-adm@ubuntu-devnet:~$ sudo lvdisplay | grep "LV Path"
  LV Path /dev/ubuntu-vg/ubuntu-lv
  devnet-adm@ubuntu-devnet:~$ sudo lvextend -l +100%FREE /dev/ubuntu-vg/ubuntu-lv
  devnet-adm@ubuntu-devnet:~$ df -h | grep "lv"
  /dev/mapper/ubuntu--vg-ubuntu--lv 37G 14G 22G 39% /
devnet-adm@ubuntu-devnet:~$ sudo resize2fs /dev/mapper/ubuntu--vg-ubuntu--lv

## Slide 19: Ubuntu server install
Pre-lab task #2: Ubuntu Server
ChangeMe2024!
ChangeMe2024!
On the next pages, just keep the defaults and move on, until you reach this page

## Slide 20: Ubuntu server install
Pre-lab task #2: Ubuntu Server
  devnet-adm@ubuntu-devnet:~$ sudo apt update
devnet-adm@ubuntu-devnet:~$ sudo apt upgrade

## Slide 21: Connecting to the server using SSH
Pre-lab task #2: Ubuntu Server
Now would be a great time to connect to the Ubuntu server using your favourite SSH client. Like MobaXterm, SecureCRT, PuTTY, etc. You can also use the ssh CLI tool in your preferred shell
The main reason for this is copy-paste, which you will use during these pre-lab tasks, and much more in the deep dive itself  It might be possible to get good copy-paste behavior in the VirtualBox console, but the eventual instructions for that is still "to-be"
If you have static IP and SSH up and running, the next time you reboot your Ubuntu Server, you could use "Headless Start" to prevent the console window pop-up.
If you need the console when started headless, just use the "Show" button found where the Start button usually is before the VM is started

## Slide 22: VirtualBox Guest Additions
Pre-lab task #2: Ubuntu Server
  devnet-adm@ubuntu-devnet:~$ sudo apt install build-essential dkms linux-headers-$(uname -r)
devnet-adm@ubuntu-devnet:~$ sudo mkdir -p /mnt/cdrom
devnet-adm@ubuntu-devnet:~$ sudo mount /dev/cdrom /mnt/cdrom
mount: /mnt/cdrom: WARNING: source write-protected, mounted read-only.
devnet-adm@ubuntu-devnet:~$ cd /mnt/cdrom
devnet-adm@ubuntu-devnet:~$ sudo ./VBoxLinuxAdditions.run
devnet-adm@ubuntu-devnet:~$ sudo reboot
RightCtrl + F switches between full-screen and window
Tap RightCtrl to "free" input from guest

## Slide 23
Static IP vs DHCP
network:
version: 2
ethernets:
enp0s3:
dhcp4: true
# dhcp4: false
# addresses:
# - 192.168.10.7/24
# routes:
# - to: default
# via: 192.168.10.1
# nameservers:
# addresses: [1.1.1.1,8.8.8.8]
99_config.yaml
Pre-lab task #2: Ubuntu Server
(example with DHCP)
(example with static IP)
One method to change between DHCP and static IP, is to edit the YAML files in /etc/netplan/
We just create a new file called 99_config.yaml, and when we run "netplan apply" it will use that file for config. We delete the auto-created "50-cloud-init.yaml"
For simplicity, I usually just comment out the parts that I don't use.
For DHCP I comment out the lines related to static
For static config I comment the line "dhcp4: true" and uncomment the rest
Change this to whatever name you have here
  devnet-adm@ubuntu-devnet:~$ sudo nano /etc/netplan/99_config.yaml
  (copy-paste from the example in the top right corner, then save and quit)
devnet-adm@ubuntu-devnet:~$ sudo chmod 600 /etc/netplan/99_config.yaml
devnet-adm@ubuntu-devnet:~$ ls -l /etc/netplan/
total 8
-rw------ 1 root root 593 Sep 04 13:35 50-cloud-init-yaml
-rw------ 1 root root 85 Sep 08 15:46 99_config.yaml
(... cut for brevity ...)
devnet-adm@ubuntu-devnet:~$ sudo rm /etc/netplan/50-cloud-init.yaml
devnet-adm@ubuntu-devnet:~$ sudo netplan apply

## Slide 24: Create an SSH key -> Import to Ubuntu keystore
Start by opening Powershell (not CMD for this task)
Then, logging in to your Ubuntu Server using SSH
Create SSH key for your user
Copy the public part of your key to Ubuntu
Reference: https://code.visualstudio.com/docs/remote/ssh-tutorial
Pre-lab task #2: Ubuntu Server
  PS C:\> ssh -l devnet-adm 192.168.10.7
  devnet-adm@ubuntu-13:~$ exit
  PS C:\> type ~\.ssh\id_ed25519.pub | ssh -l devnet-adm 192.168.10.7 "cat >> .ssh/authorized_keys"
Change to your
server's IP
  PS C:\> ssh-keygen -t ed25519

## Slide 25
Git clone the example files
Pre-lab task #2: Ubuntu Server
  devnet-adm@ubuntu-devnet:~$ cd ~
  devnet-adm@ubuntu-devnet:~$ git clone https://github.com/akoksrud/wifi-automation
  Cloning into 'wifi-automation'...
  remote: Enumerating objects: 20, done.
  remote: Counting objects: 100% (20/20), done.
  remote: Compressing objects: 100% (15/15), done.
  remote: Total 20 (delta 2), reused 15 (delta 1), pack-reused 0
  Receiving objects: 100% (20/20), 15.61 KiB | 841.00 KiB/s, done.
  Resolving deltas: 100% (2/2), done.
  devnet-adm@ubuntu-devnet:~$ cd wifi-automation
  devnet-adm@ubuntu-devnet:~$ ls -l
  total 52
  drwxrwxr-x 2 devnet-adm devnet-adm 4096 Jul 1 18:38 examples
  -rw-rw-r-- 1 devnet-adm devnet-adm 35149 Jul 1 18:38 LICENSE
  drwxrwxr-x 2 devnet-adm devnet-adm 4096 Jul 1 18:38 presentation
  -rw-rw-r-- 1 devnet-adm devnet-adm 63 Jul 1 18:38 README.md
  drwxrwxr-x 2 devnet-adm devnet-adm 4096 Jul 1 18:38 solutions
  devnet-adm@ubuntu-devnet:~$
Git will not be used for version control or backup in this lab, but it is highly recommended to use when building your own projects

## Slide 26: Pre-lab task #3: Install Docker on the Ubuntu Server
Installing Docker on Ubuntu Server
Docker is a platform for running containers (isolated/controlled environments)
As Docker containers we will run
  YANG-Suite to explore IOS-XE YANG models
  Telegraf, InfluxDB and Grafana to visualize Telemetry data from IOS-XE
We will use "docker-compose" for our container setups
  All settings for a container specified in a YAML file
To test the Docker installation, we will run
  hello-world, a very small container that outputs "Hello from Docker!" if Docker is correctly installed
  alpine, a very small footprint linux container
Pre-lab task #3: Docker

## Slide 27: Installing docker
  # Add Docker's official GPG key:
  sudo apt update
  sudo apt install ca-certificates curl gnupg
  sudo install -m 0755 -d /etc/apt/keyrings
  curl -fsSL https://download.docker.com/linux/ubuntu/gpg | sudo gpg --dearmor -o /etc/apt/keyrings/docker.gpg
  sudo chmod a+r /etc/apt/keyrings/docker.gpg
  # Add the repository to Apt sources:
  echo \
  "deb [arch="$(dpkg --print-architecture)" signed-by=/etc/apt/keyrings/docker.gpg] https://download.docker.com/linux/ubuntu \
  "$(. /etc/os-release && echo "$VERSION_CODENAME")" stable" | \
  sudo tee /etc/apt/sources.list.d/docker.list > /dev/null
  sudo apt update
  # Install Docker:
  sudo apt-get install docker-ce docker-ce-cli containerd.io docker-buildx-plugin docker-compose-plugin
  # Add current user to docker group, to be able to run containers without sudo
  sudo groupadd docker
  sudo usermod -aG docker $USER
  sudo reboot
Pre-lab task #3: Docker
Copy-paste should be OK from this slide, but it doesn't always like if you copy-paste the full content at once, so just do it in some separate chunks

## Slide 28: Docker first run
Pre-lab task #3: Docker
  devnet-adm@ubuntu-devnet:~$ docker run hello-world
Hello from Docker!
This message shows that your installation appears to be working correctly.
(... cut for brevity ...)
For more examples and ideas, visit:
https://docs.docker.com/get-started/
devnet-adm@ubuntu-devnet:~$
  devnet-adm@ubuntu-devnet:~$ docker pull alpine
  Using default tag: latest
  latest: Pulling from library/alpine
  ec99f8b99825: Pull complete
  Digest: sha256:b89d9c93e9ed3597455c90a0b88a8bbb5cb7188438f70953fede212a0c4394e0
  Status: Downloaded newer image for alpine:latest
  docker.io/library/alpine:latest
  devnet-adm@ubuntu-devnet:~$ docker run -it alpine
  / # cat /etc/os-release
  NAME="Alpine Linux"
  ID=alpine
  VERSION_ID=3.20.1
  PRETTY_NAME="Alpine Linux v3.20"
  HOME_URL="https://alpinelinux.org/"
  BUG_REPORT_URL="https://gitlab.alpinelinux.org/alpine/aports/-/issues"
  / # apk add nano
  (... cut for brevity ...)
  / # nano /tmp/test.txt
  / # exit
The hello-world container is a small container, that just helps you check if your Docker installation is working
Alpine is a very slim Linux distro. As an empty container, it requires about 8MB disk space. A lot of pre-built containers (like we will use later) are based on the alpine image.
We will first pull Alpine, then run it and connect to its terminal using the "-it" option
When connected to the Alpine container, we can do regular Linux stuff, and also install apps using apk. As an example we will install nano, edit a text file, and exit the container
Containers are deleted after exiting, unless permanent files are specified (we will use that later)

## Slide 29: Pre-lab task #4: Install Postman on your laptop
Download and follow the instructions on
  https://www.postman.com/downloads/
Pre-lab task #4: Postman

## Slide 30: Create a Postman account
Create a Postman account
After creating the account, I would always recommend to enable 2FA
Log in to the Postman app using your account
Pre-lab task #4: Postman

## Slide 31: Pre-lab task #5: Install VS Code on your laptop
Download from https://code.visualstudio.com/
Some recommended extensions
  Ansible
  Python
  Remote - SSH
  Codeium
A word of caution - beware of fake plugins/extensions
  https://www.bleepingcomputer.com/news/security/malicious-vscode-extensions-with-millions-of-installs-discovered/
Pre-lab task #5: VS Code

## Slide 32: VS Code
Extensions:
Python
Ansible
Remote - SSH
Source control (Git):
If you press here you are asked to log in etc. You don't have to do this to complete the lab, it will not be used.
Language (Python/Ansible/etc)
Pre-lab task #5: VS Code
Python environment
Some active extension
(Codeium, GitHub Copliot, etc)
Explorer (files etc)
Command palette

## Slide 33: Pre-lab task #6: 9800-CL (optional)
In this task we will install Cisco 9800-CL on VirtualBox
This task is marked as optional, but:
You may do some (most) of the C9800 tasks in the deep dive using a common WLC instead of having your own
This might be the case if you have a weak laptop, are using MacOS, or are primarily interested in the non-Cisco stuff from the lab
Pre-lab task #6: 9800-CL

## Slide 34: Pre-lab task #6: 9800-CL (optional)
Start by downloading the software
  https://software.cisco.com
  "Access downloads"
  Log in
  9800-CL version 17.15.1 is used in this lab. Download the ISO image
  Any recent version should work, but if we use the same version the APs don't have to download software if changing WLCs
  If you do not have access to Cisco Software, you can use the common 9800 wlc9 (see topology map)
  Example uses Ultra-low specs
    RAM: 6144MB
    Processors: 2
    HDD: 16GB
Pre-lab task #6: 9800-CL

## Slide 35: Create VM
Pre-lab task #6: 9800-CL
Change the name to reflect
your pod number. E.g.
wlc11
wlc12
wlc13
etc

## Slide 36: Create VM
Pre-lab task #6: 9800-CL

## Slide 37: Modify VM
Pre-lab task #6: 9800-CL

## Slide 38: Modify VM
Pre-lab task #6: 9800-CL

## Slide 39: Modify VM
Pre-lab task #6: 9800-CL

## Slide 40: Modify VM
Pre-lab task #6: 9800-CL
Important

## Slide 41: Modify VM
Pre-lab task #6: 9800-CL

## Slide 42: Modify VM
Pre-lab task #6: 9800-CL

## Slide 43: Run VM
Pre-lab task #6: 9800-CL
Take some minutes to boot...
It looks like this when first boots are completed and ready for config:

## Slide 44: Configure WLC
Pre-lab task #6: 9800-CL
Type "no" to enter initial configuration dialog
Enter your enable secret twice (from topology sheet or create your own)
Enter "0" to return to CLI without saving

## Slide 45
Pre-lab task #6: 9800-CL
Initial config
Copy the config script
Replace the text {pod-number} with your pod number
It should be 5 occurences
  Hostname: hostname wlc{pod-number}
  IP: ip address 192.168.10.{pod-number}
  SSID name: wlan lab-network 17 lab-network{pod-number}
  Mobility group: wireless mobility group name automationlab{pod-number}
  RF-group: wireless rf-network automationlab{pod-number}
The first section (40ish lines) must be manually entered, then connect using SSH
The second section can be copy-pasted after connecting to WLC with SSH
You should change the country code from NO to your country, or to CZ for local compliance
The last line should be pasted alone after the rest is finished
!!! Enter this manually to get SSH up and running !!!
enable
conf t
hostname wlc{pod-number}
ip domain name automationlab.local
crypto key generate rsa
4096
!
vlan 10
name management
!
interface Vlan 1
shutdown
!
interface vlan 10
description management
ip address 192.168.10.{pod-number} 255.255.255.0
no shutdown
!
interface GigabitEthernet1
shutdown
description Uplink
switchport trunk allowed vlan 10,11
switchport mode trunk
switchport trunk native vlan 10
no shutdown
!
ip default-gateway 192.168.10.1
ip route 0.0.0.0 0.0.0.0 192.168.10.1
aaa new-model
username devnet-adm privilege 15 algorithm-type sha256 secret ChangeMe2024!
enable algorithm-type sha256 secret ChangeMe2024!
aaa authentication login default local
aaa authentication enable default enable
line vty 0 30
privilege level 15
logging synchronous
transport input ssh
!
!!! Log in with SSH, then you can copy-paste the rest !!!
conf t
!
interface GigabitEthernet2
description Out-of-Band
shutdown
!
interface GigabitEthernet3
description HA-sync
shutdown
!
vlan 11
name lab-network
!
do terminal length 40
ip dhcp bootp ignore
no service pad
no pae
service tcp-keepalives-in
service tcp-keepalives-out
ntp server 40.119.148.38
service timestamps debug datetime msec localtime
service timestamps log datetime msec localtime
service password-encryption
aaa session-id common
aaa authorization exec default local
clock timezone CET 1 0
clock summer-time CEST recurring last Sun Mar 2:00 last Sun Oct 3:00
ip http server
ip http authentication local
ip http secure-server
no logging console
no logging monitor
logging buffered 40960
configuration mode exclusive auto
errdisable recovery cause all
errdisable recovery interval 600
ip name-server 1.1.1.1 8.8.8.8
ip ssh time-out 15
!
line con 0
exec-timeout 5 0
logging synchronous
stopbits 1
line vty 0 30
exec-timeout 60 0
privilege level 15
logging synchronous
transport input ssh
!
wireless mobility group name automationlab{pod-number}
wireless mobility dscp 0
!
wireless rf-network automationlab{pod-number}
wireless client max-user-login 3
ap dot11 5ghz shutdown
ap dot11 2 shutdown
wireless country NO
no ap dot11 2 shutdown
no ap dot11 5 shutdown
!
wireless management interface vlan10
!
wireless profile flex lab-flex-profile
native-vlan-id 10
vlan-name 10
vlan-id 10
vlan-name 11
vlan-id 11
!
ap profile lab-ap-profile
mgmtuser username devnet-adm password 0 ChangeMe2024! secret 0 ChangeMe2024!
ssh
!
wireless tag site lab-site-tag
no local-site
flex-profile lab-flex-profile
ap-profile lab-ap-profile
!
wlan lab-network 17 lab-network{pod-number}
radio policy dot11 5ghz
security ft over-the-ds
wmm require
security wpa psk set-key ascii 0 ChangeMe2024!
no security wpa akm dot1x
security wpa akm psk
no shutdown
!
wireless profile policy lab-policy
no central authentication
no central dhcp
no central switching
dhcp-tlv-caching
http-tlv-caching
vlan 11
no shutdown
!
wireless tag policy lab-policy-tag
wlan lab-network policy lab-policy
!
ap filter name lab-filter-rule
ap name-regex .
tag policy lab-policy-tag
tag rf default-rf-tag
tag site lab-site-tag
ap filter priority 100 filter-name lab-filter-rule
!
password encryption aes
key config-key password-encrypt
PasswordForDecryptForAutomationLab!
PasswordForDecryptForAutomationLab!
!
!
exit
!
!
! The last line should be pasted alone, after the rest is finished
!
wireless config vwlc-ssc key-size 2048 signature-algo sha256 password 0 CertPasswordAutomationLab
Copy this to Notepad++
Replace {pod-number} with number
Then paste in conf mode on 9800:

## Slide 46: Prepare WLC for API connections
Enable NETCONF, RESTCONF, and create the users
Enable Role-Based Access Control and create some RO users
Note about the last command
  Some times it will take a couple of minutes before the command is "ready to run". Try later if you get an error
  username restconf-adm privilege 15 secret restconf-pass
  username netconf-adm privilege 15 secret netconf-pass
  netconf-yang
  restconf
  ip http secure-server
  aaa authorization exec default local
Pre-lab task #6: 9800-CL
  username restconf-read privilege 1 secret restconf-read
  username netconf-read privilege 1 secret netconf-read
  exit
  request platform software yang-management nacm populate-read-rules privilege 1

## Slide 47: Pre-lab task summary
You should now be ready for the deep dive labs, by having installed
  VirtualBox
    Virtual Mahine 1: 9800-CL
    Virtual Machine 2: Ubuntu Server w/Docker
  Postman
  VS Code w/some extensions
Pre-lab task summary